## Slide 1: Way Forward for MUSIM
S1-192589
(wasS1-192588)
Ellen Liao, Intel

## Slide 2: The User preference of MUSIM UE
[CPR.8.1-2]: A MUSIM UE should allow the user to configure the user’s preference for the same or different services among multiple USIMs provided by the same or different MNOs.
Can we agree that user preferences are configured by the user?
  Decision: TBD
Can we agree that this requirement is needed?
  Decision: TBD
Need Description in TS22.101?
  Yes, but the text needs to be rephrased
Can we agree that the configured user preference is used by the MUSIM UE to handle the MT service?
  Decision: YES. The can be the working assumption
Notes: Draft-description
Votes: requirement:6; NO: 9
MMI (NO)
OPPO: UE implementation; OS, modems, no test case.
==
Decision:
Convida-Cate: requirement is better
Xiao mi:
Jack
EriK: if non-human device
===

## Slide 3: Service requirement 8.2-1
[CPR.8.2-1]:
The 3GPP system shall be able to indicate to the UE as part of the paging procedure the type of traffic that triggered the paging.
This information may be used by a user or MUSIM UE to determine whether it needs to respond to a mobile terminated call on one registered USIM while the UE is engaged in active communication on another USIM.
The granularity of the paging information shall discriminate between the following service categories;
IMS and non-IMS based Voice service.
IMS and non-IMS based SMS or USSD
IMS service other than voice or SMS
Other service not listed above e.g. data services including video.
Rephrase the service requirement:
  Assumption: a MUSIM UE, each associated USIM can be in idle mode or connected mode.

## Slide 4: Service requirement 8.2-1
    What are the assistant info?
      Associated USIM is in Idle mode:
        paging with information of service categories to the idle mode UE
        Service categories:
        Assumption:
          Traffic type of the MT service can be identified by the network
          information is generic service categories
      Associated USIM is in Connected mode:
        Caller party ID (only for voice/multimedia telephony service)
    Can we agree that these assistant information are helpful to the MUSIM UE for handling the MT services: [TBD]
    Can we live with the following sentence? [TBD]
    This information may be used by a user or MUSIM UE to determine whether it needs to respond to a mobile terminated service on one registered USIM [in idle mode or connected mode] while the UE is engaged in active communication on another USIM.

## Slide 5: Service requirement 8.2-1 about SR-1
The 3GPP system shall be able to indicate to the UE upon presentation of an MT service with information about the type of traffic corresponding to that MT services well as call party id (for voice/multimedia telephony services only). This information may be used by a user or MUSIM UE to determine whether it needs to respond to a mobile terminated service on one registered USIM [in idle mode or connected mode] while the UE is engaged in active communication on another USIM.
  Decision: TBD

## Slide 6: Service requirement 8.2-1 about Assistant information
For associated USIM in Idle mode:
Service Categories Granularities of the paging information:
IMS and non-IMS based Voice/SMS or USSD
IMS service other than voice or SMS
Priority Service with User/Operator’s perspective
Editor’s Note or TBD
For associated USIM in Connected mode:
Caller party ID (only for voice/multimedia telephony call)
Editor’s Note or TBD

## Slide 7: Other SRs
Suspend/Resume
[Decision: TBD]
  [CPR.8.2-2]: The 3GPP system shall be able to suspend an active communication, e.g. when the UE needs to perform activity associated with another USIM.
  [CPR.8.2-3]: The 3GPP system shall be able to resume a suspended communication, e.g. when the UE has completed activity associated with another USIM.
Paging collision issues
[Decision: TBD]
  [CPR.8.2-4]: The 3GPP system shall be able to minimize paging collision for paging related to multiple USIMs in the UE.
Notes: 2589
==
Completeion: