## Slide 1: 5G enabling naked eye holography service
China Mobile

## Slide 2: Defination: Naked eye holography service
Naked eye holography service
  Defination: Presenting real objects’ 3D images on devices using holography technology, without wearing head-mounted display(HMD) equipments, e.g. glassess.
  Difference with AR/VR
    without any HMD equipment, e.g. glassess,;
    presenting different contents from different angles; as for AR/VR, we can view the same virtual content from any angle;
    using different technical principle: holography is used to ontain real object’s features and present 3D contents based on these features; AR/VR is used to present virtual contents which are produced by computing technology.
Scope of this study:
  Service and performance requirements for 5GS, not include specific media handling (e.g. codecs).

## Slide 3: Motivation & Opportunity——Naked eye holography service
2D holography is mostly based on multiple video streams, without special display technology and data format.
With the high rate of advances in network, high-resolution rending, object capture/display technology and solution of the "medium" problem...Devices will be able to display 3D hologram directly, without wearing HMD equipments to view contents.
Holography is next generation technology to bring new visual experience and interactive method, and it’s keeping evolving.
Holography service can be broadly applyed in different domains, e.g. medical treatments, communication, education, industry...
Holography technology | 2D holography |  |  | 3D holography |  |  | ideal holography
 | ASKA3D | Projection film | stereoscopic grating | Point Cloud | Light field |  | digital holography
 |  |  |  |  | Camera array | Plenoptic camera | 
Recommended bandwidth Primary experience | 29.2-65.6 Mbps | 10.0-22.5 Mbps | 12.8-28.9 Mbps | 105.6-237.6 Mbps | 255.74-575.4 Mbps | 47.7-105 Mbps | 379.56-854.02 Gbps
Recommended bandwidth Good experience | 238.0-535.5 Mbps | 79.3-178.5 Mbps | 106.2-238.9 Mbps | 3.4-7.65 Gbps | 15.87-35.7 Gbps | 1.4-3.15 Gbps | 17.20-38.69 Tbps
Development stage of holographic technology

## Slide 4: Current Situation of Industrial Development
The holograpic industrial chain structure has been completed and promotes rapid development of vertical market.
The results of industrial investigation shows that the holography technology is close to maturity.
2015-2019 Global market size of holographic industry
market size(100 million Yuan)
growth rate(%)
*Source: Global Holographic Display Market- Industry Analysis and forecast 2027: By Technology, Product Type, Application, and Region
*Source: Global Holographic Imaging Market: Industry Analysis and Forecast (2020-2026)
Global Holographic Display Market-2027, byRegion

## Slide 5: WID Objectives:
Study use cases related to naked eye holography service and identify potential service and performance requirements for 5G system. Aspects to be studied include:
  Identify holography information characteristics( including data/traffic model) and service requirements for transferring holography information.
  Identify KPIs regarding naked eye holography service, including hologram resolution, viewing angle, latency, reliability, data rate, etc.
  Other aspects, e.g. charging, security...
  Note: Studying specific media handling (e.g. codec) is out of the scope of this SID.

## Slide 6
Thank you!

## Slide 7: Use case 1: Holographic interactive desk
② Action collection device
① Holographic imaging equipment
③ Desk structure
The user action data is collected to realize the interaction between the user and the hologram
display objects’ 3D hologram
normal working desk surpporting holographic imaging equipment
Leap motion
Kinect
Looking glass
Holographic pyramids
projector+Holographic film
Holographic display for interaction areas
user
normal desk

## Slide 8: Use case 1: Holographic interactive desk
View biological cells
It can observe biological cells closely to analyze the biological structure and mechanism inside cells.

## Slide 9: Use case 2: Model display
Transmission media
Transmission content
Human
single
double
virtual
Picture
Video
Model
Hologram
Object
virtuality
Environment
real
virtual
Interactive mode
gesture
audio
tactile
static
dynamic
Remote diagnosis
Digital content import
Holographic heritage restoration
Holographic model cloud storage
Scenarios
Holographic display
Traditional display

## Slide 10: Use case 3: Human interaction
Typical scenario
Model holography · Remote classmate hologram
synchronous operation · smooth communication
Scenario feature
User Experience Indicators
Holographic display
Traditional display
Holographic scenario
Traditional scenario
Experience Indicators Comparison
High
audio,vidio, tactile
<10ms
16k
90°~180°
2×10^15 ops
audio,video
200ms
4k
0°
real-time collectionand transmission
latency
immersive presentation
resolution
Viewing angle
intraction
network stability
syncronization