## Slide 1: Discussion on UE-Network Coordinated AI/ML service OPPO
3GPP SA WG1 #97-e
Electronic Meeting, 14 – 24 Feb. 2022
S1-220038r2

## Slide 2: Background
R18 SA1 study on AMMT identify the requirements for AI/ML model transfer on 5GS regards 5GS as a channel to transfer data about AI/ML, e.g. very high data rate is required for model distribution and device-NW split inference/Federated Learning.
Scenarios and aspects, missing or not fully covered in Rel-18, have been identified and suggested to be further investigated in Rel-19, i.e.:
  AI/ML model transfer for device-NW coordinated AI/ML operation, e.g., NW-assisted information for predicting model transfer in 5G hotspot coverage, or device route planning
  AI/ML model transfer over 5G direct device connection, e.g., for distributed learning/inference.
Proposed study areas in Rel-19:
  Device-NW coordinated AI/ML operation
  AI/ML model transfer over 5G direct device connection, e.g., for distributed learning/inference.

## Slide 3
Device-side AI operation is needed in many scenarios. High data rate connection becomes precondition (e.g. for AI model downloading, AI training with NW) for 5G devices to finish some AI/ML task, as shown in Rel-18 FS_AMMT KPI.
Ultra-high data rate (via high-order MIMO/mmWave) is a valuable resource for 5G operators and UEs, but has not fully utilized because it may be available only in certain hotspots or LOS beam areas.
Considering, for example, smart-transportation use cases, mobile AI devices (Robots, Drones, Smart) need to plan the route not only based on the location of destination and transportation map, but also considering the 5G link quality.
UE could intelligently predict (or move toward) the hotspot/LOS area to access the high data rate for AI services (AI/ML model downloading, Split inference/training), using e,g, AI-based route planning based on the predicted achievable data rate throughout the unvisited area.
“To Go or Not to Go: On Energy-Aware and Communication-Aware Robotic Operation”, IEEE TRANSACTIONS ON CONTROL OF NETWORK SYSTEMS, VOL. 1, NO. 3, SEPTEMBER 2014
Device-NW coordinated AI/ML operation, e.g., NW-assisted information for UE to predict model transfer in 5G hotspot coverage, or device route planning

## Slide 4: Device-NW coordinated AI/ML operation, e.g., NW-assisted information for UE to predict model transfer in 5G hotspot coverage, or device route planning
Some NW-assisted information exposure could be beneficial for the device (or 3rd party transportation company) - not requiring to disclose sensitive information about the network or devices. For example, the NW and device can perform split AI route planning, and exchange only intermediate AI/ML inference data.
The gap is analyzed below:
Potential functions enabled by SA2 R18 SID on “5G System Support for AI/ML-based Services” | Requirements of device route planning for 5G hotspot access
NW predicts a UE’s QoS consistency along a route reported by the UE (assuming UE has planned the route). | Mobile UEs needs to predict the hotspot locations /beam directions throughout the unvisited area (UE cannot plan the route without the apriori information).
NW predicts a UE’s QoS consistency without considering the real wireless channel conditions (assuming UE has planned the route). | Mobile UEs needs to predict the achievable data rate based on channel conditions, e.g. channel fading, blockage.

## Slide 5: Distributed AI training/inference involving direct device connection
5G direct device connection can be used to perform distributed learning/inference among devices, achieving the goal of using local data with privacy protection, energy saving, training efficiency. etc. Potential scenarios are, for example:
  For Distributed Learning, controlled by network, each device uses the localized data while transfer the intermediate data to other nodes in order to train a big model.
  For Distributed Inference, the device, holding valuable input data but with low power/computation resource, may calculate the first few layers of a AI model and offload the intermedia data to another device using D2D link for the final inference result.
  For Federated Learning, Using D2D can involve devices outside 5G hotspot for distributed AI training/inference, partly offload computation to neighboring device, so as to improve the training accuracy/generalization and save device power.
Legacy 5G SL cannot well support Distributed AI training/inference.
New 5GS KPIs and functional requirements should be investigated, for example, different QoS requirement on Uu and slidelink in relay scenario, and taking application, model storage, user consent into consideration for D2D discovery.

## Slide 6: Back slide

## Slide 7: Distributed AI training/inference with D2D enhancement - Example use cases
UC-1: Hybrid splitting architecture based on model parallelism with the participation of UEs and networks
UC-2: Factory service flow (Intermediate data can be changed between two robots and the robot with low battery can continue working)
UC-1: By using the model parallelism, the transmission of intermediate training results between different nodes can realize data sharing between UEs under the premise of ensuring privacy, expand the training set of the model, and improve the training efficiency.
UC-2: When the battery level reaches a certain value, a part of the AI/ML model can be transferred to another robot by splitting the AI/ML model