## Slide 1: ProSe status SA2-SA3 JM
SA2#101, Taipei
Qualcomm Inc. (Rapporteur)
S2-140442

## Slide 2: SA2 ProSe status
SA2 is working on the ProSe components that are prioritised by SA and described in SP-130506. Namely:
  ProSe Communication which includes:
    ProSe Communication 1-many “in network”
    ProSe Communication 1-many “out of network”
    ProSe UE-Network Relay
  ProSe E-UTRA direct discovery which includes
    Dynamic configuration/Authorisation for discovery
    Open discovery
    Restricted discovery
  EPC-level discovery
  ProSe assisted WLAN direct
  Identifiers used for discovery
  System aspects (network sharing, roaming etc)
SA2 has agreed in a set of conclusions and endorsed solutions already for certain components
SA2 plans to close the TR 23.703 at SA2#101 with endorsed solutions
SA2 plans to complete TS 23.303 at SA2#101bis (17-21 Feb 2014) and send for approval at SA2#63

## Slide 3: Conclusions in TR 23.703 v1.0.0
Direct discovery (these points copied from TR 23.703 clause 8.5)
  PC3 interface is used for ProSe configuration and the functional entity that provisions the UE with some necessary parameters is a new EPC node named Direct Provisioning Function (DPF);
    The mechanism for UE authorisation from PLMNs that are involved in the discovery procedure is FFS
    The mechanism for authorisation for applications using ProSe direct discovery is FFS
  Necessary subscription parameters in HSS will be defined for ProSe direct discovery as will be determined by the related procedures;
  For operator controlled open discovery the allocation and processing mechanisms via PC3 for ProSe Application Identities is based in principle on solution D13 in TR 23.703;
    It is FFS if allocation and processing mechanisms for Prose Application Identities over PC3 use 3GPP control plane or user plane
  The format of ProSe Application Identities for open discovery may have a structure so as to allow partial matching at the UE side reflecting application-specified interests, and thus reduce the number of processing of discovered ProSe Application Identities;
  The values of ProSe Application Identities as defined in solution D13 in TR 23.703 for open discovery is not expected to be specified in 3GPP, but another organization is expected to specify that on behalf of operators' community (e.g. GSM Association);
  ProSe Application Identities for open discovery shall have a standards defined format in 3GPP to allow the 3GPP function to process them. The exact format is FFS;
  Both discovery models "I am here" (model A) and "who is there"/"are you there" (model B) as described in clause 4.1.4 of TR 23.703 are relevant.

## Slide 4: Conclusions in TR 23.703 v1.0.0 (cont.)
EPC-level discovery (these points copied from TR 23.703 clause 8.3)
  It has been agreed that in Rel-12 EPC-level ProSe Discovery shall be supported using solution D4 in TR 23.703 as a basis, with the following assumptions:
    The PC3 reference point is established in the user plane of EPS
    Proximity tracking relies on user plane LCS (SUPL) in Rel-12
    The roaming architecture is not specified in Rel-12
  In order to fully exploit synergies with the IMS there is an IMS variant of the Device Registration and Device Deregistration procedures, in addition to their non-IMS variant.
    It is FFS whether the UE registration procedure via IMS and UE deregistration via IMS, i.e. if the use of IMS as part of EPC level discovery, is needed in Rel-12
  In order to allow for early Proximity Request cancellation without bringing the targeted UE in connected mode it has been agreed to support the targeted UE’s initial location check via the HSS as an option.
Endorsed solution described in Annex H

## Slide 5: Conclusions in TR 23.703 v1.0.0 (cont.)
ProSe assisted WLAN direct (these points copied from TR 23.703 clause 8.4)
  It has been agreed that in Rel-12 EPC support for WLAN direct communications shall be supported both
    As an incremental part of EPC-level discovery using solution W1 in TR 23.703 as a basis, and
    As a stand-alone procedure using solution W3 in TR 23.703 as a basis
  Endorsed solution described in:
    As an incremental part of EPC-level discovery: Annex H
    Standalone procedure: Annex I

## Slide 6: Conclusions in TR 23.703 v1.0.0 (cont.)
ProSe communication 1-many (these points copied from TR 23.703 clause 8.2)
  No need for dynamic ProSe group management prior to transmission (i.e. no notion of "ProSe group joining");
  Distributed architecture: all UEs being equal in data traffic transmission, there is no single point of failure;
  When sending traffic to a group of receivers, the sender uses a multicast address in the Destination Layer-2 ID field of the layer-2 data frame;
  There is no QoS support apart from priority handling;
  UEs are configured with a set of information that would allow one-to-many communication to work;
  UEs are provided with information regarding radio resources to be used for out of network operation;
  A mechanism for providing the aforementioned information to UEs needs to be standardised in Rel-12;
  Network independent procedures for one-to-many communication are to be standardised in Rel-12;
  The "network layer" stack for one-to-many communication in decentralized mode is based on IP;

## Slide 7: Conclusions in TR 23.703 v1.0.0 (cont.)
ProSe UE-to-Network Relays (these points copied from TR 23.703 clause 8.6)
  It has been agreed that in Rel-12 the study on UE-to-Network Relay will focus on the following type of solutions:
    Application Layer Gateway (ALG) type of relay (e.g. solutions R6, R7, R8 in TR 23.703);
    L3-based relay (e.g. solutions R3, R11 in TR 23.703);
    It is FFS whether both relay types will be specified in Rel-12.
  It has been agreed that the following applies for the UE-to-Network Relay:
    At EPS level (excluding the ProSe Function) the network perceives only one entity – the UE-to-Network Relay;
    Relay selection on PC5 takes into account information that is announced by, or solicited from, the UE-to-Network relay and that reflects a meaning such as “I can act as a relay for public safety”. It is FFS which other criteria are used for relay selection.

## Slide 8: (Additional) working assumptions in SA2#101 (tbc by end of the meeting)
Overall architecture
  PC3 reference point is established in the user plane of EPS
Direct discovery
  Focus on open discovery for commercial use (in coverage)
  Restricted discovery for public safety use (in/out of coverage)
EPC-level discovery
  No IMS variant will be defined
Disclaimer: Depends on documents under revision

## Slide 9: SA2 questions to SA3
What security requirements apply between a remote UE and ProSe UE-Network Relay on PC5 control signalling?
What are the privacy requirements for Prose UE IDs or user ids transmitted for ProSe discovery that will affect our work?