## Slide 1: Discussion on when and how to get UE Usage Type at DCN
Oct. 8, 2015
NTT DOCOMO
S2-153373
TSG SA WG2 #111
Chengdu, P. R. China, 19-23 October 2015

## Slide 2: When should dedicated MME/SGSN get UE Usage Type?
For TAU/RAU w/ S-GW change procedure, a dedicated MME/SGSN should know the UE Usage Type before establishing new bearers.
  When establishing bearers, a dedicated MME/SGSN needs to know the UE Usage Type value since it should set its value for the DNS query to retrieve appropriate S-GWs for this UE Usage Type.
  It would be OK for a dedicated MME/SGSN to select an appropriate S-GW from MMEGI/Null-NRI or SGSN Group ID in the redirected TAU/RAU message from RAN in case this dedicated CN accommodates only one UE Usage Type. However, if several UE Usage Types are mapped into one dedicated CN, this will not work since DNS query is based on using UE Usage Type.
We need a solution of how the dedicated MME/SGSN get the UE Usage Type if the old MME/SGSN doesn’t support DECOR.
  If the old MME/SGSN doesn’t support the DECOR feature, the dedicated MME/SGSN cannot get the UE Usage Type by the Context Response message.

## Slide 3: How can dedicated MME/SGSN get UE Usage Type?
Our preference is Alt.1
Alternative | Pros | Cons
1. Redirected messages should include UE Usage Type. | No need to perform ULR/ULA to retrieve UE Usage Type. | Impact on RAN3 specification for S1AP/RANAP. SA2 needs to slightly modify TS 23.401.
2. Dedicated MME should perform ULR/ULA after Identification/Context Req/Resp procedures. | No RAN impact. No need to modify TS 23.401. | Signaling for HSS would increase than we expected.

## Slide 4: Alt.1: Redirected messages should include UE Usage Type.
UE
eNB
Old MME/SGSN
new MME
Dedicated MME
HSS
TAU Request
TAU Request
Context Request
Context Response (no UE Usage Type)
Reroute NAS Message Request (original TAU message, MMEGI for Dedicated CN, UE Usage Type, Additional GUTI)
Initial UE message (original TAU message, MMEGI for Dedicated CN, UE Usage Type)
Update Location Request
Update Location Answer (UE Usage Type)
Context Request
Context Response (no UE Usage Type)
Update Location Request
Update Location Answer (UE Usage Type)
Context Acknowledge (NACK)
Update Location Request
Cancel Location Request
Cancel Location Acknowledge
Update Location Answer
bearer estb.
TAU Accept
Authentication / Security
Context Acknowledge
bearer deletion
For TAU/RAU procedure, the new MME/SGSN should include UE Usage Type in Reroute NAS Message Request and RAN node should also forward this UE Usage Type to a dedicated MME/SGSN so that it can select an appropriate S-GW for the UE Usage Type.
(This can also be applied to Attach procedure.)
Old MME does not support Decor and hence cannot provide UE Usage Type

## Slide 5: Alt.2: Dedicated MME should perform ULR/ULA after Context Req/Resp procedure.
UE
eNB
Old MME/SGSN
new MME
Dedicated MME
HSS
TAU Request
TAU Request
Context Request
Context Response (no UE Usage Type)
Reroute NAS Message Request (original TAU message, MMEGI for Dedicated CN, Additional GUTI)
Initial UE message (original TAU message, MMEGI for Dedicated CN)
Update Location Request
Update Location Answer (UE Usage Type)
Context Request
Context Response (no UE Usage Type)
Update Location Request
Update Location Answer (UE Usage Type)
Context Acknowledge (NACK)
Update Location Request
Cancel Location Request
Cancel Location Acknowledge
Update Location Answer
bearer estb.
TAU Accept
Authentication / Security
Context Acknowledge
bearer deletion
For TAU/RAU procedure, a dedicated MME/SGSN should perform this procedure in order to select an appropriate S-GW for the UE Usage Type.
(Attach procedure also needs to take the same steps.)
Old MME does not support Decor and hence cannot provide UE Usage Type