## Slide 1: Source: Qualcomm Incorporated Title: RRC_INACTIVE System architecture aspects Agenda Item: 6.5.12 Work Item / Release: 5GS_ph1/Rel-15
SA WG2 Meeting #S2-120 S2-172655
27 - 31 March 2017, Busan, South Korea (was S2-171802)

## Slide 2: System Aspects
Key questions:
  What is NAS Connection Management (CM) state?
    1) What is N2/N3 status?
    2) What is Mobility Model?
    3) Does CN / NAS need to be aware of RRC_INACTIVE state?
    4) Do we need Core Network paging in RRC_INACTIVE?
  Other aspects:
    5) Core network assistance to RAN for RRC_INACTIVE?
    6) How is RRC_INACTIVE enabled/disabled?
    7) Mismatch of states at CN and UE
    Not handled in this revision:
    8) PLMN selection in RRC_INACTIVE
    9) Inter-RAT mobility between NR and eLTE. Relation to Light Connection?
    10) Inter-RAT mobility in all other cases to GERAN/UTRAN.
    11) UE location accuracy
    12) Access control for RRC_INACTIVE.

## Slide 3: General
  SA2 assumes that from architecture standpoint RRC_INACTIVE applies to NG-RAN (i.e. it applies also to E-UTRA connected to 5G CN )
    LS to RAN2 is needed to start alignment on this point
  This document use NR terminology with the above understanding

## Slide 4: 1) N2/N3 status while in RRC_INACTIVE
  N2 and N3 must be active and terminating @ anchor gNB. Same as for CM-CONNECTED
  UE is in CM-CONNECTED
  CN considers the UE as CM-CONNECTED when in RRC_INACTIVE state in RAN

## Slide 5: 2) Mobility Model
From Core Network perspective:
  Any trigger for UE context transfer from anchor gNB (original N2/N3 termination) to a new serving gNB (new N2/N3 termination), looks like a transfer of N2/N3 termination point.
    Procedure will be based on handover procedure.
  UE context transfer from one gNB to another for RRC_INACTIVE should reuse the same procedures towards the Core Network as for RRC_CONNECTED.

## Slide 6: 3) Does CN / NAS need to be aware of RRC_INACTIVE state?
In some cases (still FFS) CN needs to be know when the UE transitions in/out of RRC_INACTIVE
  This will be discussed in case by case basis

## Slide 7: 4) Do we need special Core Network paging procedure in RRC_INACTIVE?
No input paper indicated that it is needed (as of now)
This decision may be challenged due to discussion in SA WG2 and RAN WGs
Note: The term “special” means a procedure other than the CN paging procedure used while the UE is CM-IDLE.

## Slide 8: 5) Core network assistance to RAN for RRC_INACTIVE?
RAN needs to receive at least the following information from the AMF before transitioning a UE from RRC_CONNECTED to RRC_INACTIVE:
  The registration area (TAI list) provided to the UE
    In order to ensure that all the cells in the RAN Paging Area are able to be connected to the current UPFs (c.f. EPC Serving GW) of the UE, the AMF needs to provide the TAI list of the UE to the RAN
  A maximum allowed DRX value
  Possibly:
    Some prioritization information (this needs further study, might be useful if there’s RAN paging prioritization in 5G CN)
Other information is FFS
Whether all info mentioned above is mandatory to be always included in FFS
The CN assistance information is provided during N2 activation with the (new) anchor gNB(attach, TAU, service request, handover).
The mechanism to update the CN assistance info to RAN while the UE is CM_CONNECTED e.g. to update the TAI-list is FFS

## Slide 9: 6) Should CN have control to enable/disable RRC_INACTIVE?
CN provides assistance information to RAN (see previous slide)
FFS whether this information is per UE or is always provided if “CN supports procedures for RRC_INACTIVE”

## Slide 10: 7) Mismatch of states at CN and UE
UE in CM-IDLE and AMF in CM-CONNECTED/RRC_INACTIVE
  When UE transitions to CM-IDLE, it immediately start NAS recovery
    Exact mechanism for NAS recovery in “5G NAS” will depend on CT1
    CT 1 need to ensure that this cannot occur (e.g. by replicating the EMM abnormal case behaviour from 24.301 into their equivalent 5G spec)
UE in CM-CONNECTED/RRC_INACTIVE and AMF in CM-IDLE
  UE monitors both RAN and CN paging. If UE receives CN paging it moves to CM-IDLE and performs NAS recovery
  Whether the UE can also respond to CN paging with “Resume” in certain cases is FFS