## Slide 1: Discussion on SMSF supporting domain selecion
China Mobile

## Slide 2: Requirement of SMSF supporting domain selection
Before SMSF is introduced, there are two entities which can perform MT domain selection for SMS: SMS-GMSC and IP-SM-GW
Requirement for SMSF to support MT domain selection
  Many operators do not deploy domain selection on SMS-GMSC at the beginning of SMS system deployment. Operators may have concern on upgrading legacy SMS-GMSC to support it due to supporting SMSoNAS, especially operators with huge SMS subscriber. Moreover, current MAP protocol only support domain selection for up to 3 entities
  Domain selection on IP-SM-GW is deployed only for IMS subscribers. But the solution mandates the operators to deploy IP-SM-GW even they do not provide SMSoIP. Another issue is that IP-SM-GW will have to proxy all SMS not for IMS users, which may be a big capacity considering of SMS for IoT terminals. There will be a big redundance of SMS delivery capacity between IP-SM-GW and SMSF.
  As a newly introduced functionality, SMSF is a good place to cover domain selection requirements of 5G SMS, independent with whether SMSoIP is deployed or not.
  In summary SMSF supporting MT domain selection is necessary for the scenario that operators have no IP-SM-GW or want a standalone deployment of SMS domain for non-SMSoIP users

## Slide 3: Current solution in 3GPP specs
When SMSF receives a MT message, it first tries to deliver the message via SMSoNAS
If the delivery fails, SMSF determine the next domain for re-attempting the delivery
  The determination is implementation specific
  The next domain can be another SMSF belonging to a different RAT, IP-SM-GW or SGs MSC, etc.
When the UE is roaming and supports SMS on both of 3GPP and non-3GPP accesses, 2 SMSF may be selected in different VPLMNs

## Slide 4: Remaining issues for SMSF domain selection
The message forwarding interfaces between SMSF and other entities need further clarification
How to handle interworking between PLMNs when roaming
It is possible that 2 SMSFs are selected in different vPLMNs as specified in previous slide
The interface in blue in the figure between different PLMNs for SMS forwarding may not be available
Domain selection is expected as a HPLMN functionality, but SMSF is currently in VPLMN when roaming

## Slide 5: Solution optimization proposal
To solve these remaining issues, it is proposed to optimize the current SMSoNAS solution as below
hSMSF is introduced to do MT domain selection and delivery re-attempt
vSMSF does not re-attempt MT messages in another domain, by which message forwarding interfaces between vPLMNs are avoided
SMSF related interfaces are clarified
  New SBI between hSMSF and vSMSF is introduced
SMSF and IP-SM-GW can be collocated or integrated for architecture simplification

## Slide 6: SMSF selection during registration
AMF selects vSMSF and initiates activation procedure including hSMSF address towards vSMSF
vSMSF initiate activation procedure similar to AMF towards hSMSF, including the access type of RAT connecting to this vSMSF
hSMSF stores different contexts of vSMSFs with the access types and register its address in UDM

## Slide 7: MO procedure
MO procedure is the same with current specified procedure

## Slide 8: MT procedure
UDM selects hSMSF to deliver the message
When hSMSF receives MT SMS message, it selects a vSMSF based on previously stored vSMSF contexts
A new service operation of SMSF is defined to transport MT SMS message from hSMSF to vSMSF

## Slide 9: Re-attempt after delivery fails
UDM returns the address of first entity based on operator’s policy
If the message delivery via selected vSMSF fails, hSMSF can select other available entity, e,g, another vSMSF to re-attempt via SMSoNAS
If all vSMSF fails to deliver the message, hSMSF selects another entity to re-attempt in other ways, e.g. via UDM
If all domains fails, hSMSF reports delivery failure to SMSC
The domain selection logic is implementation specific

## Slide 10: Thank you!