## Slide 1: Discussion about network resource scheduling for operating slices China Mobile, Alibaba, Tencent, China Unicom, Huawei, HiSilicon, ZTE

## Slide 2: What Slice Customers care about in slice SLA
Candidate attributes slice customers care about in slice SLA
  Most related on the slice UE or flow level
    Service experience for each slice UE
    QoS for slice UE and flow, e.g., latency, bitrate
    etc.
  Slice level attributes
    Coverage
    Capacity
    etc.
Better Qos profile for slice UE can be solved by Key Issue 5: NWDAF-Assisted QoS Profile Provisioning in eNA TR23.791
  Derive the qos profile based on the service experience

## Slide 3: Issues when deploying and operating many slices
Backgrounds
  Popular deployment:
    shared RAN: using RAN resource scheduling to guarantee the SLA of slice, e.g., TTI, not mandatorily assign part of frequency to any slice
    shared transport network: leveraging Flex-E interface and tunneling to reduce the latency and improve the isolation and reliability
    dedicated CN with dedicated or shared DC resource: deploying UPF into edge side to reduce the latency
  Network resource and capability is limited, which is hard to meet unlimited requirement of unlimited slice customers
UPF
Shared RAN
AMF
SMF
UDM
Slice A
Slice B
Slice C
Shared TN
Dedicated CN
Dedicated CN
Shared TN
AMF
AMF
UPF
UPF
PCF
SMF
SMF
PCF
PCF
Use proper configuration of AN, TN and CN to meet the slice SLA. Some configuration is common to many slices, while some configuration is specific to a slice
Question or Issue
  how to figure out the proper common configuration to meet the SLAs of many slices at the same time

## Slide 4: Some new attributes captures network capability/capacity and slice customer requirement
More slice level attributes or KPIs are raised(part of them discussed in GSMA NEST Group)
  How many percent of UEs’ service experience(slice UE/flow QoS) satisfied
    There is risk to guarantee the QoS of UE and flow at any time and under any conditions
  Slice priority
    It can be used to assist the network resource scheduling under limited network resource environment
  Uplink/downlink bandwidth/bitrates Per slice per RAN node(gNb)
    It can capture the slice customer requirement more exactly under limited network resource environment
  etc.

## Slide 5: Candidate solution leveraging NWDAF (1)
Input(variable) e.g. from OAM
  ~(i: different slice ): Slice specific attribute KPI, part of RAN/CN performance measurements
  ~part of RAN/CN performance measurements
  : reflect the weight of the above performance data
Bound of Object function(h(x))
  Slice priority
Object function(h(x))
  Slice Service Requirement: How many percent of UEs’ service experience(slice UE/flow QoS) satisfy per slice per application
Slice ID | 1 | 2 | 3 | 4 | … | N
Slice Priority | 1 | 1 | 2 | 2 | … | 9
Note 2: It is important to figure out better Slice level KPIs and RAN/CN performance measurements, which can be supported by operators. Close cooperation with SA5 is needed.
…
Please note higher slice priority has lower weight .
Note1: Function relationship between x and h(x) is only an example.
Slice 2
Slice 1
Slice N

## Slide 6: Candidate solution leveraging NWDAF (2)
OAM
RAN
CN
NWDAF
1-1. Data collection (slice level KPIs, RAN/CN performance measurements)
2-1. Data Analytics per slice priority (slice level KPIs, RAN/CN performance measurements)
PCF
AMF
UPF
…
1-2. slice priority + slice service requirement
3-1a. slice level KPIs + RAN performance measurements
3-1b. slice level KPIs + CN performance measurements
an example of procedure and how to use the data
2-2. Data Analytics per slice priority in use (decided by PCF)

## Slide 7
Thanks!