## Slide 1
Handling of slice based overload control at NG-RAN
NEC, Interdigital, AT&T, KDDI, NICT, Convidawireless
SA WG2 Meeting #130 S2-1900686
21 – 25 January 2019, Kochi, India rev of S2-1900433

## Slide 2
Rel-15 UE and Network behaviour
    An AMF invokes Slice based overload control at NG-RAN by sending Start Overload message containing a congested S-NSSAI(s).
    When a NG-RAN receives Requested NSAAI during the RRC connection establishment procedure and the requested NSSAI are indicated as congested by the AMF then the NG-RAN sends a GENERIC wait time in the RRC connection release to the UE.
    When the UE receives GENERIC wait time in the RRC connection Release message it will not send any AS and NAS signalling till the wait time expires. This procedure may block ALL services at the UE.

## Slide 3
  When the AMF requests NG-RAN to perform overload control for one service/Slice (S-NSAAI) then the NG-RAN will send generic wait time to the UE if the UE has sent only the congested S-NSSAI during the RRC Connection establishment procedure (e.g. in the RRC Connection Setup Complete message (enhanced E-UTRAN connected to 5G) or RRC Setup Complete message (NR connected to 5G)). As a result all the other services (essential services e.g. V2X) at the UE are blocked till the generic wait time expires. This will create bad user experience. The same issue happens in case of non-3GPP access also.
  For example a UE supports IoT, V2X and eMBB services. A IoT related slice is congested and the AMF requests 5G-RAN to perform overload control for IoT only. When the UE includes IoT slice only during the AS connection establishement procedure then the NG-RAN releases the AS connection with generic wait time. After receiving the generic wait time the UE is not allowed establish AS connection for any services. Therefore the user will not get V2X and eMBB services althougth eMBB and V2X slices are not congested. This has serious consequences for services like V2X.
Issue : Drawback of the Rel-15 UE and Network behaviour

## Slide 4
    Following solutions are proposed in Rel-16 to introduce a better mechanism to handle the slice based overload control at a NG-RAN and an UE. Two CRs are submitted for proposal 1 and proposal 2. It is proposed to captures Proposal 1 in the specification to solve the issue described in the discussion paper.
Proposal 1: Sending a slice specific wait time for each congested S-NSSAI.
The 5G-AN sends wait time for each congested S-NSSAI present in the requested S- NSSAI in the RRC Connection Release message. On receiving the wait time for each S- NSSAI the UE shall not initiate any NAS/AS signalling for this S-NSSAI till the wait timer is running.
Proposal 2: Sending a common wait time for all congested S-NSSAI.
The 5G-AN includes a common wait time for all congested S-NSSAI present in the requested NSSAI in the RRC Connection Release. The UE will run a single wait time for all congested S-NSSAI and shall not initiate any NAS/AS signalling related to the congested S- NSSAI till the timer expires.
Proposal

## Slide 5
RAN2 Specification: 3GPP TS 38.331 v 15.4.0
– RRCRelease-v1540-IEs ::= SEQUENCE {
waitTime RejectWaitTime OPTIONAL, -- Need N
nonCriticalExtension SEQUENCE {} OPTIONAL
}

## Slide 6
Comparison of current behaviour and Proposals.
Current Specification (23.501 v 15.4.0) | Proposal 1 (S2-1900434) | Proposal 2 (S2-1900435)
5.19.5.2 AMF Overload Control When releasing a 5G-AN signalling connection for the case c) above, the 5G-AN indicates to the UE an appropriate wait timer that limits further 5G-AN signalling connection requests until the wait timer expires. | When releasing a 5G-AN signalling connection for the case c) above, the 5G-AN indicates to the UE a separaten appropriate wait timer for each S-NSSAI present in the Requested NSSAI that limits further 5G-AN signalling connection requests related to the S-NSSAI(s) present in the Requested NSSAI until the corresponding wait timer expires. | When releasing a 5G-AN signalling connection for the case c) above, the 5G-AN indicates to the UE a singlen appropriate wait timer for S-NSSAI(s) present in the Requested NSSAI that limits further 5G-AN signalling connection requests for the S-NSSAI(s) present in the Requested NSSAI until the wait timer expires.
UE behaviour: The UE is not allowed to initiate any NAS signalling i.e. the UE CAN NOT perform Mobility Registration Update on changing Registration Area. MT paging will be missed. perform SR to get service of other Slice which is in allowed List. perform Registration update procedure to include S-NSSAI in the allowed S-NSSAI list. No new service is possible. | UE behaviour: The is allowed to initiate signalling and user services which are not indicated as congested. The UE can perform mobility Registration procedure. Service Request procedure to get services from other slices. Registration update procedure to include S-NSSAI in the allowed S-NSSAI list. No new service is possible. | UE behaviour: The is allowed to initiate signalling and user services which are not indicated as congested. The UE can perform mobility Registration procedure. perform Service Request procedure to get services from other slices. perform Registration update procedure to include S-NSSAI in the allowed S-NSSAI list. No new service is possible.
User impact:: If one service is congested then all the other services are blocked (e.g. congestion in IoT slide may block critical services V2X, URLCC. This is will have serious impact on user. Critical services WILL BE impacted | User Impact: when one service is indicated as congested it HAS NO impact on other services. There is advantage of proposal 1 over proposal 2 is that the UE will run different wait time for different slice as congestion levels can be different for different slices. | User Impact: when one service is indicated as congested it HAS NO impact on other services.