## Slide 1: Source: Ericsson, Nokia, Nokia Shanghai Bell Title: Correction to PDU Session Establishment for Home Routed Roaming Document for: Agreement Agenda Item: 6.5.3 Work Item / Release: 5GS_Ph1 / Release 15 tdoc : S2-1901490

## Slide 2
AMF
V-SMF
H-SMF
AAA
PDUSession_CreateSMContext Request
PDUSession_CreateSMContext Response
PDUSession_Create Request (vsmfPduSessionUri)
AAA Request
AAA Response
PDUSession_Update Request
N1N2Transfer Request
N1N2Transfer Response
PDUSession_Update Request
AAA Request
AAA Response
PDUSession_Update Response
N1N2Transfer Request
N1N2Transfer Response
Issue with PDU Session Establishment for Home Routed Roaming when DN-AAA is involved (from clauses 4.3.2.2 and 4.3.2.3 of TS 23.502 v15.4.1)
PDUSession_UpdateSMContext Request
PDUSession_Update Response
NAS (PDU Session Establishment Request)
NAS (Authentication)
NAS (Authentication)
PDUSession_Create Response
NAS (PDU Session Establishment Accept)
UE
PDUSession_UpdateSMContext Response
Issue: Not working, as the resource URI of H-SMF is not known by V-SMF yet

## Slide 3
AMF
V-SMF
H-SMF
AAA
2. PDUSession_CreateSMContext Request
PDUSession_CreateSMContext Response
3. PDUSession_Create Request
4. AAA Request
AAA Response
PDUSession_Create Response
5. N1N2Transfer Request
N1N2Transfer Response
8. PDUSession_Update Request
9. AAA Request
AAA Response
PDUSession_Update Response
13. N1N2Transfer Request
N1N2Transfer Response
Solution Alt 1: Create Response sent as first reply from H-SMF
7. PDUSession_UpdateSMContext Request
1. NAS (PDU Session Establishment Request)
6. NAS (Authentication)
NAS (Authentication)
14. NAS (PDU Session Establishment Accept)
UE
PDUSession_UpdateSMContext Response
PDUSession_Update Response
12. PDUSession_Update Request (N1, N2 container, mapped EPS bearer...)
PCF interaction
UPF interaction
Notes: In Nsmf_PDUSession_Create service operation, a number of parameters (see below) will have to be changed from Mandatory to Optional in Output:
  QFI(s), QoS Profile(s), Session-AMBR, QoS Rule(s), QoS Flow level QoS parameters if any for the QoS Flow(s) associated with the QoS rule(s), H-CN Tunnel Info, Enable pause of charging indication

## Slide 4
AMF
V-SMF
H-SMF
AAA
2. PDUSession_CreateSMContext Request
PDUSession_CreateSMContext Response
3. PDUSession_Create Request
4. AAA Request
AAA Response
5 PDUSession_Update Request
6 N1N2Transfer Request
N1N2Transfer Response
9. PDUSession_Update Request
10. AAA Request
AAA Response
PDUSession_Update Response
14. N1N2Transfer Request
N1N2Transfer Response
Solution Alt 2: Immediate reply from H-SMF (only difference from Alt 1 is gray marked)
8. PDUSession_UpdateSMContext Request
PDUSession_Update Response
1. NAS (PDU Session Establishment Request)
7 NAS (Authentication)
NAS (Authentication)
PDUSession_Create Response
15. NAS (PDU Session Establishment Accept)
UE
UPF interaction
PDUSession_UpdateSMContext Response
PCF interaction – final ARP
PDUSession_Update Response
13. PDUSession_Update Request (N1, N2, mapped EPS bearer contexts)
Difference from Alt 1
Notes: In Nsmf_PDUSession_Create service operation, a number of parameters (see below) will have to be changed from Mandatory to Optional in Output:
  QFI(s), QoS Profile(s), Session-AMBR, QoS Rule(s), QoS Flow level QoS parameters if any for the QoS Flow(s) associated with the QoS rule(s), H-CN Tunnel Info, Enable pause of charging indication

## Slide 5
AMF
V-SMF
H-SMF
AAA
PDUSession_CreateSMContext Request
PDUSession_CreateSMContext Response
PDUSession_Create Request (vsmfPduSessionUri)
AAA Request
AAA Response
PDUSession_Update Request
N1N2Transfer Request
N1N2Transfer Response
PDUSession_Update Request
AAA Request
AAA Response
PDUSession_Update Response
N1N2Transfer Request
N1N2Transfer Response
Solution Alt 3: PDUSession_UpdateSMContext Request received in V-SMF resulting in PDUSession_Update Response
PDUSession_UpdateSMContext Request
PDUSession_Update Response
NAS (PDU Session Establishment Request)
NAS (Authentication)
NAS (Authentication)
PDUSession_Create Response
NAS (PDU Session Establishment Accept)
UE
PDUSession_Update Response
PDUSession_UpdateSMContext Response
How V-SMF know it has to wait for UpdateSMContext Update ?
Should PDUSession_Update response be sent here?

## Slide 6
AMF
V-SMF
H-SMF
AAA
PDUSession_CreateSMContext Request
PDUSession_CreateSMContext Response
PDUSession_Create Request (vsmfPduSessionUri)
AAA Request
AAA Response
PDUSession_Update Request (hsmfPduSessionUri)
N1N2Transfer Request
N1N2Transfer Response
PDUSession_Update Request
AAA Request
AAA Response
PDUSession_Update Response
N1N2Transfer Request
N1N2Transfer Response
Solution Alt 4: H-SMF returns hsmfPduSessionUri in PDUSession_Update Request (existing call flow unchanged)
PDUSession_UpdateSMContext Request
PDUSession_Update Response
NAS (PDU Session Establishment Request)
NAS (Authentication)
NAS (Authentication)
PDUSession_Create Response
NAS (PDU Session Establishment Accept)
UE
PDUSession_UpdateSMContext Response
New: H-SMF add hsmfPduSessionUri as a new attribture.

## Slide 7: Comparison and Proposal
 | Alt 1 and Alt 2 | Alt 3 | Alt 4 | Comment
Call flow changed | Yes | Yes, Special handling in V-SMF, i.e. Nsmf_PDUSession_UpdateSMContext Request received in V-SMF results in sending of Nsmf_PDUSession_Update Response to H-SMF | No | 
Backward compatibility | No, some parameters in Nsmf_PDUSession_Create response are changed from Mandatory to Optional | Yes | Yes | 
[Observation-1] Alt 1 & Alt 2 are more SBI compliant, however the change is not backward compatible because a number of mandatory parameters will have to be changed to Optional. (Alt1 &2 would have been the best solution if they were brought up 6-9 month earlier)
[Observation-2] Alt 4 does not change the message flow, it’s backward compatible and the impact to the system is minimal.
[Proposal-1] It’s proposed to adopt Alt 4.
  See 23.502 CR1025 (S2-1901596)
Notes: In Nsmf_PDUSession_Create service operation, a number of parameters (see below) will have to be changed from Mandatory to Optional in Output:
  QFI(s), QoS Profile(s), Session-AMBR, QoS Rule(s), QoS Flow level QoS parameters if any for the QoS Flow(s) associated with the QoS rule(s), H-CN Tunnel Info, Enable pause of charging indication

## Slide 8
THANK YOU !