## Slide 1: Discussion on SA2 Edge computing study
Huawei, Intel

## Slide 2: Status quo of MEC in SA2- local routing & mobility
UE-aware local routing (SSC mode 2/3(incl. BP-based multi-homing)
UE IP changes during UE mobility
  L3/L4 connection (e.g. TCP/TLS/QUIC connection) using the new IP need to be renegotiated
UE-unaware local routing (UL CL-based)
UE IP does not change during UE mobility
  If NAT is used after local PSA, the “UE IP” may change from the PoV of MEC APP server in case local PSA relocated

## Slide 3: Status quo of MEC in SA2- AF influenced traffic routing
Two mechanisms have been standardized for AF to provide traffic routing information to the SMF to influence the UPF (re)selection.
For MEC case, AF is implied as part of MEC environment.

## Slide 4: Open issues – How to integrate EC with 5GS
As the important deployment scenario in 5G era, MEC should be organically integrated with 5GS to maximum the benefits of MEC deployment in operator’s environment.
Currently the relationship between the two systems, and if it’s possible to integrate with each other are not clear.
  E.g. the following texts are quoted from ETSI MEC white paper
    In a 5G integrated deployment the role of the data plane is delegated to the User Plane Function (UPF). A UPF plays the central role in routing the traffic to desired applications and network functions.
From: ETSI white paper <<MEC in 5G networks>>
https://www.etsi.org/images/files/ETSIWhitePapers/etsi_wp28_mec_in_5G_FINAL.pdf
UPF
Edge computing system
An example for integration of EC and 5GS

## Slide 5: Open issues – Discovery of application server hosted in MEC
In MEC deployment, there can be multiple server instances with different IP addresses serving same FQDN. The DNS requests from UE need to be resolved to IP of an local MEC APP server(e.g. IP2 in above figure) for the following local routing.
When UE moves, the DNS resolution of a FQDN of MEC APP server need to be updated for future MEC APP server discovery.
Note: As DNS is the most dominant method for request routing, some other mechanisms e.g. any cast, URL rewriting, HTTP direction, may also be used.

## Slide 6: Open issues – Localized network capability exposure
  Current network capability openness are based on multiple CP NFs, e.g. AMF, SMF, PCF and NEF. These CP NFs are most likely be deployed at a “high” location to avoid frequently relocation. However, this means current network capability exposure (via AMF and NEF) are relative slow and non-optimized.
  Some simple applications (e.g. video stream server) are stateless, hence cannot invoke network openness APIs to get the network information.
  An localized/enhanced network capability exposure need to be investigated to meet the requirements of MEC APP servers.

## Slide 7: Open issues – Seamless application migration
Application migration based on UE location, which can be done by methods e.g.
  VM/Docker migration
  L3/L4+application layer context migration
After successful application migration, the user plane path is changed to new application location, which can be done by e.g.
  Case 1: SSC mode 2/3/BP, UE use new IP to re-establish L3/L4 connection to the new app server
  Case 2: ULCL, UE use same IP to continue the old L3/L4 connection to the new app server
Issues need to be addressed in SA2
  During application migration, how to ensure the on-fly packets can be lossless and in-order handled.
  In above case 1, is it possible/required to avoid the re-establishment of L3/L4 connection
  Note: This study focuses on the optimized packet routing mechanism to avoid packet losing and disordering. The details of application(context) migration is not in the scope of the study.

## Slide 8: Open issues – Traffic steering for MEC applications
Gi-LAN traffic steering has been standardized in EPC TS 23.203, but not studied for 5GC yet.
Why traffic steering should be considered together with EC in 5G
  Traffic steering is a common requirement for service functions(e.g. . NAT, anti-virus, parental control, DDoS protection…) outside UPF.
  In 5G era, these functions may be deployed on either MEC or traditional environments.
  It’s an opportunity to study a unified traffic steering mechanism in 5GS for both MEC and other local DN deployments.
Further, Investigate necessary UPF enhancements (e.g. load balancing, MPTCP/QUIC proxy)required for flexible MEC deployment

## Slide 9: 5GS MEC deployment guideline
To support the edge computing and deployment together with 5GS, some enablers have been specified since Release 15 as described in clause 5.13 in 3GPP TS 23.501, e.g. Locally deployed UPF and DN, UL CL based Local Routing and Traffic Steering, User plane (re)selection, and AF influenced traffic routing. Related enhancement are further specified in Release 16 5G_URLLC work item.
However, currently in the industry, it is still lack of common understanding on the end-to-end system architecture when both the 5GS and edge computing are deployed. The relationship between 5GS and edge computing system is not obvious to the reader given that the upper-layer MEC aspects are out of scope of TS 23.501 and 23.502, which can lead to potential obstacles for the future business deployment of edge computing together with 5GS. What would be useful for the first-time reader is to provide some guidance on how to use the enablers defined in clause 5.13 of TS 23.501 to support the time sensitive services (e.g. V2X, online gaming, VR/AR, etc.) including aspects of Session and Service Continuity, efficient traffic routing to the localized DN, differentiated QoS handling and differentiated charging rate based on the differentiated QoS offer.

## Slide 10: Summary: New edge computing study item in SA2
To address the following technical gaps for supporting MEC with 5GS
  Investigate the potential architecture impact when considering edge computing/localized DN;
  Discovery of IP address of application server deployed in edge computing environment;
  System supports for seamless change of application server serving the UE;
  Localized network capability exposure between network and edge applications;
  Supporting for traffic steering in N6-LAN deployed in edge computing environment ;
  User plane enhancement to support application in MEC/localized DN;
To provide deployment guidelines for typical MEC use cases including URLLC, V2X, AR/VR/XR, UAS etc., based on the existing Rel-15/16 MEC enablers in TS 23.501 and TS 23.502 and new enablers derived in this study.

## Slide 11: Thank you! Your supports are welcome

## Slide 12: Backup

## Slide 13: MEC related standardization in ETSI MEC ISG
Mobile edge platform manager
  Management of edge platform infrastructure
  Management of Life cycle of MEC applications
  Management of Application related requirements and rules, e.g. service authorization, DNS configuration, traffic rule.
Mobile edge orchestrator
  Maintain the E2E view of the MEC system
  Management of MEC application installation
  Application instantiation, termination and migration
Edge platform
  MEC service registration and service discovery
  Provide network information to the application, e.g. UE location
  DNS handling
  Control of the MEC data plane for Traffic rules
Data Plane
  Execute the traffic rules to route the traffic to the appropriate application(s)
Potential overlapping with traffic routing defined in 5GS