## Slide 1: Contents of document are the same as the EPC Dedicated Bearers for Ethernet endorsed in S2-1813344
Document for Information.
Source: Vodafone
SA WG2 Meeting #131
February 25 – March 1, 2019, Santa Cruz, Tenerife, Spain
Agenda item:6.31 EPC Dedicated Bearers for Ethernet
Tdoc S2-1902143

## Slide 2: EPC Dedicated Bearers for Ethernet
Source: Vodafone, Qualcomm Inc., MediaTek, Telecom Italia, Cisco Systems
SA WG2 Meeting #129bis November 26 - 30, 2018, West Palm Beach, USA
Agenda item: 7.1
Tdoc S2-1813344
Rev of S2-182493

## Slide 3: Rationale
3GPP’s ecosystem continues to expand to more than smartphones
Many parts of the world (see annex) might not be in 5GCore coverage
Small/Medium Enterprises in developed countries might not get dedicated in-building cells
Reasonable number of applications (machines) expected to only use Ethernet (without IP)
Many machines require QoS with some guarantees, e.g. a GBR bearer
EPC does not allow GBR bearers to be the default bearer.
 Dedicated bearer support for ‘Ethernet’ would be useful for EPC in Rel 16
Release 15 situation summary
R15 5GCore maps its Ethernet PDN type to “Non-IP” in EPC
Any 5GCore Ethernet GFBR QoS Flows are mapped onto the Default PDN connection at mobility to EPC

## Slide 4: R15 components that can be reused
TS 29.244 (clause 5.13) CUPS stage 3 provides support for a SMF to configure a UPF for Ethernet use - this would already be used by a 5G-Core capable UE needing an Ethernet PDN type that establishes PDN connectivity over EPC access.
In line with S2-1811560, not change the EPC's PCC specs, but e.g. use APN to select a PGW-C that supports "SMF+PGW-C" functionality and the N7 interface (with Ethernet support) to the PCF
Use the (Release 5) ‘container functionality’ of the EPC Traffic Flow Template to carry Ethernet header TFTs between PGW-C and UE. This could be invisible to a VPLMN that supports R13 "non-IP".

## Slide 5: More detail on R15 Status
Release 13 EPC supports “non-IP” PDN connections but there is very limited description of how these PDN connections could be used for Ethernet support.
Release 15 5GCore supports “Ethernet” and “Unstructured” PDN connections and – at mobility with EPC – maps them to non-IP.
At handover/mobility, from 5GCore to EPC, dedicated bearers are not transferred.
TS 23.401 clauses 4.3.17.8.1 and 4.7.2.1 indicate that Dedicated Bearers are not supported for the Non-IP PDN type, but do not specify that any node is required to reject them.
TS 24.301 clause 6.1.1 says that the network shall not initiate Dedicated Bearers for non-IP PDN connections -> but UE support for an Ethernet TFT would be needed.
TS 36.323 (PDCP) has SDU Type specified, but probably only for SideLink (PC5) use.
TS 36.413/38.413 indicate PDN type (Non-IP/Unstructured/Ethernet) to the RAN to disable Header Compression.
Packet filters are carried in the TFT in EPC and are specified in TS 24.008. The TFT is a container mechanism between UE and PDN-GW and e.g. is used for TS 24.229 Authentication Tokens.

## Slide 6: Proposals
Agree to draft TEI-16 EPC CRs for dedicated bearer support on EPC for 3GPP access.
Decide whether to use Non-IP PDN type in EPC, or, new EPC Ethernet PDN type
Allocate 1.5 TU spread over 2 meetings in SA2 for this work.
d) No RAN impact expected

## Slide 7: END