## Slide 1: URLLC Key Issue #7: Automatic GBR service recovery after handover / at GFBR establishment Questions to help find Way Forward
Document for input to drafting session
Source: Vodafone
SA WG2 Meeting #131 February 25 – March 1, 2019, Santa Cruz, Tenerife, Spain
Agenda item: 6.20
Tdoc S2-1902185

## Slide 2: After Kochi meeting, KI#7 has at least the following proposed solutions (List from S2-1901818, LG Electronics)
Solution #16 "Automatic GBR service recovery after handover"
Solution #20 "SMF starts the pending timer for the non-accepted GBR QoS flow" : proposed by S2-1901362 (CR#0010, Qualcomm)
Solution #21 "Extending notification control for QoS flow setup and handover" : proposed by S2-1901363 (CR#0011, CATT)
Solution #22 "Automatic GBR service recovery after handover" : proposed by S2-1901364 (CR#0013, LGE)
Solution #23 "Always On control for URLLC GBR QoS Flow" : proposed by S2-1901374 (CR#0015, Tencent)

## Slide 3: Key Issue #7; Automatic GBR service recovery after handover (TR 23.725 v1.2.0)
When a machine needs a Guaranteed Bit Rate service, it is likely to need that quality level in order to do its job. Hence if the QoS level cannot be maintained (e.g. handover into a congested cell; temporary cell overload due to higher priority services; etc), the QoS level should be restored as soon as possible, and, without a storm of signalling messages.
Release 15 5GC has partially solved this issue by introducing a "notification" mechanism that allows the core network to request the RAN to not release the radio bearer/QoS Flow when the QoS guarantee cannot be met, but, instead to notify the Core Network when the QoS drops, AND, when the RAN has restored the QoS level. This allows the controller of the machine (e.g. car/train) to adapt its behaviour (e.g. reduce speed) and ensures that the RAN continues to try to restore the QoS level while the device is in that cell.
However, at Xn or N2 handover, the target RAN node applies admission control and if it cannot support the required GBR QoS, the target RAN node does not establish that QoS Flow. In such a case, if, e.g. due to movement of the UE, the source RAN node has no choice but to handover to that target RAN node, then the target RAN node will complete the handover but will NOT notify the CN if and when the GBR QoS can be supplied to that UE.
As the machine needs to have its GBR service restored as soon as possible, the CN needs to repeatedly attempt to re-establish the GBR service. These re-attempts involve a considerable number of signalling messages, and are sent without any awareness of RAN congestion or potential link quality.
This is an inadequate solution for any mobile "non-human device" that needs to maintain a GBR data link during mobility (e.g. a car, a train, robots moving around a factory).

## Slide 4: Questions (1)
a) is a core network timer based solution sufficient?
If yes we can probably stop here….
… but key issue #7 seems to make it clear that service restoration is needed As Soon As Possible
b) is this an MBR>GBR case (as in V2X TR 23.786 solutions #16, #17, #27) or does this relate to the Bit Rate that the machine really needs?
…The key issue seems to be focussed on the latter case (or when rate adaption as reached the lowest usable bit rate)
c) Is it useful that the RAN can check over a time period [eg 2 seconds] before notifying the Core Network that the GFBR QoS level is available?
- in existing establishment/handover processes, the RAN will tend to make a decision based on the instantaneous radio situation in the NG-RAN?

## Slide 5: Questions (2)
d) do we need to define a new QoS parameter or just re-use the R15 Notification Control parameter?
- the existing R15 notification control parameter assumes that the application can adapt;
- however, this is the case of a machine that needs that GBR
e) do we want the function to work at Flow Establishment (and Modification)?
This is the ‘bearer establishment’ case, not the handover case, and does not seem to be part of R15 (as the RAN would reject the GFBR if it cannot serve it)
f) (when the QoS cannot be met) at handover, should the target reject the flow and then the core network request its (re-)establishment, or, does the RAN accept the flow and ‘notify’ the core network that QoS is not met?

## Slide 6: Questions (3)
g) (when the QoS cannot be met) does the RAN map the GFBR flow into e.g. the same Logical Channel Group as the default flow, or, does it allocate the GFBR flow to a separate Logical Channel Group (LCGs are linked with uplink Buffer Status Reports)?
h) Will the RAN continue allocating the uplink/downlink resource to the QoS Flow (after notifying the core network)
i) Does the UE need to be informed by signalling that the GFBR can’t be guaranteed?
j) (if g is yes) is this RRC or MM or SM signalling?

## Slide 7: End