## Slide 1: Source: Ericsson Title: Implication of not requiring S6b from PGW-C+SMF for ePDG support Document for: Discussion/Decision Agenda Item: 6.31 Work Item / Release: TEI 16
SA WG2 Meeting #133 Reno, Nevada, USA, 13-17 May 2019
Tdoc S2-1905073

## Slide 2: Background
During 3GPP SA2#132 (April 08-12, 2019),
  A proposal is made to make S6b optional, see discussion S2-1903424 and WID S2-1904565
The above proposal assumes impact only on PGW-C+SMF to support
  N10 for PDN connection establishment from ePDG and
  P-CSCF restoration
The above proposal assumes zero-impact on HSS and UDM
The intention to make S6b optional thus to remove diameter interface from PGW-C+SMF also implies Gx will not be supported (even for UEs not capable of 5G)
PGW-C+SMF
UDM
AAA
HSS
WiFi AP
ePDG
2
3
4
5
6
S6b
Swx
Swm
N10
1
Numbers are for message flow on next slide
PCF
PCRF
Gx
N7
4a

## Slide 3: Implication of not requiring S6b from PGW-C+SMF for ePDG support (1/3)
Simplified flow, Text (or line) in Orange mean implication
PGW-C+SMF
AAA
HSS
ePDG
UDM
2. Swm: Diameter-EAP-Request
3. Swx: Multimedia-Authentication-Request
Swx: Server-Assignment-Request
4. S2b: Create Session Request
5. S6b: AA-Request (PGW ID)
HSS stores PGW Id received from AAA
6. Swx: Server-Assignment-Request (Server-Assignment-Type=PGW_Update, PGW ID)
Current behavior (i.e. using S6b)
N10: Nudm_UECM_Registration Request (NF ID, SUPI, PEI, NF Type, PDU Session ID, DNN, PGW-C FQDN…)
UDM gets PGW-C FQDN, and synchronized with HSS
If N10 (instead of S6b) is used, and diameter interface is removed from PGW-C+SMF
[Obervation-2] If N10 is used instead of S6b, UDM needs to differentiate if Nudm_UECM_Registration is for ePDG support or for PDU Session setup in 5GC, and HSS will need a differentiate if PGW ID (for a DNN) from UDM is for ePDG support, and if so the HSS does not need to notify the AAA and ePDG of the PGW ID (as in this case it’s the ePDG that selects the PGW ID and such notification is superfluous) (see next slide for illustration)
[Obervation-3] PDU Session ID is mandatory in Nudm_UECM_Registration service operation, which implies that UE must be 5G capable (i.e. support N1 mode) in order to provide PDU Session ID in PCO during PDN connection establishment;
[Obervation-1] HSS receives PGW UPDATE from AAA, and HSS accepts only the update if the user is registered from the same AAA.
1. IKEv2 Authentication and Tunnel Setup
PCRF
4a. Gx: CCR/A-I
PCF
N7: Npcf_SMPolicyControl_Create (PDU Session ID, DNN, S-NSSAI)
[Obervation-1a] PDU Session Id is mandatory in PCF interaction, implying that UE must be 5G capable.
Notes: == 23.502 ==
5.2.3.2 Nudm_UECM (UECM) service
5.2.3.2.1 Nudm_UECM_Registration service operation
Service operation name: Nudm_UECM_Registration
Description: Register UE's serving NF (if NF Type is AMF, SMSF) or Session's serving NF (if NF Type is SMF) on the UDM. This operation implies the following:
- The authorization, if applicable, to register the NF service consumer in UDM for the UE (e.g. based on UE roaming/RAT restrictions applicable when NF type is AMF). If this is successful, the NF service consumer is set as a serving NF for the corresponding UE/Session context.
- When the consumer is AMF, it is implicitly subscribed to be notified when it is deregistered in UDM. This notification is done by means of Nudm_UECM_DeregistrationNotification operation.
- When the consumer is AMF or SMF, it may optionally use this operation to subscribe to be notified of the need for P-CSCF Restoration. This notification is done by means of Nudm_UECM_PCscfRestoration operation. For more information regarding P-CSCF restoration procedures see TS 23.380 [38].
Inputs, Required: NF ID, SUPI, PEI, NF Type, Access Type (if NF Type is AMF, SMSF), PDU Session ID (if NF Type is SMF). If NF Type is SMF: DNN or Indication of Emergency Services, PGW-C+SMF FQDN for S5/S8 if the PDU Session supports EPS interworking. If NF type is AMF and Access Type is 3GPP access: Registration type. If NF type is SMSF: SMSF MAP address and/or Diameter address.
Inputs, Optional: P-CSCF Restoration notification information, GUAMI, backup AMF(s) (if NF Type is AMF), "Homogeneous Support of IMS Voice over PS Sessions" indication (if NF Type is AMF). Backup AMF(s) sent only once by the AMF to the UDM in its first interaction with the UDM.
Outputs, Required: Result indication.
Outputs, Optional: None.
See step 14a of clause 4.2.2.2.2 for an example usage of this service operation.

## Slide 4: Illustration for [Observation-2]
PGW-C+SMF
UDM
AAA
HSS
ePDG
Swx
Swm
{PGW FQDN, DNN}
N10: Nudm_UECM_Registration Request (NF ID, SUPI, PEI, NF Type, PDU Session ID, DNN, PGW-C FQDN, indication for ePDG support…)
When HSS receives PGW FQDN for a DNN for ePDG support, the HSS should not notify the AAA and ePDG of the PGW FQDN is already aware of the PGW FQDN.

## Slide 5: Implication of not requiring S6b from PGW-C+SMF for ePDG support (2/3)
Current P-CSCF restoration (ref. 23.380)
PGW-C+SMF
AAA
HSS
ePDG
S6b
Swx
Swm
IMS
S-CSCF
1. Cx: P-CSCF rest ind
2. P-CSCF rest ind
3. P-CSCF rest ind
PGW-C+SMF
UDM
AAA
HSS
ePDG
Swx
Swm
N10
IMS
S-CSCF
1. Cx: P-CSCF rest ind
?
[Observation-4] P-CSCF restoration may not work if HSS sends the P-CSCF rest ind to AAA as Swx session exist, unless HSS becomes aware if S6b or N10 is used for PDN connection established by ePDG which means impact on HSS, and maybe on UDM to differentiate if N10 is used for PDN connection from ePDG or for PDU Session in 5GC.
?
P-CSCF rest ind
P-CSCF rest ind
P-CSCF restoration if N10 is used instead of S6b
P-CSCF rest ind over S6b

## Slide 6: Implication of not requiring S6b from PGW-C+SMF for ePDG support (3/3)
Scenarios | UE is 5GC NAS capable? | Network allows 5GC interworking | N10 possible?
Scenario-1 5GC interworking supported | Y | Y | In non-roaming and home routed roaming, N10 may be possible with implication in [Observations-2&3&4]. In LBO roaming, HPLMN does not have control whether or N10 can be used by the VPLMN
Scenario-2 5GC interworking NOT supported | Y | N | If legacy PGW-C is selected, then S6b shall be used as in pre-Rel16 network. If combined PGW-C+SMF is used, N10 may be possible with implication as in Scenario-1.
Scenario-3 UE not 5G capable | N | Does not matter | S6b (and Gx) shall be used unless backward incompatible change for PDU Session ID is introduced.
[Observation-5] For Scenario-1 (i.e. UEs supporting N1 mode and NW supporting 5GC interworking), in non-roaming and home routed roaming, N10 may be possible but with additional impact on HSS and PGW-C as captured in [Observations-2&3&4], however, in LBO roaming, the HPLMN does not have control whether N10 can be used by the VPLMN.
[Observation-6] For Scenario-3 (i.e. UEs not supporting N1 mode), S6b and Gx are required anyway for PDN connection established by ePDG, unless PDU Session ID is changed from Mandatory to Optional over N10 and N7 which is backward incompatible change that should be avoided as much as possible, or PGW-C fake a PDU Session ID which is problematic when multiple PGW-C+SMFs are involved.
[Observation-7] With the assumption that no backward incompatibility change will be introduced, if a PGW-C with SMF capability (i.e. PGW-C+SMF) is also expected to serve the UEs not supporting N1 mode, then such PGW-C+SMF shall continue to support S6b and Gx for PDN connection established by ePDG, i.e. S6b and Gx cannot be made optional.

## Slide 7: Implication on scenario of UEs not capable of 5G attached to the network via EUTRAN
Requirement to support Gx in [Observation-6] also applies to the scenario that UEs not supporting N1 attach to the network via EUTRAN.

## Slide 8: Summary of Observations
[Obervation-1] HSS receives PGW UPDATE from AAA, and HSS accepts only the update if the user is registered from the same AAA.
[Obervation-1a] PDU Session Id is mandatory in PCF interaction, implying that UE must be 5G capable.
[Obervation-2] If N10 is used instead of S6b, UDM needs to differentiate if Nudm_UECM_Registration is for ePDG support or for PDU Session setup in 5GC, and HSS will need a differentiate if PGW ID (for a DNN) from UDM is for ePDG support, and if so the HSS does not need to notify the AAA and ePDG of the PGW ID (as in this case it’s the ePDG that selects the PGW ID and such notification is superfluous)
[Obervation-3] PDU Session ID is mandatory in Nudm_UECM_Registration service operation, which implies that UE must be 5G capable (i.e. support N1 mode) in order to provide PDU Session ID in PCO during PDN connection establishment;
[Observation-4] P-CSCF restoration may not work if HSS sends the P-CSCF rest ind to AAA as Swx session exist, unless HSS becomes aware if S6b or N10 is used for PDN connection established by ePDG which means impact on HSS, and maybe on UDM to differentiate if N10 is used for PDN connection from ePDG or for PDU Session in 5GC.
[Observation-5] For Scenario-1 (i.e. UEs supporting N1 mode and NW supporting 5GC interworking), in non-roaming and home routed roaming, N10 may be possible but with additional impact on HSS and PGW-C as captured in [Observations-2&3&4], however, in LBO roaming, the HPLMN does not have control whether N10 can be used by the VPLMN.
[Observation-6] For Scenario-3 (i.e. UEs not supporting N1 mode), S6b and Gx are required anyway for PDN connection established by ePDG, unless PDU Session ID is changed from Mandatory to Optional over N10 and N7 which is backward incompatible change that should be avoided as much as possible, or PGW-C fake a PDU Session ID which is problematic when multiple PGW-C+SMFs are involved.
[Observation-7] With the assumption that no backward incompatibility change will be introduced, if a PGW-C with SMF capability (i.e. PGW-C+SMF) is also expected to serve the UEs not supporting N1 mode, then such PGW-C+SMF shall continue to support S6b and Gx for PDN connection established by ePDG, i.e. S6b and Gx cannot be made optional.

## Slide 9: Proposal
Based on [Observation-1] ~[Observation-7],
  using N10 instead of S6b for PDN connection establishment from ePDG implies additional impact on PGW-C, HSS and maybe UDM.
  The combined PGW-C+SMF shall support S6b and Gx for UEs not capable of 5G, unless only legacy PGW-C is mandated for those UEs, or backward incompatible change (i.e. PDU Session ID made Optional from Mandatory) is introduced (implication needs to be further investigated for incompatibility).
It’s proposed to keep S6b as it is today for PDN connection establishment from ePDG, and to keep Gx for UEs not capable of 5G.
[Proposal-1] It’s proposed NOT to use N10 for S6b for PDN connection establishment from ePDG which means that PGW-C+SMF shall continue to support S6b.
[Proposal-2] It’s proposed that PGW-C+SMF continue to support Gx if the PGW-C+SMF is also expected to serve UEs not supporting N1 mode. This proposal applies to scenarios that such UEs attach to the network via ePDG and via EUTRAN.

## Slide 10
THANK YOU !