## Slide 1: Source: Ericsson Title: Enhancement to Monitoring Event Configuration and Network Parameter Configuration Document for: Discussion/Decision Agenda Item: 6.31 Work Item / Release: TEI16
SA WG2 Meeting #133 Reno, Nevada, USA, 13-17 May 2019
Tdoc S2-1905078

## Slide 2: Introduction
Issue: in Rel-15: HSS accept only one request for pTAU/RAU timer setting and any new request if accepted will result in cancellation of the previously accepted Monitoring Request per TS 23.682 v15.8.0:
      5.6.1.3 Specific Parameters for Monitoring Event: Loss of connectivity
      5.6.1.4 Specific Parameters for Monitoring Event: UE reachability
      …If the subscribed periodic RAU/TAU Timer was previously set by a different Monitoring Request identified by a different SCEF Reference ID for the same UE then, depending on operator configuration, the HSS either performs step 8 to reject the Monitoring Request with an appropriate Cause or accepts the request. …In case the HSS accepts this request, then it cancels the previously accepted Monitoring Request by including the SCEF Reference ID of that Monitoring Request in step 8
    Issue#1 may happen in the following scenarios:
    Scenario-1: Multiple configurations of the same event type
    Discussed in S2-1900455 during SA2#130 and attempted to be addressed in S2-1904512 (in SA2#132, postponed) which proposed to provision the multiple configurations from the HSS to the MME, impacting also on S6a and MME.
    Scenario-2: Configurations from different event types, e.g. configurations from both monitoring event type “Loss of Connectivity” and monitoring event type “UE Reachability” could affect setting of the pTAU timer
      Remain to be addressed
    Scenario-3: Multiple network parameter configuration, and possibly combined with Scenario-2
      Remain to be addressed

## Slide 3: Discussion – SCS/AS input for setting subscribed parameter (1/2)
[Observation-1] There are multiple input parameters from SCS/AS to 3GPP network to set the same subscribed parameter,
  Multiple configurations from different SCS/ASes for the same monitoring event type, and/or
  Configurations from multiple monitoring event types, and/or
  Network Parameter Configuration
Subscribed pTAU/RAU Timer
Specific parameter for monitoring event “UE Reachability”:
Maximum latency
Network para configuration:
Maximum latency
Local O&M configuration
From SCS/ASes to SCEF and then to HSS
Subscribed Active Time
Specific parameter for monitoring event “UE Reachability”:
Maximum Response Time
Network configuration:
Maximum Response Time
Local O&M configuration
From SCS/AS to SCEF and then to HSS
Specific parameter for monitoring event “Loss of connectivity”:
Maximum Detection Time
Specific parameter for monitoring event “Loss of connectivity”:
Maximum Detection Time
Specific parameter for monitoring event “UE Reachability”:
Maximum latency
Network para configuration:
Maximum latency
Specific parameter for monitoring event “UE Reachability”:
Maximum Response Time
Network configuration:
Maximum Response Time
1…n
1…n
1…n
1…n
1…n

## Slide 4: Discussion – SCS/AS input for setting subscribed parameter (2/2)
Relation between configurations for the monitoring event(s) and Network Parameter Configuration
  TS 23.682 has the following:
  5.6.1.4 Specific Parameters for Monitoring Event: UE reachability
  UE reachability indicates when the UE becomes reachable for sending either SMS or downlink data to the UE, which is detected when the UE transitions to ECM-CONNECTED mode (for a UE using Power Saving Mode or extended idle mode DRX) or when the UE will become reachable for paging (for a UE using extended idle mode DRX). This monitoring event supports Reachabilty for SMS and Reachability for Data. Only a One-time Monitoring Request for Reachability for SMS is supported. The SCS/AS may include the following parameters in the Monitoring Event configuration request to the SCEF:
  - Reachability Type indicating whether the request is for "Reachability for SMS", or "Reachability for Data", or both.
  …
  NOTE 3: The Network Parameter Configuration via SCEF feature (see clause 4.5.21) feature supersedes the option of setting Reachability Type to "configuration" during configuration of the UE Reachability Monitoring Event which is no longer recommended.
[Observation-2] Reachability Type “configuration” mentioned in NOTE 3 does not seem to be mentioned anywhere else.
[Observation-3] It’s unclear if Network Parameter Configuration supersedes the configurations of an monitoring event, e.g. if Maximum Latency in Network Parameter Configuration supersedes the Maximum Latency in monitoring event “UE reachability” when Reachability Type is “Reachability for SMS” or “Reachability for Data”.

## Slide 5: Discussion – Setting subscribed pTAU (1/2)
Clause 5.6.1.3 of TS 23.682 specifies the following:
  5.6.1.3 Specific Parameters for Monitoring Event: Loss of connectivity
  Loss of connectivity indicates when the 3GPP network detects that the UE is no longer reachable for either signalling or user plane communication. Such condition is identified when the mobile reachability timer expires in the MME or SGSN (see TS 23.401 [7], TS 23.060 [6], when the UE detaches and when an active UE is purged (see TS 29.272 [31])). The SCS/AS may provide a Maximum Detection Time, which indicates the maximum period of time without any communication with the UE after which the SCS/AS is to be informed that the UE is considered to be unreachable.
  Step 4 …HSS sets the subscribed periodic RAU/TAU timer using the value of Maximum Detection Time.
[Observation-4] Monitoring event “Loss of Connectivity” is reported at the expiration of mobile reachability timer, or at UE detached, or UE purged.
[Observation-5] In our understanding, Maximum Detection Time indicates how tolerant the SCS/AS is, regarding the period of time without any communication with the UE. For example, if an SCS/AS includes MDT or Maximum Latency 3h, it means
  The SCS/AS want to be aware (i.e. get notified) when the 3GPP detects Loss of Connectivity, regardless of the reason (e.g. expiration of mobile reachable timer, or UE detached, or UE purged), and
  (2) The SCS/AS can accept that a UE being considered “Loss of Connectivity” if the UE does not communicate with the network UP TO 3h.
  (1) and (2) above do not mean that the 3GPP network cannot report the detected Loss of Connectivity event before the 3h is reached, otherwise there will be two consequences:
    Consequence-1: there will be an issue that an SCS/AS with longer MDT may still consider the UE reachable and try to send packets to the UE but will get dropped, and
    Consequence-2: Loss of Connectivity due to UE detach or UE purge will not be possible to be reported as the UE’s context may be removed as part of UE detach or purge procedure. To request a UE that does not have (valid) UE Context (i.e. not existing in the network) to report an event does not make sense.
  Based on the above, any pTAU/RAU timer not longer than the interval indicated in the Maximum Detection Time should be able to fulfill the requirement of SCS/ASes, i.e. if multiple SCS/ASes request different values of Maximum Detection Time for the monitoring event “Loss of connectivity”, and if the lowest value is used for setting the pTAU/RAU timer, the requirements from all the SCS/ASes will be fulfilled.

## Slide 6: Discussion – Setting subscribed pTAU (2/2)
Per clause 5.6.1.4 of TS 23.682, Maximum Latency indicating maximum delay acceptable for downlink data transfers. Maximum Latency is used for setting the periodic TAU/RAU timer for the UE as it sets the maximum period after which a UE has to connect to the network again and thereby becomes reachable.
[Observation-6] In our understanding, any delay shorter than the interval indicated in the Maximum Latency should be able to fulfill the requirement of the SCS/AS, i.e. if multiple SCS/ASes request different values of Maximum Latency for the same event, and if the lowest value is used for setting the pTAU/RAU timer, then the requirements from all the SCS/ASes will be fulfilled.
[Observation-7] By the same analogy as in [Observation-5 &-6], if different values from different monitoring events and/or from network configuration are requested by the SCS/ASes, and if the lowest value is used for setting the pTAU/RAU Timer, then the requirements from all the SCS/ASes will be fulfilled.
[Observation-8] As captured in [Observation-5, -6, &-7], if the lowest value from different SCS/AS requests is chosen, all the SCS/ASes’ requirement will be fulfilled, and in our view there is no need for HSS to cancel the monitoring request previously used to set the pTAU/RAU timer.
Based on [Observation-5] ~[Observation-8], the following is proposed:
[Proposal-1] HSS maintain the requests from different SCS/ASes as follows:
  Multiple configurations for the same monitoring event type; and
  Multiple configurations from different monitoring event types; and
  Multiple Network Parameter Configurations
[Proposal-2] When multiple input parameters are used in selecting the subscribed pTAU/RAU timer, the HSS use the lowest value to set the pTAU/RAU Timer.

## Slide 7: Discussion – Setting subscribed Active Time
Per clause 5.6.1.4 of TS 23.682, Maximum Response Time indicating the time for which the UE stays reachable to allow the SCS/AS to reliably deliver the required downlink data. Maximum Response Time is used for setting the Active Time for the UE. When the UE uses extended idle mode DRX, the Maximum Response Time is used to determine how early this monitoring event should be reported to the SCS/AS before the next Paging Occasion occurs.
[Observation-9] For the setting of the subscribed Active Time, if the highest values from the requested configurations and network parameter configurations that are accepted by the HSS is used for setting the Active Time, then the requirements from all the SCS/ASes will be fulfilled.
[Proposal-3] When multiple input parameters are used in selecting the subscribed Active Time, the HSS use the highest value to set the Active Time.
The definition of “Max Response Time” seems misleading, it should be something like “minimum active time” ?

## Slide 8: Discussion –HSS-SCEF-SCS/AS interactions when the configuration from the monitoring request or network parameter configuration from some SCS/ASes are not selected
If the configuration from the monitoring request or network parameter configuration from some SCS/ASes are not selected, e.g.
  SCS/AS1 request 3h for Maximum Latency for monitoring event “UE Reachability”,
  SCS/AS2 request 2h for Maximum Latency for monitoring event “UE Reachability”
  based on [Proposal-2] and [Proposal-3], HSS will select 2h. It may be necessary to inform the SCS/AS1 that 2h (instead of 3h) is applied in the 3GPP network.
[Proposal-4] As a result of [Proposal-2] or [Proposal-3], the HSS optionally notifies the SCEF (which then notifies the SCS/AS) of the actual value that is being applied in the 3GPP network.

## Slide 9: Proposals
[Proposal-1] HSS maintain a table including the following:
  Multiple configurations for the same monitoring event type; and
  Configurations from different monitoring event types; and
  Multiple Network Parameter Configurations
[Proposal-2] When multiple input are used in selecting the subscribed pTAU timer, the HSS use the lowest value from the different input to set the pTAU Timer.
[Proposal-3] When multiple input are used in selecting the subscribed Active Time, the HSS use the highest value from the different input to set the Active Time
[Proposal-4] As a result of [Proposal-2] or [Proposal-3], the HSS optionally notifies the SCEF (which then notifies the SCS/AS) of the actual value that is being applied in the 3GPP network.
  23.682 CR0448 (S2-1905079)
NOTE: The above proposal affects only the handling in HSS and does not impact S6a interface and MME.

## Slide 10
THANK YOU !