## Slide 1: Discussion on NR PC5 communications
Samsung, LG Electronics
3GPP SA WG 2 Meeting#133
13 – 17 May, Reno, NV, USA
Agenda item : 6.6
Work Item / Release : eV2XARC / Rel-16
S2-1905578

## Slide 2: Table of Contents
Working assumption on relation of V2X applications and V2X services
Working assumption on relation of V2X services and QoS Flows
Working assumption on granularity of PC5 unicast link
Conclusions and proposals

## Slide 3: 1. Relation of V2X applications and V2X services
V2X service is defined in clause 3.1 of TS 23.287
  V2X service: A service, offered by V2X applications and V2X Application Servers. It may include message or other data delivery, as defined in TS 22.185 [2] and TS 22.186 [3]
Relation of V2X applications and V2X services.
  One V2X application can have more than one V2X service.
  One V2X service can be associated with more than one V2X application.
  V2X applications : V2X services = N : M mapping, e.g.,
V2X application#1
V2X service#1
V2X service#2
V2X service#3
V2X application#2
V2X service#1
V2X service#4
One V2X application can have more than one V2X service.
One V2X service can be associated with more than one V2X application.

## Slide 4: 2. Relation of V2X services and PC5 QoS Flows
Each V2X packet is associated with one V2X service.
The V2X layer determines QoS requirements (e.g. PQI plus other QoS parameters) and a PFI for the V2X packet.
Different V2X packets associated to the same V2X service may require different QoS treatment. Consequently, each V2X packet can be sent to the AS layer with a different PFI, e.g.,
V2X Service#1
QoS Requirements#1
PQI#1
PQI#2
PQI#3
QoS Requirements#2
QoS Requirements#3
V2X Service#2
QoS Requirements#4
PQI#4
PQI#5
QoS Requirements#5
V2X Application#1
Application layer provides QoS Requirements.
V2X layer determines QoS requirements and a PFI for the V2X packet.
PFI#1
PFI#2
PFI#3
PFI#4
PFI#5

## Slide 5: 3. Granularity of PC5 unicast link
A PC5 unicast link is established between UE A and UE B.
  One PC5 unicast link can support more than one PC5 QoS Flow.
  One PC5 unicast link can support more than one V2X service.
  The granularity of the PC5 unicast link is the same as the pair of Application layer ID of UE A and Application layer ID of UE B.
    It is up to application layer implementation whether
      Case 1) one Application layer ID is associated with one V2X application,
      Case 2) one Application layer ID is associated with more than one V2X application, or
      Case 3) one Application layer ID is used for all V2X applications in the UE.
[Case 3]
[Case 1 or Case 2]

## Slide 6: 4. Conclusions and proposals
Proposal 1: endorse the working assumptions for PC5 communication over NR:
Working Assumption 1
  The relation of V2X applications and V2X services can be N-to-M mapping.
Working Assumption 2
  Different V2X packets associated to the same V2X service may require different QoS treatment. Consequently, each V2X packet can be sent to the SDAP layer with a different PFI.
Working Assumption 3
  One PC5 unicast link can support more than one PC5 QoS Flow.
  One PC5 unicast link can support more than one V2X service.
  The granularity of the PC5 unicast link is the same as the pair of UE A’s Application layer ID and UE B’s Application layer ID.
Proposal 2: add the following
NOTE: The usage of application layer identifier, e.g. one Application layer ID is associated with one V2X application, one Application layer ID is associated with more than one V2X application, or one Application layer ID is used for all V2X applications in the UE, is up to application layer implementation.
Proposal 3: agree the companion pCRs in S2-1905579, S2-1905135, S2-1905581.

## Slide 7: Thank you