## Slide 1: Discussion on Smarter User Plane
Cisco, Softbank

## Slide 2: Network Automation Goals
Extend N3/N9 QoS/Slice intent to transport
  Seamlessly integrate 5GC slices and transport slices
  Neutral host and Transport provider Multi Tenancy
Location and Identity Abstraction
Remote UPF programming
Inter AN, UPF and DN meta data exchange

## Slide 3: Current QOS Based Behavior
gNB
UPF
Slice B
Slice A
Transport
Node
Transport
Node
Slice B
Slice A
Slice B
Slice A
gNB (or UPF, CU, or DU) maps 5QI to outer DSCP field of transport packet
Each Transport Node handles individual packet hoop by hop to fulfil defined QoS on specific node

## Slide 4: Desired End to End Behavior
gNB
UPF
Transport
Node
Transport
Node
Slice B
Slice A
gNB (or UPF, CU, or DU) maps 5QI to outer DSCP and defines end to end transport behavior based on 5QI and Slice information
Transport nodes behaves based on gNB definition

## Slide 5: Relationship Between User Plane and Transport
gNB
UPF
UPF
N3
N9
Far Edge
Edge
DC
xHaul
VPN
Behavioral Mapping
Behavioral Mapping

## Slide 6: N3/N9 and transport QoS mapping
gNB
UPF
UPF
N3 Slice A’’ (DSCP)
N9 Slice A’’ (DSCP)
Far Edge
DC
On-Path Queues (DSCP)
On-Path Queues (DSCP)
DSCP Mapping
DSCP Mapping
Edge
N3 Slice A’ (DSCP)
N9 Slice A’ (DSCP)
N3 Slice B (QFI)
N3 Slice A (QFI)
QFI Mapping
RRH

## Slide 7: RAN-Transport Interaction
In current architecture there is very limited interaction between RAN and Transport network
  It is limited to outer IP header of the packet.
  Transport network can use only IP addressing concept and QOS concept in DCSP field to alter behavior
  For upstream traffic destination IP address and QOS mapping can define traffic separation on transport network
  For downstream traffic only delineation of different SLA required only QOS mapping of 5QI to DSCP can be used
Such approach is obviously insufficient for network slicing concept
  UPF and CU needs more control of transport network behavior
  It needs to include transport network slice selection
  UPF and gNB needs to be capable of defining transport network behavior using different behavioral models
  RAN network needs to be capable to define end to end transport behavior, not only hop by hop transport behavior
This behavior needs to be consistently defined across all dataplane interfaces where network slicing is relevant

## Slide 8: Relationship Between User Plane and Transport
Transport Management System needs to map the 5G System features and SLA to routing and switching. For example:
  Concept of a slice at a transport level is a configuration that maps VLAN, IP addresses or header markings to a routing and QoS profile that meets the SLA
    The UPF has the slice information. Can it not convey this to the N6, N9, F1 and N3 transport?
    With virtualization being used across different domains – instead of having disparate domains – can the 3GPP domain convey intent of packets towards the other domains?
  URLLC requires low latency and high availability. The transport for F1, N3, N9 and N6 does not know the PDN is a URLLC PDN unless there is local configuration on the transport entities.
    The UPF has the URLLC information. Can it not convey this to the N6, N9 and N3 transport?
    Local Configuration on transport entities can be cumbersome and providing the intent of the packet within the packet to program and make intelligent routing decisions could be useful
  Mobility requires the efficient routing of user plane packets
  As more use cases require flexibility of user plane and ability to steer packets mid-path – tunneling adds inflexibility and requires extensive pre-knowledge of use cases and packet path

## Slide 9: N3/N9 and transport QoS mapping
Limited DSCP and ToS Bits compared to number of slices and individual QCI or QFI per slice
Eventually – all slices and flows could be mapped to same DSCP / ToS – thus limiting options and service differentiation
L1
L2
IP
GTP-U
Access Network Protocol Layers
Access Network Protocol Layers
L1
L2
UDP / IP
GTP-U
Relay
PDU Layer
L1
L2
UDP / IP
GTP-U
Relay
L1
L2
IP
L1
L2
IP
GTP-U
UE
(R)AN
UPF UL-CL / Branching Point
PSA
PDU Layer
Application
N3
N9
N6
No packet information and transport mapping
QFI  DSCP / ToS Bits
(Static Pre-Provisioned Mapping)
QFI  DSCP / ToS Bits
(Static Pre-Provisioned Mapping)

## Slide 10: Example Header Extension - Uplink
Internet
gNB
C1
UPF2
UE
IPv6 Hdr
SA = G::, DA = S1::
SR Hdr
(U2::, C1::) SL=2
Payload
IPv6 Hdr
SA = A::, DA = Z::
IPv6 Hdr
SA = A::, DA = Z::
Payload
IPv6 Hdr
SA = A::, DA = Z::
Payload
T.Encaps.Red
<S1::, C1::, U2::>
End.DT with PSP
IPv6 Hdr
SA = G::, DA = U2::
Payload
IPv6 Hdr
SA = A::, DA = Z::
S1
IPv6 Hdr
SA = G::, DA = C1::
SR Hdr
(U2::, C1::) SL=1
Payload
IPv6 Hdr
SA = A::, DA = Z::
N6
N3
N3
N3

## Slide 11: Example Header Extension - Downlink
IPv6 Hdr
SA = U2::, DA = C1::
SR Hdr
(G::, S1::) SL=2
Payload
IPv6 Hdr
SA = Z::, DA = A::
IPv6 Hdr
SA = Z::, DA = A::
Payload
IPv6 Hdr
SA = A::, DA = Z::
Payload
T.Encaps.Red
<C1::, S1::, G::>
End.DX with PSP
IPv6 Hdr
SA = U2::, DA = G::
Payload
IPv6 Hdr
SA = Z::, DA = A::
IPv6 Hdr
SA = U2::, DA = S1::
SR Hdr
(G::, S1::) SL=1
Payload
IPv6 Hdr
SA = Z::, DA = A::
Internet
gNB
C1
UPF2
UE
S1
N6
N3
N3
N3

## Slide 12: IP Address Agnostic Networking
The IP Address assigned to a PDU determines the path of the packet
  Could the path be determined by the identity of the PDU rather than the IP Address?
  Can the UPF forward packets between UE’s and between UE and DN using the identity rather than the IP addresses?
  Can the packet itself carry some of the information rather than individually configure intermediate nodes / domains?
  The network today carries pre-defined state and introduces inflexibility due to specific IP address based routing as the only option

## Slide 13: Conveying Meta Data
UPF Chaining using N9 is reliant on each UPF performing PDR and FAR
  PDR is reliant on PCC rules that include Layer 7 DPI inspection
  Heuristic detection can take multiple packets before the rule is matched
  Accounting across UPF and distributed network topology fragments quota
  With UPF chaining, the same packet will have to go through packet rule matching multiple times causing compute inefficiency
  Communicating meta data about a flow in the N9 header will significantly simplify distributed UPF application based policy and charging
Traffic Engineering during sunny day scenarios or steering during failure scenarios requires reprogramming today or pre-programming
  Carrying meta-data can provide intent of the packet towards the domains – transport, compute – thus improving efficiencies and service capabilities
When routing or traffic failures occur, rerouting of packets requires intervention or inefficient load balancing as the packet itself does not carry useful information

## Slide 14: Meta Data Transfer
(R)AN
UPF
UPF
N3
N9 Classification Result
N3 UE Location
N9 UE Location
N6 UE Location
DN

## Slide 15: Conveying Meta Data to DN
A UPF at the edge may need to convey application meta data to the DN
Application domain today is becoming a lot more aware of the packet domain and capabilities
  Significant out of band signaling and synchronization required to carry identity, intent and capabilities
  Application can benefit in receiving additional packet information when possible and enabled