## Slide 1: Discussion on UPF service area for User Plane CIoT 5GS Optimisation
Sunghoon Kim
Samsung

## Slide 2: UPF Service Area?
TS 23.501, Definition
UPF Service Area: An area consisting of one or more TA(s) within which PDU Session associated with the UPF can be served by (R)AN nodes via a N3 interface between the (R)AN and the UPF without need to add a new UPF in between or to remove/re-allocate the UPF.
UPF Service Area Handling (5.6.11 of TS 23.501)
If UE moves out of the UPF Service Area, SMF need to determine whether add I-UPF or remove/re-allocate UPF
SMF may subscribe Location Reporting for Area of Interest based on UPF Service Area, then the SMF will be notified from the AMF which detects UE presence in Area of Interest.

## Slide 3: User Plane CIoT 5GS Optimisation
User Plane CIoT 5GS Optimisation enables transfer of user plane data from CM-IDLE without the need for using the Service Request procedure to establish Access Stratum (AS) context in NG-RAN and UE.
If UE moves to other NG-RAN, context fetch is performed between NG-RANs, and then N2 Path Switch procedure is triggered.
The UE may include early uplink data in the Connection Resume.
NG-RAN maintains the N3 tunnel endpoint information while a UE is in CM-IDLE with Suspend. UPF is instructed to remove DL N3 Tunnel Info of AN during Connection Suspend procedure, while UPF keeps UL N3 Tunnel Info (i.e. UPF accepts and forwards UL data).
NG-RAN can send UL data to the UPF before performing path switch procedure if UL data received by EDT from the UE.
Combination of EDT and sending UL data before path switch procedure brings benefit for
Power saving of UE: No need for DRB establishment, UE can be moved to CM-IDLE immediately after EDT in case of RAI: Single Uplink Only
Signalling efficient in Core Network: No need to activate User Plane (DL N3 Tunnel) which reduces the number of signalling = 6 (RAN – AMF, AMF – SMF, SMF – UPF) in case of RAI: Single Uplink Only

## Slide 4: Issue
NG-RAN has no idea about UPF Service Area
If UE moves out of UPF Service Area, NG-RAN cannot send MO EDT to the UPF of which UL N3 tunnel info stored in the UE context, by definition of UPF Service Area
If UE sends data with EDT/UP CIoT 5GS Optimisation on NG-RAN#2, NG-RAN#2 cannot send
the data (by EDT) to the UPF#1 because it is out of UPF service Area of UPF#1.
UPF#1
UPF#2
UL N3 Tunnel
! Out of UPF#1 serving Area
NG-RAN#1
NG-RAN#2
UL N3 Tunnel
UPF#1’s Service Area
UPF#2’s Service Area
Xn

## Slide 5: Possible Solutions
Principle: User Plane CIoT 5GS Optimization has been developed for the sake of power and signaling efficiency. Therefore, the solution should not bring significant cost of power or signaling which diminishes overall benefit of the feature.
Alternative 1: NG-RAN aware of UPF Service Area
  SMF provides UPF Service Area to the NG-RAN within N2 SM Information. If the NG-RAN determines that current location of the UE is out of UPF Service Area, the NG-RAN does NOT send UL data (received by EDT) before completing N2 Path Switch procedure. After N3 Tunnel activation, the NG-RAN sends the UL data.
  Evaluation: New N2 SM information and logic are required on NG-RAN. But it also resolves the case for EDT with RRC-Inactive (if UE moves out of UPF service area while CM-Connected/RRC-Inactive)
Alternative 2: Area of Interest based NG-RAN operation
  SMF subscribes Area of Interest to the AMF based on UPF service area, and the AMF requests Location Reporting control for the Area of Interest to the NG-RAN. When UE sends UL EDT, The NG-RAN determines whether UE is out of Area of Interest based on the location reporting control, and if the UE is out of the Area of Interest, the NG-RAN performs N2 Path Switch procedure before sending UL data.
  Evaluation: Location Reporting for the Area of Interest is not only the case for UPF service area. It can be triggered by the request from PCF (e.g., UE presence) or LADN. Therefore, the NG-RAN may unnecessarily determine not to send the UL data received by EDT before N2 Path Switch.
  NOTE: As specified in 5.6.11 of TS 23.501, SMF may determine an Area of Interest based on UPF service Area, and subscribes location reporting. Based on location notification, the SMF determines how to deal with the PDU Session, e.g. reallocate UPF.

## Slide 6: Possible Solutions
Alternative 3: new NG-RAN forwards UL data to old NG-RAN
  New NG-RAN forwards UL data (received by EDT) to the old NG-RAN, then old NG-RAN sends the data to the UPF where UL N3 Tunnel information addresses.
  Evaluation: It has impact on both User Plane and Control plane over Xn interface. (Need to setup forwarding tunnel, and forward data over user plane) From signaling point of view, too much effort for the benefit.
Alternative 4: Range of GTP Tunnel information configuration at NG-RAN
  If NG-RAN has been configured the range of GTP tunnel information which the NG-RAN can make user plane connectivity, the NG-RAN can determine whether the UL N3 Tunnel information (fetched from the old NG-RAN) is valid for user plane connectivity. If it is not valid, NG-RAN performs path switch procedure first before sending UL data (received by EDT)
  OAM system configures NG-RAN about available GTP Tunnel Information range with regarding UPF Service Area.
  NOTE: GTP Tunnel information is composed of UDP port, IP address, and TEID.
  Evaluation: It has no impact on CN. However, it requires configuration effort by OAM system. OAM system has to retrieves relevant GTP tunnel information which is available for user plane connectivity between NG-RAN nodes and UPFs, and needs to configure to NG-RAN nodes. It may bring multi-vendor deployment issue as it needs to ensure every NG-RAN (supporting EDT with UP Optimisation) should support the configuration and related operation (determining whether user plane connectivity is valid)

## Slide 7: Proposal
It is proposed to move forward with alternative 1, as it provides standardized way with below two main changes (which seems less impact than other alternatives)
  Adding one more IE in N2 SM context from SMF to NG-RAN
  NG-RAN needs to determine the current location of the UE is inside of UPF service area.
Related CR for TS 23.501 has been submitted (S2-1907729)
CR against TS 23.502 for EDT support should capture this proposed change