## Slide 1: Candidate way forward option to delegated discovery
Huawei
SA WG2 Meeting #134 S2-1908045
Sapporo, Japan, 24 - 28 June 2019

## Slide 2: Option A (Original Working Agreement)
SMF selection:
1. AMF does not use delegated discovery in HR roaming, or if the PLMN is configured to support ETSUN.
PCF selection:
2. In the roaming case, delegated discovery and selection is not used for UE policy association establishment procedure.

## Slide 3: Option B (Huawei)
SMF selection:
AMF sends the service request to the SCP with all the related selected parameters. The SCP use those parameter to do the SMF selection.
If one SMF matched those parameter, the request is forwarded to that SMF.
If SMF can not be found,
  The AMF discover and select the H-SMF from the interaction with NRF.
  The AMF send the request with (H-SMF)+ selection parameter(without DNN) to SCP.
  The SCP select the V/I-SMF and forward the request to the V/I-SMF
  The V/I-SMF send the request to the received H-SMF.
PCF selection
Always the AM association established first.
UE policy association establishment :
  The AMF select the H-PCF from the interaction with NRF.
  The AMF send the SCP the V/H-PCF ID for the association establishment.

## Slide 4
AMF
1. Request (selection and discovery parameters for H-SMF)
7. Request
13. Response
3. Error Response
2. Discovery of SMF
Option B----SMF selection
SCP
V-SMF
12. Request
14. Response
SCP
H-SMF
8. Request
10. Request
11. Response
Y
NRF
4. H-SMF selection Req
5. H-SMF selection
9. Request
7a. Discovery of V-SMF

## Slide 5: Proposed way forward
Option B is compromised proposal from the offline discussion. It can be considered as way forward.