## Slide 1: Discussion on the UP Establishment on the second access of a MA PDU Session in an ATSSS-incapable VPLMN
MediaTek Inc.
3GPP TSG SA2#136AH S2-2000826
Incheon, Korea – January 13th – 17th, 2020 Agenda Item 7.3

## Slide 2: Scenario 1 Follow CT 1 specs
An ATSSS-Capable UE registers
  via Non-3GPP access in HPLMN which is ATSSS-capable
  via 3GPP access in VPLMN which is not ATSSS-capable
This UE has established a MA PDU Session with UP resources in Non-3GPP access in HPLMN
This UE initiates a PDU Session Establishment procedure with MA PDU Request + Same PSI to VPLMN to establish the UP resources on the second access (i.e. 3GPP access) in VPLMN

## Slide 3: Scenario 1: Description of the Network Operation
Since VPLMN is an ATSSS-Incapable network,
  AMF2 will interpret the UE’s MA PDU Request as an Initial Request and select SMF2 which does not support ATSSS.
SMF2 may select SMF3 which does not support ATSSS in HPLMN
UE receives the PDU Session Establishment accept for a SA PDU Session

## Slide 4: Scenario 1: Problem
Network cannot detect that the PSI sent by the UE is already used by the MA PDU Session in HPLMN
The MA PDU Session context with same PSI is replaced by SA PDU Session with same PSI in UDM in HPLMN

## Slide 5: Scenario 1: Solution
UE detects the PSI is used by an SA PDU Session but originally the PSI is used by a MA PDU Session
  UE locally releases the MA PDU Session in HPLMN to align with network
Benefit
  The network does not need to trigger any signaling with the UE
  No change in the network
Disadvantage
  The released MA PDU Session may have ongoing services, the UE may need to initiate the PDU Session establishment procedure to renew the services

## Slide 6: Scenario 2 Follow SA2 specs
An ATSSS-Capable UE registers Non-3GPP access in HPLMN which is ATSSS-capable and registers 3GPP access in VPLMN which is an ATSSS-Incapable network
This UE has established a MA PDU Session which has the UP resources built on Non-3GPP access in HPLMN
This UE initiates a PDU Session Establishment procedure with MA PDU Request indication + “existing PDU session” request type + Same PSI to VPLMN to establish the UP resources on the second access (i.e. 3GPP access) in VPLMN

## Slide 7: Scenario 2: Problem
AMF2 will interpret the UE’s MA PDU Request as an initial request but since this Request type is set to “existing PDU Session”, the AMF-2 will detect this does not match with initial request
Or SMF2 can detect this conflict for initial request against “existing PDU Session”
No proper cause codes are used by network

## Slide 8: Scenario 2: Solution
A new cause code or reused cause code are needed by the AMF or by the SMF to indicate to the UE
Enhance AMF
  AMF-2 reject the UE’s MA PDU Session request with a proper error cause to the UE
    #90: Payload was not forwarded
Enhance SMF
  AMF-2 processes as it is an initial request but SMF-2 rejects the UE’s MA PDU Session with a proper error cause to the UE
    #54: PDU Session does not exist
Benefit
  The network can use proper cause code to indicate the UE that ATSSS is not supported
Disadvantage
  A new cause code is added

## Slide 9: If Solution for Scenario 1 is selected
Impacted SA2 spec
  Clause 5.32.2 of TS 23.501: Multi Access PDU Sessions
    Re-word the description which includes of the MA PDU Request indication…
  Clause 4.22.2 of TS 23.502: Non-Roaming and Roaming with Local Breakout
    Re-word the description which includes of the MA PDU Request indication and the Request Type = “initial request”…
  Clause 4.22.7 of TS 23.502: Adding/ Re-activating/ De-activating User-Plane Resources
    Re-word the description which includes of the MA PDU Request indication and the Request Type = “existing PDU Session”…

## Slide 10: If Solution for Scenario 2 is selected
Impacted CT 1 spec of TS 24.501
  Clause 9.11.3.47 Request Type
    Remove the “MA PDU request” from Request type IE
  Add new clause 9.11.3.xx MA PDU Request Indication IE
    Define a new IE for MA PDU Request
  Clause 8.2.10 UL NAS transport
    Include the new IE in the UL NAS transport message
  Clause 5.4.5.2 UE initiated NAS transport procedure
    Consider the new IE and remove the description including of the MA PDU Request
  Clause 6.4.1 UE-requested PDU session establishment procedure
    Consider the new IE and remove the description including of the MA PDU Request

## Slide 11: Way Forward
Solution for Scenario-1 (Follow CT 1 spec)
  Refer to Option 3 and Option 4 in ZTE’s DP
Solution for Scenario-2 (Follow SA2 spec)
  Refer to Option 2 in ZTE’s DP
It proposes
  Option 3 or Option 4 are preferred solutions – align with CT 1 spec