## Slide 1: Vertical_LAN TSC drafting session
TSC drafting session
Devaki Chandramouli
November 19, 2019

## Slide 2
TSCAI related papers
7.7.2 | S2-1911129 | CR | Approval | 23.503 CR0325R1 (Rel-16, 'F'): QoS mapping for uplink TSC communication | Vivo | Rel-16 | Vertical_LAN | Revision of S2-1909078 from S2#135
7.7.2 | S2-1911704 | DISCUSSION | Decision | TSCAI for aggregated TSN Streams. | Ericsson | Rel-16 | Vertical_LAN | Revised to S2-1911929
7.7.2 | S2-1911929 | DISCUSSION | Decision | TSCAI for aggregated TSN Streams. | Ericsson | Rel-16 | Vertical_LAN | Revision of S2-1911704
7.7.2 | S2-1911705 | CR | Approval | 23.501 CR1981 (Rel-16, 'F'): Applying Per-Stream Filtering and Policing | Ericsson | Rel-16 | Vertical_LAN | 

## Slide 3: AF responsibilities
Determines (BAT) Burst Arrival Time (considering UE-DS-TT residence time, CN-PDB) in reference to TSN GM used for IEEE 802.1Qci gate operation
Determines Periodicity in reference to TSN GM
Determines Delay requirement in reference to TSN GM
Determines Maximum Burst Size
AF forwards TSN QoS container with {BAT, Periodicity, Maximum Burst Size, flow direction}, Delay requirement and priority to PCF
AF may aggregate multiple TSN streams if they have same periodicity and traffic class; in this case AF creates a single TSN QoS container for the aggregated TSN streams
Editor’s note: whether the conversion for TSN GM to 5G GM at the AF is FFS.

## Slide 4: PCF Responsibilities
Forward TSN QoS container as-is to SMF
Determine the 5QI (with associated PDB) for the 5G QoS flow as specified in TS 23.501/3
Editor’s note: need for VLAN header and priority to determine 5QI is FFS.

## Slide 5: SMF responsibilities
Convert the following parameters in reference to 5G GM to create the TSCAI
  Burst Arrival Time
  Periodicity
Send TSCAI (in reference to 5G GM) to 5G AN.
One TSCAI is created per TSN QoS container. It is assumed we have one TSCAI per QoS flow.