## Slide 1: FS_IIoT Show of hands questions
Nokia (Rapporteur)

## Slide 2: Key Issue #1 Uplink Time Synchronization
Background
  There are 4 methods documented as part of solution #1 to support BMCA for Time Synchronization. Need to pick one Method as way forward.
  Method 1 – TSN AF determines the port role, announce message is forwarded over CP (C-plane based).
  Method 2 – NW-TT determines port roles; DS-TT forwards all announce messages, U-plane.
  Method 3 – NW-TT determines port roles; If message Priority Vector is better than the current Port Priority Vector, DS-TT forwards announce, U-plane
  Method 4 - NW-TT determines port roles; NW-TT forwards announce message on behalf of DS-TT, U-plane.
Way forward: <>

## Slide 3: Key Issue #2 UE-UE TSC Communication
Background
  Item 1: Varying views on support for UE-UE communication for IEEE TSN bridge with or without any pre-configuration.
Questions:
  Options for item 1:
    Option 1: Allow UE-UE communication, 5GS acting as IEEE TSN bridge supported only if they are configured as part of 5G VN group.
    Option 2: Allow UE-UE communication considering AF request for QoS, as long as they are within the same 5GS acting as IEEE TSN Bridge for ETH PDU Sessions.
    Option 3: Allow both options – option 1 & 2.
  Way forward: < >

## Slide 4: Key Issue #2 UE-UE TSC Communication
Background
  Item 2: Varying views on how the local switching within UPF should be controlled.
Questions:
  Options for Item 2:
    Option 1: Local switching within UPF is autonomously determined based on MAC learning and IP routing* knowledge. When local switching is performed, QoS updated considering AF request for listeners and talkers.
    Option 2: Local switching within UPF is controlled via N4 (FAR/PDR) rules. When local switching is performed, QoS updated considering AF request for listeners and talkers.
    Option 3: Allow both options
    Way forward: < >
* in case of IP@, it is about knowing target UE’s IP prefix for routing

## Slide 5: Key Issue #3A Support for deterministic services
Background
  Support for H&F for ETH (non-IEEE TSN) PDU Sessions.
  Support for H&F for IP PDU Sessions.
Questions:
  Should we support H&F for ETH (non-IEEE TSN) PDU Sessions? (YES/NO)
  Options to support H&F for ETH (non-IEEE TSN):
    Option 1: With Rel-16 Qbv parameters
    Option 2: With TSCAI parameters
    Option 3: Option 1 or Option 2 is fine.
  Should we support H&F for IP (non-IEEE TSN) PDU Sessions? (YES/NO)
  Options to support H&F for IP (non-IEEE TSN):
    Option 1: With Rel-16 Qbv parameters
    Option 2: With TSCAI parameters
    Option 3: Option 1 or Option 2
  Way forward: < >

## Slide 6: Key Issue #3B Exposure of TSC services Exposure of Time Synchronization
Background
  Conclusion has the following:
  Editor's note: whether there is a need to include validity time for AF time sync request is FFS. Also, how to support validity time is FFS.
  Options
  Option 1: AF assumed to activate and deactivate requests (thus maintain validity period accordingly).
  Option 2: AF provides validity period for the request, 5GS maintains the validity period (i.e. new activate requests are not allowed when the validity period expires) and activated time synchronization are deactivated by the deactivate request.