## Slide 1: FS_IIoT Show of hands questions
Nokia (Rapporteur)

## Slide 2: Key Issue #1 Uplink Time Synchronization
Background
  There are 4 methods documented as part of solution #1 to support BMCA for Time Synchronization. Need to pick one Method as way forward.
  Method 1 – TSN AF determines the port role, announce message is forwarded over CP (C-plane based).
  Method 2 – NW-TT determines port roles; DS-TT forwards all announce messages, Mix of U-plane and C-Plane.
  Method 3 – NW-TT determines port roles; If message Priority Vector is better than the current Port Priority Vector, DS-TT forwards announce, U-plane
  Method 4 - NW-TT determines port roles; NW-TT forwards announce message on behalf of DS-TT, U-plane.

## Slide 3: Key Issue #1 Uplink Time Synchronization
Questions:
  Options for BMCA:
    Option 1: BMCA is C-plane based; Ingress port forwards the Announce messages to TSN AF (or NEF) for BMCA procedure which determines the PTP port states, TSN AF (or NEF) informs the DS-TT and/or NW-TT port states if needed.
    Option 2: BMCA is U-plane based; Ingress port forwards the Announce messages to NW-TT for BMCA procedure which determines the PTP port states, and informs TSN AF (or NEF) on the BMCA result if needed.
    Way forward: < >

## Slide 4: Key Issue #2 UE-UE TSC Communication
Background
  Item 1: Varying views on support for UE-UE communication for IEEE TSN bridge with or without any pre-configuration.
Questions:
  Options for item 1:
    Option 1: Allow UE-UE communication, 5GS acting as IEEE TSN bridge supported only if they are allowed as configured for e.g., same member of a group, same DNN/S-NSSAI.
    Option 2: Allow UE-UE communication considering AF request for QoS, as long as they are within the same 5GS acting as IEEE TSN Bridge for ETH PDU Sessions.
    Option 3: Allow both options – option 1 & 2.
  Way forward: < >

## Slide 5: Key Issue #2 UE-UE TSC Communication
Background
  Item 2: Varying views on how the local switching within UPF should be controlled.
Questions:
  Options for Item 2:
    Option 1: Local switching within UPF is autonomously determined based on MAC learning or controlled by CNC.
    Option 2: Local switching within UPF is controlled via N4 (FAR/PDR) rules.
    Option 3: Allow both option 1 or 2
    Option 4: When local switching is performed, QoS updated by SMF/PCF considering AF request respectively for listeners and talkers.
    Way forward: < >
* in case of IP@, it is about knowing target UE’s IP prefix for routing

## Slide 6: Key Issue #3A Support for deterministic services
Background:
  Key issue 3A “focuses on enhancing the NEF framework”; all areas for study of KI#3A only deal with the NEF-AF (TR 23.700-20 clause 5.3.2)
  There is no explicit SA1 requirement about a need for hold and forward functionality for VIAPA services.
Proposed way forward:
  Ask question below but confirm with SA1 if there is a requirement before documenting any conclusion in the TR.
Question 1:
  Should it be possible for the NEF to derive Rel-16 Qbv parameters based on QoS information provided by VIAPA applications?
  Note: Rel-16 hold and forward functionality in DS-TT and NW-TT is assumed to be reused as-is.
Question2: burst spread is used for TSC scheduling
  Option 1: Burst Spread can be provided by AF to SMF via NEF/PCF
  Option 2: Burst Spread can be detected by UPF and provided to SMF
  Option 3: Support both

## Slide 7: Key Issue #3B Exposure of TSC services Exposure of Time Synchronization
Background
  Conclusion has the following:
  Editor's note: whether there is a need to include validity time for AF time sync request is FFS. Also, how to support validity time is FFS.
  Options
  Option 1: AF assumed to activate and deactivate requests (thus maintain validity period accordingly).
  Option 2: AF provides validity period for the request, 5GS maintains the validity period (i.e. new activate requests are not allowed when the validity period expires) and activated time synchronization are deactivated by the deactivate request.