## Slide 1
Source: OPPO
Title: Discussion on paging cause way forward
Document for: Discussion and Agreement
Agenda Item: 8.10
3GPP TSG SA WG2#142-e meeting
16th – 20th November 2020
Tdoc 2008781

## Slide 2
How to use if Multiple Paging Cause adopted (two opt.)
It has been excluded by interim conclusion
There can be a misalignment (unexpected behavior) because UE does not know which paging cause(s) the PLMN supports (NOTE-1)
Opt.1
Answer paging based on user selection
Opt.2
Answer paging based on UE configuration
MMI used to ask user whether to respond every time the paging arrives
User presets whether to respond the paging per each paging cause
Opt.2 Mandate the paging cause(s) PLMN shall support?
No possibility to mandate each PLMN to realize it
Opt.1 Let UE know which paging causes a PLMN supports?
Different UE may have different behavior for the same paging cause
UE behavior will not be unified.
No benefit for this case? (e.g. how to satisfy both handset vendor and MNO)
Regulate for which paging cause the UE should respond
5GS does not support it. Also there is no difference compared to “important service” indication in essence
NOTE-1: Each PLMN may support different paging cause(s) in Rel.17 (and further release), which will lead to a misalignment.
For example, user presets UE should respond to paging cause=voice, SMS, but the registered PLMN only support paging cause=voice that means the PLMN never add “paging cause=SMS” even when the DL data is SMS. As a result, the UE will not know which paging is for SMS and thus cannot respond as user request.
How
To
Resolve ?
Two
Opt.
Two
Opt.
No possibility for UE to aware it

## Slide 3
Based on the discussion in previous slide, we don’t see any reasonable way for UE implementation when multiple paging cause is adopted. Thus propose:
- Multiple paging cause is not recommended to normative work;
- One paging cause is good enough. We prefer to use “important service indication” to give more flexibility.