## Slide 1: Pre-SA2#143E 5MBS Coordination Call
LiMeng
Mengli.Raymond@Huawei.com
2021.01.28

## Slide 2: Agenda
Way forward for addressing the open issues in SID phase;
  Including the summary of moderated email discussion.
  Documents if any.
Skeleton of the new TS for 5MBS;
Discuss the draft documents provided by the major contributors;
Other inputs;
Meeting Bridge (Microsoft Teams)
  Click here to join the meeting

## Slide 3: Way forward for addressing the open issues in SID phase (1/2)
Way forward based on email discussion:
  UP-based join is not supported in Release 17.
  MB-SMF is assumed to allocate Area session identifier.
  Determine the details of TMGI and its relationship with SNPN in the normative phase.
  The interface for PSA receiving MBS data: Support N9 interface only, since N9 could support multicast and unicast.
  Address the AS-based authorization in the normative phase.
  Use “MBSF+MBTF” terminology.
  ETSUN: no specific issue & unclear requirement.
  DDoS attack: stage 3 work.
Open issues include:
  Roaming scenario.
    LBO and HR (see next slides)
  SMF finding MB-SMF.
    UDM/NEF/PCF/NRF (see next slides)
    Seems related to roaming scenario.

## Slide 4: Way forward for addressing the open issues in SID phase (2/2)
Support of Roaming scenario:
  HR:
    Resolvable but Scenario is unclear.
  LBO:
    Most parts are the same as non-roaming case, the only issue is, how to let SMF find the MB-SMF – See the right figure.
SMF finding MB-SMF
UE
SMF
UDM (for MB-SMF)
UDM (for authorization)
Join
May have two UDMs
NEF (for MB-SMF)
Currently no similar functionality in NEF
PCF (for MB-SMF)
MB-SMF ID is not policy info
NRF (for MB-SMF)
MB-SMF ID is not a static info
UDR
UDR
UDR
How to find MB-SMF?
UDM option
NEF option
PCF option
NRF option

## Slide 5: Work Plan skeleton
Clause | Clause title | Major contribution (and volunteer contributions are provided by)
4 | General Concept | 
4.1 | Principles of multicast and Broadcast communication | ZTE (CATT)
4.2 | Definition of Service levels | Samsung
5 | Architecture model | --
5.1 | General architecture | Qualcomm (vivo)
5.2 | Architecture for Interworking with EPS | Qualcomm
5.3 | Reference point and Functional entities | --
5.3.1 | Reference point | Vivo
5.3.2 | Functional entities | Vivo
5.4 | MB service provisioning | Huawei
6 | Functionalities and features | --
6.1 | Authorization to MBS service | --
6.1.1 | Authorization to the service for Multicast | Vivo
6.2 | Local MBS service | Ericsson (Huawei)
6.3 | Mobility support of MBS service | ZTE (CATT, OPPO)
6.4? | Subscription to Multicast and Broadcast services | --
6.4.1? | Subscription to Multicast services | 
6.4 | Identifiers | Tencent
6.5 | QoS Handling for Multicast and Broadcast services | CATT,
6.6 | User plane Management | Huawei
6.7 | Interworking with MBMS over E-UTRAN | Huawei
6.8 | MBS Session and Service Context | --
6.8.1 | MBS Session Context | 
6.8.2 | MBS Service Context | 
Clause | Clause title | Major contribution (and volunteer contributions are provided by)
7 | MBS procedures | --
7.0 | Common procedure for Multicast and Broadcast | 
7.0.1 | Configuration for MBS | Ericsson (vivo)
7.1 | MBS procedures for multicast Session | --
7.1.1 | MBS join and Session Establishment procedure | Qualcomm (vivo, CATT, HW)
7.1.2 | MBS leave procedure and Session Release | Vivo
7.1.3 | MBS session start(activation)/stop(deactivation)/update procedure | Samsung (vivo)
7.1.4 | UE authorization procedure for MBS join | Juniper (vivo)
7.1.5 | Mobility Procedures | Huawei
7.1.6 | Support of Local multicast service with/without the location-dependent content. | Huawei
7.2 | MBS procedures for broadcast Session | --
7.2.1 | MBS Session Establishment/Release/Update for broadcast. | Ericsson
7.2.2. | Support of Local broadcast service with/without the location-dependent content | Ericsson
7.3 | MBS procedures for inter System Mobility | --
7.3.1 | Same service is provided via eMBMS and 5MBS | Qualcomm
7.3.2 | Same service is not provided via eMBMS and 5MBS | Huawei
8 | Control and user plane stacks | --
8.1 | Control plane for Multicast and Broadcast services | 
8.2 | User plane for Multicast and Broadcast services | 
23.503: CATT

## Slide 6: Discuss the draft documents provided by the major contributors
Session join procedure
  Informative procedure in the TR
General architecture
MB service provisioning
Local MBS service
Mobility support of MBS service
QoS Handling
User plane Management
Procedures

## Slide 7: THANK YOU