## Slide 1: New SID proposal on architecture enhancements for 5G media services
Hui Ni
Huawei

## Slide 2: New media services emerge with challenging requirements
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area
Cloud/Edge/Split Rendering | 5 ms (i.e. UL+DL between UE and the interface to data network) | 0,1 to [1] Gbit/s supporting visual content with 4K, 8K resolution and up to120fps | 99,99 % in uplink and 99,9 % in downlink | - | Stationary or Pedestrian | Countrywide
Gaming or Interactive Data Exchanging | 10ms | 0,1 to [1] Gbit/s supporting visual content with 4K, 8K resolution and up to120fps | 99,99 % | ≤ [10] | Stationary or Pedestrian | 20 m x 10 m; in one vehicle (up to 120 km/h) and in one train (up to 500 km/h)
Consumption of VR content via tethered VR headset | [5 to 10] ms | 0,1 to [10] Gbit/s | [99,99 %] | - | Stationary or Pedestrian | -
4K/8K VoD
Cloud VR/AR
The next wave of media services: high resolution, more interactive, more immersive
Various new video-based media services are emerging: Cloud VR/AR, Cloud gaming, 4K/8K VoD, Video-based remote control, machine vision etc.
Challenging requirements: ms level end-to-end delay, high reliability (e.g. 99.99%), and up to 1Gbps bitrate in a form of huge bursts. All these lead to high capacity demand for media services.
Cloud Gaming
KPI for high data rate and low latency service (Source: 3GPP TS 22.261)
Media services dominate the traffic in the mobile network, the proportion can be over 70%.
Considering the stringent KPIs and high data rates of media services, it is meaningful to investigate how the 5G network can be enhanced to better serve media services.
Video-based remote control

## Slide 3: 3GPP activities related to media services
SA1:
New Services and Markets Technology Enablers (SMARTER) (TS 22.261)
Study on Network Controlled Interactive Services (NCIS) (TR 22.842)
Service requirements for video, imaging and audio for professional applications (VIAPA) (TS 22.263)
  SA2:
  Work item on 5G System Enhancement for Advanced Interactive Services (SP-190564) : Introduces new 5QIs to identify the requirements from SA1 NCIS
  Study on enhanced support of Industrial IoT (IIoT) (SP-190932): Addresses the deterministic requirements of SA1 VIAPA
SA4:
Study on Extended Reality (XR) in 5G (TR 26.928): XR use cases
Feasibility Study on Typical Traffic Characteristics for XR Services and other Media (SP-200054): XR traffic characteristics.
RAN WGs
RAN1: Study on XR Evaluations for NR (TR 38.838): Traffic model, evaluation methodology and KPI, performance evaluation
RAN3: Study on NR QoE (Quality of Experience) management and optimizations for diverse services (TR 38.890): Define QoE management method for services including video streaming, VR, etc.
Some sporadic studies for media/video/XR services has been discussed/under discussion in RAN/SA WGs.
A systematic study in Rel-18 will be helpful to investigate how the characteristics of media services from E2E point of view can be leveraged by the 5GS for a more efficient support.

## Slide 4: Potential issues for study
1. For real-time media services
  (1) Frame level integrated transmission
    The real-time media service are transmitted in the form of packet bursts, each burst carries one video frame.
    Frame level integrated transmission may be helpful for media service transmission, scheduling and QoS control. e.g.
      Each burst consists of multiple packets. Loss of one packet may cause all other packets of the same frame to become useless.
      Bursts have a special pattern (as shown in the figure) and the resource demand varies.
Example of XR traffic: 60fps, 16.67ms frame interval, and 1 frame with 60 IP packets
  (2) Layered QoS
    A media stream can include packets with different importance for the QoE of the service, e.g. I/P frames, base/enhancement parts, FoV(Field-of-View)/non-FoV packets.
    Layered QoS may be helpful for media service transmission, scheduling and QoS control. e.g.
      Preferred handling of important packets.
      Concentration of QoS degradation (if occurring) on less important packets.
Note: The content in this page is for information. This does not intent to limit the scope or potential solutions of this study.

## Slide 5: Potential issues for study
1. For real-time media services (cont.)
  (4) XR Multicast for capacity enhancement
    For some use cases, e.g. VR Classroom, the FoV of multiple users may include the same content, e.g. the classroom environment.
    Multicast can be considered as a tool to support partial traffic of a XR service.
    Examples enhancements could be:
    Introduce joint multicast-unicast transmission to improve the network capacity, e.g. transmit the background scene via multicast.
Source: X.Hou, etc. Novel Hybrid-Cast Approach to Reduce Bandwidth and Latency for Cloud-Based Virtual Space. ACM Trans. Multimedia Comput. Commun. Appl. 14, 3, June 2018
  (3) Uplink-downlink transmission coordination
    E2E performance (e.g. MTP delay for cloud VR) depends on uplink transmission and downlink transmission.
    Examples enhancements could be:
    Identify UL-DL packets belong to one user-server interaction.
    Uplink-downlink transmission coordination
1. Motion capture
2.Uplink transmission
5G Network
Cloud server
4.downlink transmission
3. Cloud processing
5. Display
E2E MTP delay
Note: The content in this page is for information. This does not intent to limit the scope or potential solutions of this study.

## Slide 6: Potential issues for study
2. For non real-time media services
  Application-behavior awared QoS control
    To improve the QoE of media service, the network may need to identify the application event.
    When user initially starts the VoD playback or jumping to new segment of the video, higher bandwidth is beneficial to complete the buffer re-filling ASAP to reducing the waiting time of user.
    After that, the bandwidth can be reduced to a suitable value considering the average bitrate.
    Examples of architecture enhancements are given as following:
    Awareness of playback behavior from application
    Adjust QoS policy based on playback behavior in real time.
Note: The content in this page is for information. This does not intent to limit the scope or potential solutions of this study.

## Slide 7: Potential issues for study
3. General issues
  (1) Mobility management enhancement
    The handover procedure may cause interruption in case huge frame arrives RAN during HO procedure.
    Mobility management enhancement can be considered to guarantee the QoE of media service for 5G UE.
  (2) Coordination with upper layer protocol
    To investigate potential coordination with upper layer (e.g. TCP, UDP, SRT) to improve end-to-end performance. E.g. For TCP-based media service, the re-transmission may cause long delay and slow startup of TCP window, which may be not necessary for some uncritical packet in the media traffic.
  (3) Network XQI (XR Quality Index)
    There is no network level metric directly reflecting network transmission impact (including RAN and CN) on XR user experience.
    The network XQI is possible defined to evaluate the impact of network transmission on XR user experience, and to be used for further network optimization.
Note: The content in this page is for information. This does not intent to limit the scope or potential solutions of this study.

## Slide 8: Rel-18 study proposal on architecture enhancements for 5G media services
Study the R18 architecture enhancements for media services with the following objectives:
Mobile Media Slice
(Media specific transmission enhancement)
NEF/PCF/
NWDAF
UPF
Media level semantics
Perception of media level characteristics
Media
Application server
SMF
AF
User device
RAN
Media
Application client
  1. Study architecture enhancements for real-time media service, including e.g.:
    Frame level integrated transmission
    Layered QoS
    Uplink-downlink transmission coordination
    XR Multicast for capacity enhancement
  2. Study architecture enhancements for non real-time media service, including e.g.:
    Application-behavior aware QoS control
  3. Study architecture enhancements for general media services, including e.g.:
    Mobility management enhancement
    Coordination with upper layer protocol, e.g. TCP/UDP/SRT
    Network XQI (XR Quality Index)
  4. Study the definition of network slice for mobile media
    Note: The SA2 work shall be coordinated with other WGs, e.g. RAN 1/2/3, SA3, SA4.

## Slide 9: Draft Rel-18 SID proposal for discussion

## Slide 10: Thank You!