## Slide 1: Study on Integration of satellite components in the 5G architecture Phase II
S2-2104671
Xiaomi

## Slide 2: Overview of satellite related work in 3GPP R17&R18
SA1
  Stage 1 of 5GSAT (5GSAT) (R17)
  Guidelines for Extra-territorial 5G Systems (FS_5GET)(R18)
SA2
  Study on architecture aspects for using satellite access in 5G (FS_5GSAT_ARCH) (R17)
  Integration of satellite components in the 5G architecture (5GSAT_ARCH) (R17)
RAN2
  Core part: Solutions for NR for NTN(NR_NTN_solutions-Core) (R17)
  Study on NB-IoT/eMTC support for Non-Terrestrial Network (FS_LTE_NBIOT_eMTC_NTN) (R17)

## Slide 3: Stage 1 requirements with potential architectural impacts not covered at stage 2 in R17
UE location related
  A UE supporting satellite access shall be able to provide or assist in providing its location to the 5G network. (22.261/6.3.2.3)
  A 5G system with satellite access shall be able to determine a UE's location in order to provide service (e.g. route traffic, support emergency calls) in accordance with the governing national or regional regulatory requirements applicable to that UE. (TS 22.261/6.3.2.3)
  The 5G system shall support mechanisms to determine the UE’s position-related data for period when the UE is outside the coverage of 3GPP RAT-dependent positioning technologies but within the 5G positioning service area (e.g. within the coverage of satellite access) （TS 22.261/6.27）
Service continuity related
  The 5G system shall support service continuity between 5G terrestrial access network and 5G satellite access networks owned by the same operator or owned by different operators having an agreement（TS 22.261/6.2.3）
Low power MIoT type of communications related
  The 5G system with satellite access shall be able to support low power MIoT type of communications. (TS 22.261/6.3.2.3)
Satellite access or satellite backhaul with the consideration of intersatellite links
  A 5G system with satellite access shall be able to support meshed connectivity between satellites interconnected with intersatellite links. (TS 22.261/6.4)
Broadcast/multicast related
  A 5G system with satellite access shall be able to optimise the delivery of content from a content caching application by taking advantage of satellites in supporting ubiquitous service, as well as broadcasting/multicasting on very large to global coverages. (TS 22.261/6.13)
  The 5G system shall support multicast/broadcast via a 5G satellite access network, or via a combination of a 5G satellite access network and other 5G access networks. (TS 22.261/6.13)

## Slide 4: Problems of the existing location mechanism
What existing positioning methods can be applied to NTN?
  Existing positioning solutions are mostly based on the measurements between UE and multiple TPs. However, UE may only have the connection with a single gNB in NTN
  The time-synchronisation of different TPs is important for RSTD measurement, however, it is hard to meet tight time-synchronisation requirements in NTN.
How to meet the performance requirements of location services?
  Latency:
    High latency due to long propagation delay
    For DL TDOA/DL AoD, the latency is 222.5-353 ms in TN, for NTN, the latency may be the value plus 6 RTTs(UE between satellite)
  Accuracy:
    wider range, wide beam spot, angle related solutions can’t provide high positioning accuracy in NTN

## Slide 5: Problems of service continuity between 5G terrestrial access network and 5G satellite access network
Case A: For an ongoing service application running over satellite access, when UE moves into an area with 5G terrestrial coverage, it may handover to the gNB providing 5G terrestrial coverage.
Case B: For an ongoing service application running over terrestrial 5G NR, when UE moves into an area of no terrestrial 5G NR coverage but under the satellite coverage, it may handover to the gNB with satellite access.
For the above 2 cases, the satellite serving gNB or the terrestrial serving gNB needs to determine the terrestrial or satellite cells to be measured by the UE.
Some service application may prefer satellite access for the benefits of service continuity, while others may prefer terrestrial access taking advantage of the short delay, large bandwidth and strong reliability.

## Slide 6: Problems of Low power MIoT type of communications over NTN
MIoT type of devices can be applied in the desert, ocean, forest, etc., where there’s only satellite coverage
Unlike a normal UE, e.g. a smartphone, MIoT type of devices are usually used for specific purpose in vertical industries, thus may have reduced capabilities, e.g. low power consumption, no GNSS, limited data rate, …
It may be a great challenge to support them when there’s only satellite coverage

## Slide 7: Problems of the support of broadcast/multicast
The coverage of one cell over satellite access may include multiple counties or across country boarders.
While it may be more efficient for the delivery of content from a content caching application by taking advantage of satellites, it may bring problem for the location dependent content transfer and MBMS Service Area.
Different level of multicast may be authorized for satellite access considering the limited satellite resources.
Guarantee service continuity for broadcast/multicast
  between 5MBS capable NG-RAN nodes
  between NG-RAN node supporting 5MBS and NG-RAN node not supporting 5MBS including the delivery mode switch
  between 5G terrestrial access network and 5G satellite access network

## Slide 8: Stage 2 Key Issues not resolved in R17
Key Issue #7 of TR 23.737 “Multi connectivity with satellite access” intended to address the following aspects:
    The impacts on 5GS when introducing multi connectivity with satellite access
    Are there any similarities with respect to ATSSS
    To take into account these impacts, what are functional nodes and procedure in 5GS to be updated?
However, there’s no further progress in R17

## Slide 9: Stage 1 R18 new requirements
TR 22.926 provided Guidelines for Extra-territorial 5G Systems, in which territories affected by regulatory requirements on communication, 3GPP Services/features affected by extra-territoriality, 5G ET UE location related used use cases, 5G ET Network location related use cases are introduced.
Architectural impacts due to these regulatory requirements may need to be considered.

## Slide 10: Proposed R18 5GSAT_ARCH Enhancement
UE location determination with satellite access or satellite backhaul
Support of low power MIoT type of communications over satellite access
Support of broadcast/multicast service over satellite access
Multi connectivity with satellite access
Architectural impacts due to extra-territoriality regulatory requirements