## Slide 1: ATSSS_Ph2 Status Report
Apostolis Salkintzis
Lenovo

## Slide 2: ATSSS_Ph2 status after SA2#145e (1/3)
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 97% | Jun, 2021 | SP-200977
General
  All tasks are completed (see next slide) and the WI achieved 97% completion.
  The details of the "correlation information" are still not agreed (see next slide) but this is excepted to be completed at the next meeting. Two proposals already discussed but further consideration is still needed.
  Good progress achieved in SA2#144e and SA2#145e with 20 CRs approved against TS 23.501/502/503

## Slide 3: ATSSS_Ph2 status after SA2#145e (2/3)
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 97% | Jun, 2021 | SP-200977
Task 1.1: PMF Enhancements to support per-QoS measurements
  Completed. PMF measurements can be supported per QoS flow.
Task 1.2: Load-Balancing without pre-defined split percentages
  Completed. Autonomous load-balance mode has been defined.
Task 1.3: UE-assistance indication
  Completed except the details of the “correlation information” sent from UE to UPF.
    Two different solutions proposed (see S2-2103870 & S2-2104080) but both were postponed
    The “correlation information” as a concept is already agreed (in SA2#144e). The CRs introducing the details of the correlation information will be handled at the next meeting (SA2#146e).
Task 1.4: Threshold conditions
  Completed.
Task 2.1: Supporting MA PDU with 3GPP access leg over EPC and Non-3GPP access leg over 5GC
  Completed.
Addition of ATSSS Rule ID and individual rule modification (S2-2104073/4074)
  It was agreed to introduce support for individual ATSSS rule modification, although this was not in the scope of ATSSS_ph2 but was considered important by many companies. The SA2 agreement affected only Rel-17, however, CT1 made the same agreement for both Rel-16 and Rel-17. Alignment CRs are expected at the next meeting to align with the stage-3 specs.

## Slide 4: ATSSS_Ph2 status after SA2#145e (3/3)
  RAN impacts and dependencies:
  None
Contentious Issue:
  None
Focus for the Next Meeting (SA2#146e):
  Work to complete the definition of the "correlation information"
Overall Plan:
  Coordinate work to align with stage-3 and define the details of the “correlation information" at SA2#146e

## Slide 5: ATSSS_Ph2 Status at SA#92-e
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 97% | Jun, 2021 | SP-200977
Progress since SA#91-e:
  ATSSS_ph2 is presented to SA for the second time (normative work initiated at SA2#143e; Jan. 2021)
  Good progress achieved in SA2#144e, SA2#145e and the WI reached 97% completion
  20 CRs approved against TS 23.501/502/503
  One small issue remains open
RAN impacts or dependencies:
  None
Next steps:
  Resolve the remaining open issue by reconsidering the associated technical proposals

## Slide 6: backup