## Slide 1
3GPP TSG SA WG2 Meeting #147e
Oct 18 – Oct 22 2021, Electronic meeting
Source: | Samsung
Title: | Discussion on EDC proposal
Document for: | Endorsement
Agenda Item: | 8.3
Work Item / Release | eEDGE_5GC / Rel-17
Abstract of the contribution: This document discusses the EDC proposal
S2-2107282

## Slide 2: EDC proposal summary (as in S2-2106480r04 in SA2#146e)
EDC Functionality
  Receive the MNO DNS address from SMF via NAS SM
  DNS client
    Send/Receive DNS Query/Response to/from MNO DNS Server (e.g. EASDF)
EDC APIs
  Resolve IP from FQDN using EDC (i.e. EASDF)
  Provides to DNS server address to the application when requested

## Slide 3: Samsung’s view on EDC proposal
It is sufficient to specify UE behaviour rather than specify new functionality (the EDC) with in the UE, so we’d like to understand the need for the latter.
If the EDC is optional it is unclear how it can satisfy a mandatory requirement of UE so it would result in multiple solutions
  The EDC API and existing APIs would need to coexist
Location of the EDC
  Option 1. EDC is located in the UE OS
    This option is the same as the existing DNS client in UE OS.
  Option 2. EDC is located in UE modem
    How does the UE OS enable EDC API for application without UE OS support?
    How to solve this if the UE OS isn’t trusted?
Notes:     Replace the existing DNS Client with EDC, or is the existing DNS client OK?
    Are two APIs expected, one for Android OS and one for the 3GPP API

## Slide 4: Options
Option 1. DNS Client in UE OS
  As implemented in the commercial UE OS
Option 2. Optional EDC in UE Modem
  New API can be used by UE OS to use
Proposal on Option 1
Let’s describe “how does it work in UE OS” (Option 1) in Annex of TS 23.548 (an example: S2-2107283)
Proposal on Option 2: Study “how the EDC works within the UE modem”
How the EDC in UE modem can communicate with Application running on UE OS?
How is it related with the existing AT command?
Whether or how UE OS provides API by wrapping the modem provided API
How and whether EDC and DNS Client co-exist