## Slide 1: - Discussion paper - Study on 5GC enhancement for satellite access Phase 2 (presentation slides for S2-2107451)
Source:
Thales, Xiaomi, Novamint, TNO
Supporting companies:
ESA, SES, Sateliot, Gatehouse, Intelsat, Hispasat, Hughes Network System, Gilat Satellite networks Ltd, Avanti communications, Eutelsat
S2-2107454

## Slide 2: 5GC enhancement for satellite access in Rel18
Where we are:
  Following study (TR23.737) Work Item for Integration of satellite components in the 5G architecture (5GSAT_ARCH) (R17) is now completed, with first normative step enabling satellite is R17.
  We are in the selection process for R18 content, for RAN and SA TSGs, ending in December 2021.
Where we want to go:
  To the definition of a consolidated R18 Study Item for satellite access in Q4, to be able to enhance and complete the 5GC architecture, in accordance with RAN feature selection.
  Working assumption is that IOT NTN connects 5GC for general functional and procedural study on 5GC framework. Adaptations for EPC, leveraging on this study on 5G enhancements, are FFS.
  The present slideware is a list of candidate features we consider as first stones in such R18 satellite SID

## Slide 3: 5GC enhancement for satellite access in Rel18
Discontinuous coverage
Store and forward (regenerative payload)
Broadcast/multicast
Network based UE location determination
Support of Performance Enhancement Proxy
Mobility and Service continuity
Relay based architecture including satellite

## Slide 4: # Discontinuous coverage
Justification:
  Dynamic support of discontinuous coverage is required for initial NGSO constellation deployment but as well to support evolution of the constellations such as loss of satellites, different releases supported in a given constellation…).
  There is an important aspect of discontinuous coverage related to dynamic GEO systems where beams/cells are intermittent due to use of dynamic beam configuration
5GC areas for study:
  Mobility Enhancement (Paging…)
  Prediction, awareness & notification of UE wake-up time, power saving optimizations.
Problem Statement:
  UE under satellite coverage only at specific time and places due to sparse constellation.
  Paging to be synchronized with UE and satellite motion.
  UE should not always stay awake for the sake of power efficiency, especially for MIoT UE
RAN#93 outcomes:
  Support for discontinuous coverage is not considered for NR-NTN
  Support for discontinuous coverage is considered priority 1 for IoT-NTN

## Slide 5: # Store and forward (regenerative payload)
Justification:
  Support of store-and-forward (S&F) capabilities will provide service coverage with NGSO satellites to areas where NTN-GWs cannot be deployed (e.g. deep-sea maritime areas). S&F capabilities would allow for a reduced network of NTN-GWs while still achieving a global service coverage for delay-tolerant/non-real-time IoT NTN services.
  From a commercial perspective, support of store-and-forward on-board NTN payload is an essential feature at the horizon of the Release 18 deployment (2025+) to enable cost effective and scalable solutions. S&F would facilitate faster market adoption and competitiveness of 3GPP solutions taking into account that, at present, proprietary non-3GPP S&F already exists on the market.
5GC areas for study:
  Session and Mobility management enhancements for the use case.
  User plane enhancements for the use case.
Problem statement:
  The satellite needs to embark eNB function and storage capability (plus, potentially, some core network functionality) in order to harvest data from IoT devices along its orbit and forward it to a core network when it encounters a NTN-GW and the feeder link can be activated. Conversely, the satellite uploads data from core network when connected to a NTN-GW and delivers it to the relevant IoT-devices when covering the targeted service area.
RAN#93 outcomes:
  Regenerative Payloads with ISL needs further discussions for NR-NTN
  Support for store-and-forward on-board NTN payload needs further discussions for IoT-NTN (SA2 support needed)

## Slide 6: # Broadcast/multicast
Justification:
  To meet for example public safety needs, software upgrades, multimedia content distribution and media content broadcasting.
  Also for IoT (type of) applications that require e.g. triggering or distribution of messages.
5GC areas for study:
  Location and MBS Service Area determination for content transfer
  Supporting differentiated QoS for MBS.
  Content transfer for UEs temporarily out of coverage due to discontinuous coverage or regenerative payload
  User plane path selection between satellite path and terrestrial path for efficient content transfer
Problem statement:
  UE Location dependent content transfer and MBS Service Area requires accurate location; however, the coverage of one cell over satellite access may include multiple countries or across country boarders
  Different UE or UE category which join in multicast service may have different QoS requirement(e.g. 5GC Individual MBS traffic delivery or 5GC shared MBS traffic delivery with PTP/PTM method), to efficient usage of network resources, especially limited satellite resources, differentiate QoS should be supported by satellite access
  When UEs are temporarily out of coverage due to discontinuous coverage or regenerative payload, store and forward may be needed in the network
  When both satellite path and terrestrial path are available, the performance of each path may be different
RAN#93 outcomes:
  5MBS needs further discussions for NR-NTN
  Broadcast/Multicast is not considered for IoT-NTN

## Slide 7: # Network based UE location determination
Justification:
  For regulatory services (e.g. lawful intercept, emergency communications, public warning service) as well as handling of extraterritoriality requirements where Law enforcement apply, the network shall be able to provide a “reliable” UE location (either network verified or network provided).
5GC areas for study:
  Refine triggering conditions after LCS framework new method definition .
  Check compliancy with regulated service requirements (network provided or verified)(TS 22.261).
  Check compliancy with extraterritoriality requirements (See SA1 extra-territoriality 5GET study)
  Possible architectural enhancement to meet location services requirements as defined in TS 22.261.
Problem statement:
  The Core Network shall be capable of making efficient use of this method according R17 UE localization mechanisms.
RAN#93 outcomes:
  Network based UE location is considered priority 1 for NR-NTN, dedicated study envisaged
  Network based UE location is not considered for IoT-NTN

## Slide 8: # Support of Performance Enhancement Proxy
Justification:
  In case of GEO satellite access for Uu interface, any connected protocol (TCP, QUIC, SCTP…) will be degraded at performance and user quality of experience levels in case of long delay.
5GC areas for study:
  Investigate if solution can be endorsed by 3GPP to enhance user quality of experience for connected protocols in case of PEP long delay.
  Investigate where PEP can be placed in 5GC architecture (SA2).
  Investigate how PEP can be integrated in security architecture (SA3).
Problem statement:
  To cope with GEO delay, a widely used solution is to make use of PEPs (performance Enhancement Proxies).
  If IP level security layer is used over satellite access, such PEPs cannot be used.
RAN#93 outcome:
  N.A.: Connected protocol performance enhancement is introduced by satellite GEO delay and proposal is to start 3GPP study at system architecture level.

## Slide 9: # Mobility and Service continuity
Justification:
  Service continuity when switching between terrestrial and satellite access networks is key to the user experience.
  When both 5G terrestrial access network and 5G satellite access are available, the performance of each access shall be considered for some specific applications for the handover, see use case defined in clause 5.7 of TR 22.822
5GC areas for study:
  Hand Over based on application preferences: enhance architecture (new mobility triggers) such that application could choose between satellite access (benefits of service continuity) or terrestrial access (benefits of short delay, large bandwidth and high reliability).
  Service continuity in case of shared satellite RAN with multiple CN e.g. on ships near coastal areas
  Mobility RAN enhancements for IoT NTN may have SA/CT impacts.
Problem statement:
  To cope for an ongoing service application, e.g. VoNR emergency call, the service continuity has to be guaranteed:
    Case A: If it is running over satellite access, when UE moves into an area with 5G terrestrial coverage, it may handover to the gNB providing 5G terrestrial coverage.
    Case B: If it is running over terrestrial 5G NR, when UE moves into an area of no terrestrial 5G NR coverage but under the satellite coverage, it may handover to the gNB with satellite access.
RAN#93 outcomes:
  Mobility and service continuity is considered priority 1 for NR-NTN
  Only TN/NTN Mobility enhancement is considered as priority 1 for IoT-NTN

## Slide 10: # Relay based architecture including satellite
Justification:
  (SA1) 5G system shall be able to support mobile base station relays using 3GPP satellite NG-RAN
  (SA2 R17) 5G system shall be able to support UE to NW relay with Uu by satellite
  Store and forward relay will strongly enhance applicability of store and forward scheme (see #2), e.g.: IoT devices needing relay that would use store and forwarding on dedicated satellite system.
5GC areas for study:
  Applicability of existing solutions for satellite?
  Store and forward relay architecture and procedures
Problem statement:
  In IoT use cases, the satellite coverage deployment scheme will most probably request store and forward support at the relay level.
  Modification of existing solutions for satellite
  Opportunistic relay connectivity of the relay Base Station to 5GC via Terrestrial or Satellite.
RAN#93 outcomes:
  NTN relays are not mentioned in RAN discussions (“NTN (Non-Terrestrial Networks) evolution - Including both NR & IoT (Internet of Things) aspects”

## Slide 11: Thank you!