## Slide 1: Location based services
Background:
for individual fallback the following procedure is agreed (see Clause 6.2.1 of TS 23.247)
  For multicast communication, local MBS and location dependent MBS services may be supported via 5GC Individual MBS traffic delivery towards RAN nodes not supporting MBS. If the SMF obtains a notification about the UE location, it checks whether the UE is still in the MBS service area of the multicast session. For a local MBS service, if the UE is no longer in the MBS service area, the SMF terminates the 5GC Individual MBS traffic delivery towards the UE. For a location dependent MBS service, if the UE is no longer in the current MBS service area, the SMF determines whether the UE is in another MBS service area of the multicast session; if so, the SMF configures the UPF to send multicast data relating to the new MBS service area towards the UE. If the SMF terminates the 5GC Individual MBS traffic delivery towards the UE, it unsubscribes at the AMF from the notifications about the UE location or "UE moving in or out of a subscribed "Area Of Interest" event using the Namf_EventExposure service.
For local MBS services the following is agreed (see Clause 6.2.2 of TS 23.247):
  Depending on policy, for the multicast MBS service the network may remove UEs outside the MBS service area of the MBS session from the MBS session context after a grace period (e.g. by using a local configured timer).
For location dependent MBS services the following is agreed(see Clause 6.2.3 of TS 23.247)
  Depending on policy, for the multicast MBS service the network may remove UEs outside all MBS service areas of the MBS Session from the multicast MBS session context after a grace period (e.g. by using a local configured timer).

## Slide 2: Location dependent MBS services
Open issues:
  The following editor´s note in TS 23.247 needs to be addressed:
    Editor's note: Procedures for the UE mobility between cells of one RAN node, e.g. when the UE leaves, enters or switches service areas due to mobility are ffs. For shared delivery it is FFS whether, the RAN node handles content switching due to mobility between service areas it serves autonomously or the core network needs notifications about this mobility to select new service areas. For the UE leaving a service area it is ffs whether the RAN node defers related notification for a grace period or the SMF defers removing UEs from the multicast session. Details require coordination with RAN
  Should the event subscription solution for individual fallback/non 5MBS capable RAN nodes also be applied towards 5MBS capable RAN nodes?
  Or should the RAN node switch autonomously between service areas for location based services?
  Depending on this, is only the service area where the UE is residing or all service areas served by a RAN node send to the RAN node when the UE joins or during handover?
    In the later case, either all service areas of the MBS session or only the service areas served by one RAN node could be communicated
  Does the RAN node inform the SMF immediately when the UE leaves the service area (local MBS) / all service areas (location dependent MBS) or apply a grace period before?

## Slide 3: Location dependent MBS services
Considerations:
  Reuse of solution for non-supporting nodes towards supporting nodes might simplify implementation.
  However the solution is not optimised:
    The solution is not optimal for the switch between service areas:
      Area of intrest event will not report the new location of the UE and thus an extra location inquiry is required to determine a new service area.
      Cell change event leads to very high signalling load
      Interaction with SMF to determine the new service area will lead to service interruptions
      The solution will lead to higher signalling load than autonomous switching at RAN node

## Slide 4: Location dependent MBS services
Considerations (continued)
  However the solution is not optimised (continued)
    The solution is not optimal when UE leaves service area:
      A UE at the cell edge might repeatedly leave and enter service area
      RAN nodes may be capable of anticipating probability that UE re-enters service area based on UE trajectory
      The solution may thus lead to higher signalling load than grace period at RAN node
      On the other hand, RAN tries to minimize cell changes and handovers in any case
  The solution for non-supporting nodes might become unworkable if the encoding of the service area is modified as the area of interest encoding for the existing event relies on tracking areas and cell Ids)

## Slide 5: Location dependent MBS services
Considerations (continued)
  Autonomous switching at RAN node requires that all several service areas served by the RAN node are communicated to the RAN node
    This happens in PDU session related signalling when a UE joins or during handover. For a service with many small service areas based on cell IDs (e.g. V2X) communicating all service areas of the service might thus not be practical or lead to high signalling load
    However, SMF has no knowledge of area served by a RAN node to do the filtering of service areas for a RAN node
    A possible alternative could be to provide this information during shared tunnel establishment from the MB-SMF
    In addition, either the MB-SMF of SMF can filter service areas for a RAN node if it obtains RAN node IDs and tracking areas of the RAN node (assuming existing service area encoding via tracking area and cell ID; cell IDs contain RAN node IDs)

## Slide 6: Location dependent MBS services
Proposals
The RAN node switches autonomously between service areas for location based services
All service areas served by a RAN node (and only those) are send to the RAN node when the UE joins or during handover.
  The SMF obtains the tracking areas served by the RAN node and the RAN node ID from the RAN node and determines the service areas based on that
The RAN node informs the SMF only after a grace when the UE leaves the service area (local MBS) / all service areas (location dependent MBS)
  A new event is defined or the area of interest event is extended with new parameters to request this behavior