## Slide 1
TEI18 proposal: Per UE S-NSSAI priority awareness in the (R)AN by sending per UE S-NSSAI priority from AMF to (R)AN
SA2#152E August 17-26 2022 S2-2206393

## Slide 2
Per UE S-NSSAI priority awareness in the (R)AN
The objective is to include in the information the AMF sends to the (R)AN when it sends the Allowed NSSAI to the (R)AN the S-NSSAI priority for the S-NSSAIs in the Allowed NSSAI. The S-NSSAI priority is derived from a Subscribed S-NSSAI priority the AMF receives. This Priority value is specific for the UE subscription and does not apply across UEs (i.e. it is not an absolute priority value that can be used by the (R)AN for decisions that apply between e.g. two UEs)
The (R)AN receives the Allowed NSSAI, but it cannot determine which of the S-NSSAIs in the Allowed NSSAI is more important for the UE. Having this information is beneficial e.g. to allow effective per UE RRM policies and also to take decisions based on the relative importance of a network slice when e.g. the candidate cells for handover may support different sets of S-NSSAIs, or e.g. when at time of congestion the "essential" set of DRBs for the more important slices of the UE need to be preserved.
For instance, a UE allowed NSSAI may include S-NSSAI 1 and S-NSSAI 2. For the RAN it is difficult to determine which target cell to use if the target support only one of them but not both.
In figure 1 the candidate target cells are TA3 and TA2 supporting S-NSSAI 1 and S-NSSAI2 respectively... which cell to choose?
In short, if the (R)AN node knows that S-NSSAI 1 is more important for the UE, it can have a tool to provide a more predictable and more appropriate service experience at times of congestion or when it needs to take decision involving ,mutual exclusivity among the S-NSSAIs in the Allowed NSSAI. This relative importance among S-NSSAIs in general cannot be the same for all the UEs. Hence the need to receive information from the AMF.