## Slide 1: NR_Slice_Core issues from SA#96
SA2#152E, 17-26 August 2022
AI#8.28
S2-2206626

## Slide 2
Mission from SA#96
TSG SA#96 asks SA WG2 to work on clarifying NR_Slice_Core in Q3. SA WG2 is asked to work on clarifying the Random access behaviour and how the NSAG priority is formed. Additionally, the sentence describing how Cell Reselection is disabled if the NSAG priorities are not sent should be clarified. Impacts on RAN shall be avoided. Interested companies also need to ensure that the corresponding stage 3 aspects are finalized at TSG CT#97.)

## Slide 3
NR_slice_core: “to do” for SA2

## Slide 4: NR_Slice Goal and what SA2 has to do
FS_NR_slice objective was (see RP-201612):
Then, in the course of the study, RAN2 discussed the concept of intended slice but concluded it is not in their scope and so we need to figure out and specify in SA2 how the intended slice is linked to the NSAG and NSAG priority. RAN2 relies on SA2 to do so by the way the NAS/AS split has been defined so far.
If SA2 does not converge on the definition of intended slice, then the goal of the NR_slice work is not achieved.
  Indeed, this would result in choosing the wrong frequency band or use the wrong RACH resources for the UE, where the definition of "correct" is "The RACH resources and the band that the UE shall select as they are corresponding to the RACH resources and the preferred band for the intended slice".
We need to clarify the rationale for selection of the Intended Slice and how this is implemented in the updates of TS 23.501 and TS23.502 necessary to meet the guidance by SA#96.
Study mechanisms to enable UE fast access to the cell supporting the intended slice, including [RAN2] a. Slice based cell reselection under network control b. Slice based RACH configuration or access barring

## Slide 5: Intended slice
From our perspective, the intended slice is a synonym for "the most important slice" for the UE at the time that the Network Slice- based Cell Reselection and Random-Access attempt are being undertaken.
It should be noted that the relevant network slices can be any of the configured network slices (i.e. those associated with the S-NSSAIs in the Configured NSSAI) in the UE (and not just the network slices associated with the S-NSSAIs in the Allowed NSSAI).
  this is because the access attempts can be triggered by registration messages for network slices not yet in the allowed NSSAI which are in the Requested NSSAI, and also because the TS 23.501 already requires that the Slices in the Requested NSSAI not yet in the Allowed NSSAI can drive network slice-based cell reselection before the Registration request with the new Requested NSSAI is sent.
Can the UE detect the importance of a network slice among the network slices that it is allowed or is requesting to use?
  A S-NSSAI per se is just a string of bits the UE has no intelligence about. The S-NSSAI can part of a RSD rule in URSP and this rule may be associated with a priority value, but this priority value is related to any alternative RSD rule for same matched TD in the URSPs.
    So, this is not really a measure of the importance of a network slice across the possible allowed or requested slices for the UE.
  Even by considering a standardized SST, it is questionable that a UE can infer the importance of an SST based on its semantics. e.g. it is unclear whether eMBB is more important for any UE than mIoT SST.
Conclusion: An autonomous decision by the UE on which slice is the most important at a given time is not possible in a deterministic way when more than one application is running and causes PDU sessions to be established on more than one slice. The UE needs information from the network to evaluate the relative importance of network slices.

## Slide 6
The current behaviour specified in SA2 TSs
The AMF provides NSAG(s) and for each NSAG the associated priority to the UE via NAS signalling.
Problems:
How the NSAG priority is determined by the AMF is not specified,
  So, there is no real way to have an interoperable solution that meets the goal of performing the Slice-based cell reselection and Random Access based on the “Intended Slice”.
A static NSAG priority value is provided to UE that can take the Allowed NSSAI S-NSSAI into account only (slices not yet in allowed NSSAI cannot be “guessed” and the next to be e.g. requested)
  This is not suitable as the UE can use S-NSSAIs that are not yet in the Allowed NSSAI when registering, and which slice(s) are associated with a SR (e.g. which slices sessions cause the SR) or RR is not predictable (UE can add or remove S-NSSAIs from current Allowed NSSAI).
  In addition, in roaming case, the S-NSSAI in VPLMN can map to >1 Slice of HPLMN: which slice of HPLMN applies for a SR or RR determined at run time in the UE before the network can act on it and this information is needed to trigger the right RACH configuration or cell reselection ahead of Requesting a new S-NSSAI.

## Slide 7
NSAG priority

## Slide 8
An off the shelf, standard UE cannot determine the S-NSSAI importance autonomously
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
UE 1
There is no ranking of applications importance defines by a standard mechanism (the RSDs priority is ranking their priority as connectivity for traffic matched by a TD in URSP, so it is not a priority of the S-NSSAI in the RSD)
There is no standard capability to gather the run time importance of applications the User is using
Only in specific vertical application the UE may be configured with each vertical applications importance, but this is not a generic expected capability.
The UE can at most detect which slices have an associated PDU session and consider these higher priority.

## Slide 9
The relationship between network slices priority and NSAG priority
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
UE 1
NSAG 1 = (S-NSSA 1, S-NSSAI 4)
NSAG 2 = (S-NSSA 2, S-NSSAI 3)
NSAG priority cannot be static as it depends on the applicable slices the UE is requesting or that are triggering a RACH access attempt.
The AMF can only know the Slices in the allowed NSSAI but not those in the next Requested NSSAI or triggering a SR.
 The UE has to receive raw information to compute the NSAG priority, and not a fixed NSAG priority value
S-NSSAI 1 | S-NSSAI 2 | S-NSSAI 3 | S-NSSAI 4 | Applicable NSAG (and NSAG priority)
x | x | x | x | NSAG1(1), NSAG2(2)
x | x | x |  | NSAG1(1), NSAG2(2)
 | x | x | x | NSAG1(4), NSAG2(2)
 |  | x | x | NSAG1(4), NSAG2(3)
x | x |  | x | NSAG1(1), NSAG2(2)
x | x |  |  | NSAG1(1), NSAG2(2)
x |  | x |  | NSAG1(1), NSAG2(3)
x |  |  | x | NSAG1
 | x |  | x | NSAG1(4), NSAG2(2)
 | x | x |  | NSAG2
 |  | x | x | NSAG1(4), NSAG2(3)
x |  |  |  | NSAG1
 | x |  |  | NSAG2
 |  | x |  | NSAG2
 |  |  | x | NSAG1
RELATIONSHIP BETWEEN APPLICABLE SLICES AND PRIORITY VALUES

## Slide 10
NSAG priority must be per UE
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
S-NSSAI 1 prio 3
S-NSSAI 2 prio 2
S-NSSAI 3 prio 2
S-NSSAI 4 prio 1
UE 1
UE 2
NSAG 1 = (S-NSSA 1, S-NSSAI 4)
NSAG 2 = (S-NSSA 2, S-NSSAI 3)
The importance/priority of a S-NSSAI is not necessarily the same across UEs.
The importance of S-NSSAIs in NSAG should determine the priority of a NSAG for a UE.
It follows the NSAG priority value may not be the same for different UEs
 | eMBB | mIoT | URLLC
Smartphone subscription | Priority 1 | Priority 3 | Priority 2
IoT subscription | Priority 2 | Priority 1 | N/A
Industrial IoT subscription | Priority 2 | N/A | Priority 1
EXAMPLE: importance of a network slice for a subscription based on its purpose

## Slide 11
The importance of a network slice is determined by the contract with the customer.
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
UE 1
The network has to be capable to provide a per UE information ( the importance of a network slice versus another cannot be the same for all possible UE subscriptions)
The HPLMN knows the set of network slices the UE subscribes to and can determine a relative ranking of importance based on the service expectations.
It is also possible that all slices have the same priority. In this case no priority value or the same priority value can be defined for the slices
This information needs to be available also to roaming partners alongside the S-NSSAIs that are allowed in the roaming partner networks.
When a UE roams, the NSAG priority is determined by considering the Mapped S-NSSAI value. If more than one S-NSSAI of HPLMN is mapped to one S-NSSAI of the VPLMN, then the VPLMN S-NSSAI priority is the highest priority of the mapped S-NSSAIs that are currently being considered for RACH configuration or Cell reselection.

## Slide 12
Roaming case – mapping between Subscribed S-NSSAI priorities and VPLMN S-NSSAI priority
V-S-NSSAI 1
V-S-NSSAI 2
H-S-NSSAI A (priority 2)
H-S-NSSAI B (priority 1)
H-S-NSSAI C (priority 3)
H-S-NSSAI B | H-S-NSSAI C | V-S-NSSAI 2 priority
x | x | 1
x |  | 1
 | x | 3
HPLMN S-NSSAI | Priority
H - S-NSSAI A | 2
H - S-NSSAI B | 1
H - S-NSSAI C | 3
X = H-S-NSSAI for RACH or Cell Reselection
VPLMN S-NSSAI | HPLMN S-NSSAI
V- S-NSSAI 1 | H-S-NSSAI A
V-S-NSSAI 2 | H-S-NSSAI B
V-S-NSSAI 2 | H-S-NSSAI C
Configured NSSAI including mapping info
Subscribed S-NSSAI priority
H-S-NSSAI A | V-S-NSSAI 1 priority
x | 2
X = H-S-NSSAI considered for RACH or Cell Reselection
Visited PLMN S-NSSAI priority derived from Subscribed S-NSSAI priority
If the S-NSSAI of the VPLM maps to >1 S-NSSAI of the HPLMN, and >1 mapped HPLMN S-NSSAIs are considered as part of cell reselection or signalling transaction triggering access attempt (because the corresponding connectivity is logically associated to >1 HPLMN S-NSSAI), the priority for the VPMN s-NSSAI is the highest priority of the applicable mapping HPLMN S-NSSAIs

## Slide 13
How does the UE operate?
APP n-1
APP n
APP 1
APP 2
Traffic Descriptor matching APP2 traffic
Route Selection Descriptor =
(DNN y, H-S-NSSAI A)
VPLMN S-NSSAI | HPLMN S-NSSAI
V-S-NSSAI 1 | H - S-NSSAI A
V- S-NSSAI 2 | H - S-NSSAI B
V - S-NSSAI 2 | H - S-NSSAI C
Configured NSSAI including mapping info
HPLMN S-NSSAI | Priority
H - S-NSSAI A | 2
H - S-NSSAI B | 1
H - S-NSSAI C | 3
Subscribed S-NSSAI priority
NSAG | VPLMN S-NSSAI
NSAG 5 | V-S-NSSAI 1
NSAG 86 | V-S-NSSAI 2
NSAG 7 (RACH) | V-S-NSSAI-1
NSAG-34 (RACH) | V-S-NSSAI 2
NSAGs
Traffic Descriptor matching APP n traffic
Route Selection Descriptor =
(DNN w, H-S-NSSAI C)
NSAGs | VPLMN S-NSSAI | H-PLMN S-NSSAI | Subscribed S-NSSAI Priority (always associated with HPLMN S-NSSAI) | calculated NSAG priority
NSAG 5 | V-S-NSSAI 1 | H-S-NSSAI A | 2 | 2
NSAG 86 | V-S-NSSAI 2 | H-S-NSSAI C | 3 | 3
NSAG 7 (RACH) | V-S-NSSAI 1 | H-S-NSSAI A | 2 | 2
NSAG 34 (RACH) | V-S-NSSAI 2 | H-S-NSSAI C | 3 | 3
Scenario: running apps cause a Registration Request with REQUESTED NSSAI = (V-S-NSSAI 1 (mapped to H-S-NSSAI-A), V-S-NSSAI 2 (mapped to H-SNSSAI c)) for new connectivity (e.g. V-S-NSSAI 2 was not yet in Allowed NSSAI)
.
.
.
NSAG for cell reselection | Priority
NSAG 5 | 2
NSAG 86 | 3
NSAG considered for RACH configuration
NSAG RACH configuration
NSAG 7
NSAG considered for cell reselection and priority
NSAG Info provided by AMF

## Slide 14
How does the UE operate ?
APP n-1
APP n
APP 1
APP 2
Traffic Descriptor matching APP2 traffic
Route Selection Descriptor =
(DNN y, H-S-NSSAI A)
VPLMN S-NSSAI | HPLMN S-NSSAI
V-S-NSSAI 1 | H - S-NSSAI A
V- S-NSSAI 2 | H - S-NSSAI B
V - S-NSSAI 2 | H - S-NSSAI C
Configured NSSAI including mapping info
HPLMN S-NSSAI | Priority
H - S-NSSAI A | 2
H - S-NSSAI B | 1
H - S-NSSAI C | 3
Subscribed S-NSSAI priority
NSAG | VPLMN S-NSSAI
NSAG 5 | V-S-NSSAI 1
NSAG 86 | V-S-NSSAI 2
NSAG 7 (RACH) | V-S-NSSAI-1
NSAG-34 (RACH) | V-S-NSSAI 2
NSAGs
Traffic Descriptor matching APP n traffic
Route Selection Descriptor =
(DNN w, H-S-NSSAI C)
NSAGs | VPLMN S-NSSAI | H-PLMN S-NSSAI | Subscribed S-NSSAI Priority (always associated with HPLMN S-NSSAI) | calculated NSAG priority
NSAG 5 | V-S-NSSAI 1 | H-S-NSSAI A | 2 | 2
NSAG 86 | V-S-NSSAI 2 | H-S-NSSAI C, H-S-NSSAI B | 3, 1 | 1
NSAG 7 (RACH) | V-S-NSSAI 1 | H-S-NSSAI A | 2 | 2
NSAG 34 (RACH) | V-S-NSSAI 2 | H-S-NSSAI C, H-S-NSSAI B | 3, 1 | 1
.
.
.
NSAG for cell reselection | Priority
NSAG 5 | 2
NSAG 86 | 1
NSAG considered for RACH configuration
NSAG RACH configuration
NSAG 34
NSAG considered for cell reselection and priority
Scenario: running apps cause a Registration Request with REQUESTED NSSAI = (V-S-NSSAI 1 (mapped to H-S-NSSAI-A), V-S-NSSAI 2 (mapped to H-SNSSAI C), V-S-NSSAI2(mapped to S-NSSAI B)) for new connectivity (e.g. V-S-NSSAI 2 was not yet in Allowed NSSAI)
Traffic Descriptor matching APP n-1 traffic
Route Selection Descriptor =
(DNN R, H-S-NSSAI B)
NSAG Info provided by AMF

## Slide 15
Summary
The NSAG priority is determined by the importance/priority of applicable slices of the NSAG considered for cell reselection or for RACH access attempt. This is evaluated at runtime in the UE and cannot possibly be provided by the AMF.
A S-NSSAI priority versus the other S-NSSAIs is per UE, it is not a property of the deployed slice in serving PLMN, but of the service requirements defined by HPLMN for the UE.
The S-NSSAI priority versus the other S-NSSAIs is determined by the HPLMN based on the service contract with the customer (e.g. type of subscription) based on the HPLMN commercial offerings (i.e. this does not require a per customer negotiation)
The S-NSSAI priority versus the other S-NSSAIs in the subscription has to be available while the UE is in the HPLMN and in the VPLMN as oit has to support the per UE differentiation in the HPLMN and in the VPLMN.
In roaming case, the Priority of a S-NSSAI of VPLMN is the highest priority of the HPLMN mapped S-NSSAI slices that are considered for RACH configuration or Cell Reselection (see previous two slides ). The HPLMN S-NSSAI priority forms the basis for determination of the mapped VPLMN S-NSSAI priorities for the UE
  Note: the stage 3 encoding of the NSAG info including the Subscribed S-NSSAIs priority can be also achieved by providing the NSAG definition by using the mapped S-NSSAIs of the HPLMN and for each such S-NSSAI the subscribed S-NSSAI priority (up to CT1 decide which method is more efficient).
AMF Sending to the UE the Subscribed S-NSSAI priority meets all the goals above

## Slide 16
RACH CONFIGURATION handling (nokia proposal)

## Slide 17
Applicable S-NSSAIs for RACH access attempt
A RACH access attempt is caused by a signalling transaction originated by the UE in CM-IDLE or RRC-Inactive state.
A signalling transaction can be related to 1 or more network slices
Signalling transaction | How many S-NSSAIs? | Which S-NSSAIs? | Can the network know these S-NSSAIs in advance
Service Request | 1 or more S-NSSAI | The S-NSSAIs of the PDU sessions the SR activates | Only if there is just one S-NSSAI in the Allowed NSSAI.
Registration Request | 1 or more S-NSSAI | The S-NSSAIs in the Requested NSSAI | Only if the UE subscribes to one S-NSSAI.
Session management | 1 S-NSSAI | The S-NSSAI of the related PDU session | Only if there is just one S-NSSAI in the Allowed NSSAI.
Applicable S-NSSAIs for a RACH access attempt are determined at the UE and cannot in general be determined in the network

## Slide 18
NSAG priority for NSAG used for RACH configuration
For the determination of the NSAG priority for RACH:
  The UE determines first the applicable S-NSSAIs that are associated with the Signalling transaction causing the RACH access attempt
  Then these S-NSSAIs are used to select only the NSAGs for RACH that are associated to these S-NSSAIs
  Finally, for each such NSAG the priority is determined to be the priority of the highest priority S-NSSAI associated with the NSAG, from the set identified at step 1
A static NSAG priority provided in registration accept cannot work because the applicable slices may vary per signalling transaction so the applicable NSAG priority may be wrong and the incorrect RACH configuration is selected..
Applicable S-NSSAIs for a RACH access attempt of the NSAG are used to determine the NSAG priority

## Slide 19
Which NSAG applies for RACH configuration?
The NSAGs for RACH configuration are broadcasted in SIB1 alongside the related RACH configuration parameters.
The UE considers candidate NSAGs for Random Access Configuration in a cell the NSAGs that are broadcasted in SIB 1, are in the UE NSAG configuration and associated with the network slices of the signalling transaction (see previous slide).
Out of the candidate NSAGs (if more than one applies) the highest priority NSAG is selected. If only one applies, then this is the selected NSAG.
Applicable NSAG for a RACH access is determined by the UE considering also NSAG priorities determined at run time based on which slices apply

## Slide 20
CELL RESELECTION handling

## Slide 21: S-NSSAIs to consider for Cell Reselection and their priorities
Based on current TSs, the UE performs slice-aware cell reselection when it is:
CM-IDLE and has an Allowed NSSAI and potentially some PDU sessions and performs Cell Reselection due to Radio Conditions
CM-IDLE and it is attempting to Register with a new set of network slices (Requested NSSAI is different from the Allowed NSSAI and includes at least a new S-NSSAI not in the Allowed NSSAI)
For Case 1) and Case 2) different sets of slices are considered as explained in the following slides.
Correspondingly, the priority of NSAGs can vary depending on the considered set and relative ranking of S-NSSAI priority.

## Slide 22: CASE 1: UE CM-IDLE and has an Allowed NSSAI and potentially some PDU sessions, performs Cell Reselection due to Radio conditions
A UE can register proactively with a set of network slices (e.g. registration based on Configured NSSAI) or it is registering based on the need to immediately establish a PDU session. Let’s suppose the UE1 and UE n both registered proactively with all the 4 S-NSSAIs.
The RAN usually steers the UE to a band best serving the active connectivity. If there is no PDU session for a network slice, this slice bands are not considered. A similar logic can be followed in idle mode also, by prioritizing S-NSSAIs of slices with PDU sessions associated with them. In short the goal is to ensure we sty in bands supporting the ongoing PDU sessions
For instance, for UE 1, the focus would be on S-NSSA 2 and S-NSSAI 4, while for UE n, the focus would be on S-NSSAI 3.
Consequently, the UE 1 would consider NSAG1(priority 4) and NSAG2 (priority 2), and UE n would consider NSAG 2 (priority 3) and set the NSAG 1 priority to a lower value than 3.
  Potentially the UE internally cold have a ranking for S-NSSAI with PDU sessions and one for S-NSSAI without PDU sessions and consider the ones with PDU sessions first.. We do not need to specify how the S-NSSAIs without PDU sessions are ranked lower (i.e. the exact values of priority), as long as they still are ranked relative to one another according to their subscribed priority.
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
UE 1
UE n
NSAG 1 = (S-NSSA 1, S-NSSAI 4)
NSAG 2 = (S-NSSAI 2, S-NSSAI 3)
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
Slice with at least one PDU session
The NSAGs and NSAG priority priority is set in the UE by:
Considering to be higher ranking the S-NSSAIs in the Allowed NSSAI with PDU sessions ordered based on their priority
Considering S-NSSAIs without PDU sessions are ranked according to the Priority but at a lower priority value than those NSAGs with PDU sessions.

## Slide 23: CASE 2: UE CM-IDLE and Requests a set of S-NSSAI(s) including a new S-NSSAI
A UE can register with a new (set of) S-NSSAIs by including in the Requested NSSAI in a Registration Request at least one S-NSSAI not yet in the current Allowed NSSAI
The text in the TS now provides that the UE can trigger Cell Reselection ahead of sending such Registration Request.
The purpose of this Reselection is to potentially move to a cell supporting the new (set of) S-NSSAIs (it is possible the current cell TA may not support the S-NSSAI).
Consequently, the UE shall consider the new S-NSSAIs in the Requested NSSAI with their priority when defining the NSAG priority, regardless of whether there are PDU sessions associated (S-NSSAIs not yet in the Allowed NSSAI have no associated PDU sessions so it is not “fair” to deprioritize them upfront), and ranks them according to the subscribed priority against any S-NSSAI )
In the example on the left, assuming the Requested NSSAI ( S-NSSAI 1, S-NSSAI2, S-NSSAI3) when the Allowed NSSAI was (S-NSSAI 2,S-NSSAI 3), the applicable NSAGs and priorities are NSAG 1 (priority 1) and NSAG2 (priority 2)
S-NSSAI 1 prio 1
S-NSSAI 2 prio 2
S-NSSAI 3 prio 3
S-NSSAI 4 prio 4
UE 1
NSAG 1 = (S-NSSA 1, S-NSSAI 4)
NSAG 2 = (S-NSSA 2, S-NSSAI 3)
The NSAGs and NSAGs priorities is set by considering all S-NSSAIs in the Requested NSSAI
{
Slice with at least one PDU session

## Slide 24
Which NSAGs and NSAG priority applies for Cell Reselection?
For Cell Resection due to radio conditions only:
  Consider NSAGs with Slices in the Allowed NSSAI.
  Slices in the Allowed NSSAI with a PDU session are ranked according to their subscribed S-NSSAI priority and slices without PDU session are ranked according to their subscribed S-NSSAI priority starting from a lower priority value than the lowest priority value of slices with a PDU session at least
    We do not specify the method for ranking inside the UE (e.g. extended priority range or groups of slices with PDU sessions and slices without PDU sessions
For cell reselection when a new S-NSSAI is in the Requested NSSAI of a Registration request:
  Consider NSAGs in the Requested NSSAI ranked according to their Subscribed S-NSSAI priority
For cell reselection when a Requested NSSAI of a Registration request is a subset of the current Allowed NSSAI:
  Continue with Cell Resection due to radio conditions only and consider the existing Allowed NSSAI

## Slide 25
Selective Disabling of slice-aware RACH configuration or
Cell Reselection

## Slide 26
Achieving Selective disablement of features
The current TS enables disabling Slice-aware cell reselection by not indicating the network slice priorities to the UE ["If the UE has not received any NSAG priority information from the AMF, the UE shall not use Network Slice based cell reselection at all"].
  This is incorrect as this would cause also the slice aware Random Access to not work since the AMF does not know the purpose of a NSAG (i.e. whether it applies to RACH or Cell reselection purposes, or both), so it cannot know for which NSAG it should not provide the priorities. Hence the AMF still has to provide to the UE all the NSAGs that match the UE subscribed S-NSSAIs to the UE, and then indicate it intends to disable Cell Reselection based on NSAG.
The selective disabling of Slice-aware Cell reselection and RACH can be justified by e.g. inbound roamers being treated differently (e.g. the RACH resources for a slice are reserved just for the Homers and only inbound roamers from specific PLMNs). This disabling can only be achieved by explicitly indication when the UE is configured with the NSAG information
Selective disabling of one of the Slice aware Random access or Cell reselection for a UE can be achieved by explicit indication. Disabling of both features for a UE can be done by not configuring any NSAG info for the UE

## Slide 27
Selective Disabling of slice-aware RACH configuration or
Cell Reselection proposed updates

## Slide 28: How NR_Slice_Core feature works (updated with NOKIA view)
AMF: provides and updates the UE with NSAG info (Network slice Access Stratum Groups based on TA where the UE is and the Subscribed S-NSSAIs priority information for the S-NSSAIs of HPLMN) in Registration Accept and UE Configuration Update Command. The NSAG info is about NSAGs which are defined in the serving PLMN, but includes also the Subscribed S-NSSAIs priority for S-NSSAIs HPLMN mapping to the S-NSSAIs of the VPLMN that belong to the NSAGs.
NSSF: can determine the NSAGs in NSAG info
UDM: Provides the subscribed S-NSSAIs priorities to the AMF
RAN: broadcasts the NSAGs applicable to a RACH pool in SIB1 and provides the cell resection Slice specific Cell Reselection Priorities via SIB 16 or RRC Connection Release. Informs the AMF of the support of NSAGs per TA and the which S-NSSAIs belong to a NSAG.
UE: Receives the NSAG Info from the AMF and based on this and:
Based on the information provide by the RAN in SIB1 can determine the RACH pool to be used.
Based on the Information in SIB16 (non-UE-specific) or, if applicable, RRC connection release (UE-specific) decides which cell to reselect and camp on.
UE
NG-RAN
AMF
NSSF
UDM
new