## Slide 1
3GPP TSG-SA WG2#152E e-meeting S2-2206843
Elbonia, 17 – 26 August 2022
Source: Qualcomm Incorporated
Title: Motivation for New TEI18 WID on Differentiating QoS for QUIC using Connection ID
Document for: Discussion/Information
Agenda Item: 10.4
Work Item / Release: TEI18 / Rel-18

## Slide 2: Introduction
IETF QUIC is a standard IETF protocol (RFC9000)
All major browsers, web server, and CDN have QUIC implementations
QUIC is growing quickly and accounted for 20% of Internet traffic (as of August 2021)
QUIC functions
  Connection+Stream multiplexing
  TLS1.3 (messages)
  Loss recovery
  In-order delivery (within stream)
  Congestion control, Flow control
  IP+UDP performs more like IP, i.e., identify endpoints

## Slide 3: Use Case(s)
Growing trends of supporting low latency applications such as game streaming over web browser (e.g., xCloud, GeForceNow, Stadia)
New framework is being worked on as WebTransport as evolution of WebRTC
5G is not well equipped to provided QoS to QUIC flows due to lack of visibility (encryption) in the header
  Only some streams in a connection may need QoS
  QoS requirement for each stream may be different (e.g., audio vs video vs control)
5G Support for Low Latency Applications over QUIC

## Slide 4: QUIC Stream Feature
Most fields in QUIC header are encrypted except for Destination/Source connection ID
Stream MUX
  One Connection ID can multiplex multiple streams
  No blocking between streams
  Streams can be added/removed independently
  Streams also be dependent of another stream (e.g., removal of parent stream -> dependent)
  Independent flow control on each connection and stream

## Slide 5: 3GPP QoS
3GPP typically uses 5-tuple to identify a flow:
  <Source IP, Destination IP, Source port, Destination port, Protocol ID>
At QUIC layer each stream can be identified by a unique Connection ID, but they will all share the same 5-tuple
E.g., a Video Telephony application may use 3 streams within one QUIC session
  One stream for signaling
  One stream for audio
  One stream for video
If an application is using QUIC as its transport, current Packet Filter Set attributes are not enough to identify specific QUIC streams and separate in different QoS flows with differentiated QoS.
This differentiation is important since:
  Only some QUIC streams in a connection may have stringent QoS requirements.
  QUIC requirements for each stream may be different (e.g. audio vs. video vs. control).

## Slide 6: Proposed enhancement
Enhance the 5G core network and NAS protocol to be able to identify and provide differentiated QoS for different QUIC streams within a same PDU session.
Objectives for this work item consist of:
  Include "QUIC source connection ID range" and "QUIC destination connection ID range" as attributes for Packet Filter Set definition.
  Exchange of QUIC connection ID packet filter support capability.
  Enhancement to Reflective QoS to create packet filters based on source/destination connection ID when QUIC applies.
Packet Filter:
  Different QoS flows for different QUIC source/destination connection IDs.
  Each QoS flow assigned QoS requirements accordingly.
  New value for Protocol ID / Next Header: “UDP+QUIC”
Reflective QoS:
  When Protocol ID / Next Header is set to "UDP+QUIC", UE uses the source and destination IP addresses, source and destination port numbers, the Destination connection ID and if present the Source connection ID of QUIC header.