## Slide 1
Pre-CC for SA2#154-AH-e
Discussion on R2-2213351 LS on PDU Set Handling
vivo

## Slide 2: QoS flow mapping for a given XR flow(e.g. video bitstream)
The QoS flow mapping for a XR flow is not only related to the PS importance, but mainly about PS QoS. We have considered different PDU Sets for a given XR flow can have different PS importance. But whether different PDU Sets for a given XR flow can have different QoS hasn’t been discussed yet.
Whether I frame/slice has different QoS requirement from the other frame/slice for a given XR frame? E.g.
    PSER: whether PDU Set(with I frame/slice) has higher PSER? E.g. if it is failed, the other frame referring to it can not be decoded.
    PSDB: same for a XR flow?
    Other QoS requirement(e.g. Resource type (Non-GBR, GBR, Delay-critical GBR); Averaging window)?
      Can a XR flow be mapped to GBR QoS flow?
  If yes(i.e. different PDU Sets for a given XR flow can have different QoS), whether those different PDU Sets for the XR flow is mapped to different QoS flows respectively?
Mapping
In order to decide how PDU sets could be mapped in radio protocols, RAN2 is wondering if different PDU sets could have different characteristics (for instance importance, PSER, and/or PSDB) and if so, which characteristics can be different and with which granularity (e.g. QoS flow, individual PDU Sets…).
RAN2 would also like to know whether different types of PDU set can be mapped to the same QoS flow and if so whether RAN should have the ability to treat those differently over the air interface. If RAN should have such an ability, RAN2 would like to know based on what information signalled to the gNB this would be based on.

## Slide 3
Thank You!