## Slide 1: Determination of Alternative S-NSSAI
Samsung

## Slide 2: Slice Replacement
Case A: notification of old S-NSSAI & determination of Alt S-NSSAI
  (AM-PCF, NSSF, both) notify to the AMF, the old S-NSSAI (i.e., S-NSSAI that needs to be replaced) + the Alternative S-NSSAI
Case B: notification of old S-NSSAI (B1), determination of Alt S-NSSAI (B2)
  B1: (AM-PCF, NSSF, both) notify to the AMF, the old S-NSSAI
  B2: (AM-PCF, NSSF, both) provide to the AMF, the Alternative S-NSSAI when queried by the AMF with the old S-NSSAI
What needs to be discussed:
  Either AM-PCF, NSSF, or both for each functionality

## Slide 3: DISCUSSION
Alternative S-NSSAI determination
  NSSF
    (+) Less signaling (signaling per S-NSSAI)
    (-) All PDU Sessions from all UEs in the S-NSSAI needs to be moved to the single S-NSSAI
  AM PCF
    (+) fine-grained steering (per UE). operator policy-based steering
    (-) More signaling (signaling per S-NSSAI per UE)
Notification on the old S-NSSAI
  NSSF
    (+) vNSSF/hNSSF interface can be used for the HPLMN old S-NSSAI for roaming UEs
    (-) All PDU Sessions from all UEs in the S-NSSAI needs to be moved to the single S-NSSAI
  AM PCF
    (+) fine-grained notification (old S-NSSAI per UE)
    (-) no interface between HPLMN/VPLMN to notify the HPLMN old S-NSSAI for roaming UEs

## Slide 4: Proposal
For the slice replacement for S-NSSAI in Serving PLMN:
  Case A
    AM-PCF notify to the AMF, the old S-NSSAI and the Alternative S-NSSAI
  Case B
    B1: AM-PCF or NSSF notify to the AMF, the old S-NSSAI
    B2: AM-PCF provides to the AMF, the Alternative S-NSSAI when queried by the AMF with the old S-NSSAI
For slice replacement for S-NSSAI in HPLMN for roaming UEs:
  Case A not supported
  Case B1. hNSSF notifies to the V-AMF (via vNSSF) of the S-NSSAI that needs to be replaced.
  Case B2. The AMF (or AM PCF) can determine Alternative S-NSSAI based on local configuration (or roaming agreement)