## Slide 1: 5GS Assistance for Federated Learning Member Selection
3GPP TSG-SA2 Meeting #155 S2-2302773
Athens, Greece, February 20 – 24, 2023
OPPO, Oracle, Toyota, Sony

## Slide 2
Federated learning based trajectory prediction-Application scenarios description
Each vehicle is trained locally based on the local data. The FL server is responsible for the distribution and aggregation of the global model. The specific procedure is described as follows:
The total training delay constraint is T. At the beginning of the round of FL, the server sends the current global model to the arriving vehicles.
The vehicle receives the model and uses it as its own initial local model, and then iteratively updates the local model H times based on local data to get updated local model and uploads it to the server.
At the end of the round, the server performs a weighted average of the local models collected in this round to obtain the updated global model.

## Slide 3
Simulation analysis- Dataset
Miami (MIA) dataset: historical trajectory data collected from the vehicles in Miami;
Pittsburgh (PIT) dataset: historical trajectory data collected from the vehicles in Pittsburgh.

## Slide 4
Simulation analysis
Model trained on the MIA dataset achieved good results on the PIT validation dataset.
The result shows that model training on a more diverse dataset with more geographic location features can effectively improve the model generalization and expand the applicable area of the model.

## Slide 5
5GS assisted FL member selection- Criteria: UE current and historical location
Definition
FL Coverage Area: The coverage area that the specific FL server applies the training.
Model’s Applicable Area: The area that the FL trained model can apply.
Historical Nomadic Period: The historical nomadic period is referred to the minimum duration that the UE was roving within the visited AoI.
Target Area of Interest (AoI): The target AoI which is beyond the FL coverage area but is within the model’s applicable area.
Information exchanges
AF to 5GS (input criteria):
FL coverage area (UE current location)
Target geographical area (UE historical location)
5GS to AF(candidate UEs):
5GS selects the in-coverage UEs coming from the target area and have moved into the target area during historical nomadic period.

## Slide 6: Criteria: UE Direction and separation distance
Vehicles can only move on the road which makes that geographically close vehicles tend to have similar data sets from in-vehicle cameras or sensors.
To avoid to select these nodes with similar data sets for FL training, 5GC needs to ensure that the distance between each candidate UE provided to the FL server is adequately apart.
As shown in the figure, car1 and car2 are running at different direction on the road and may have different data sets from in-vehicle camera. For location based FL member selection, this situation need to be considered

## Slide 7: Assistance information for federated learning
The data set of a single UE generally cannot represent the characteristics of the applicable area for model training. With assistance from 5GS, Federated Learning can collect multiple representative UE data sets to form a integral data set for model training in the applicable area
Candidate UE selection based on certain filtering criteria requested by the 3rd party
Model’s applicable area
Model’s applicable area
Unsuitably collected multiple UEs’ dataset
Effective UEs’ dataset representing model applicable area
UE current location | Indicate the certain area that the selected UE appears
UE historical location | Indicate the certain area that the selected UE appeared in a historical period of time
UE direction | Indicate the selected UEs should include different moving direction
UE separation distance | Indicate the selected UEs should comply with a minimum separation distance with each other

## Slide 8: Criteria: UE latency performance
The left picture shows the training convergence with different FL scheduling strategy (potentially with 5GS assistance)
  FC: An efficient scheduling algorism with a good tradeoff between the latency per round and the number of rounds.
PF: Schedules N=3 devices with the best latency performance at the moment out of all M devices
To achieve the best FL performance (i.e. FC), the right picture shows a intermediate training result per round regarding UE number, selected UE ids)
(Reference: TWC-2021 Joint Device Scheduling and Resource Allocation for Latency Constrained Wireless Federated Learning)
Dynamic UE scheduling helps to accelerate FL training a lot;
UE selection based on real-time network resource measuring helps for FL member determination;

## Slide 9: Specific procedure for the 5GC assistance to Member selection