## Slide 1: Discussion on 5GC enhancement for satellite access Phase 3
China Telecom

## Slide 2
SA1
  Stage 1 of 5GSAT (5GSAT) (R17)
  Guidelines for Extra-territorial 5G Systems (FS_5GET)(R18)
  5G system with satellite backhaul(R18)
  Stage 1 Study on satellite access - Phase 3 (R19) Normative phase is about to complete at Nov 2023
Overview on satellite related work in 3GPP
SA2
  Study on architecture aspects for using satellite access in 5G (FS_5GSAT_ARCH) (R17)
  Integration of satellite components in the 5G architecture (5GSAT_ARCH) (R17)
  Architecture support for NB-IoT/eMTC Non-Terrestrial Networks in EPS(R17)
  Study on Integration of satellite components in the 5G architecture - Phase 2 (R18)
  5GC/EPC enhancement for satellite access Phase 2 (R18)
  Study on 5G System with Satellite Backhaul (R18)I
  5G System with Satellite Backhaul (R18)
RAN
  Solutions for NR for NTN(R17)
  NR NTN enhancements(R18)
  IoT NTN enhancements(R18)
  Study on requirements and use cases for network verified UE location for NTN in NR(R18)

## Slide 3: New requirements from R19 SA1 study
Study on satellite access - Phase 3 (TR 22.865)
  GNSS independent operation to allow the satellite access and services for UE without GNSS receiver or with no access to GNSS service.
  Communication between UEs under the same satellite’s coverage regarding latency, e.g. phone call, data, LAN communication.
  The requirements about position that can be satisfied via NTN access, e.g. different position methods negotiation.
  To support delay tolerant communication service via satellite with intermittently/temporarily unavailable connectivity. Potential requirement is store and forward operation.
Study on Upper layer traffic steer, switch and split over dual 3GPP access (TR 22.841)
  Service requirements related to steering, splitting and switching of user data across two 3GPP networks which could use two different satellite NR access or one satellite NR access and one terrestrial access.
Most of above requirements can be considered as input to R19 study on 5GC enhancement for satellite access.

## Slide 4
U2N relay via satellite access
Gaps and objectives
3GPP has standardized general procedures for U2N relay, but it is not satellite access specific. Some enhancement needs to be studied to support satellite access :
Authorization for remote UE to connect U2N relay via satellite access.
U2N Relay Discovery for support of satellite access
Mechanism to support QoS of U2N relay in case of satellite access
U2N Relay enhancement to support QoE of relay service considering discontinuous satellite coverage
Mobility management of relay UEs and the remote UEs connected to the relay UE between a 5G satellite access network and a 5G terrestrial network, and between 5G satellite access networks.
Justifications and requirements
The scenario and benefit of relay UE with satellite access has been studied at 3GPP, e.g. in TS 22.261, TR 22.865, to utilize the coverage of satellite for the remote UE which may not able to access satellite directlly

## Slide 5: Service provision for UE without GNSS
Justifications and requirements
The scenario and requirement of providing satellite access and corresponding services to UE without GNSS was studied in TR 22.865, particularly to support vertical (e.g. IoT) and other usages (e.g. MBB for videosurveillance). UE without GNSS but supporting other different 3GPP positioning technologies is also included.
Gaps and objectives
Currently 3GPP satellite access and procedures assumes User Equipment rely on GNSS and service. It is not studied how to provide satellite access and corresponding services to UE without GNSS.
Objective 1: How to determine and provide to UE corresponding services allowed by the regulatory requirements and the operator’s policy in case of different location precision related to other different 3GPP positioning technologies supported by UE.
Objective 2: How to determine and provide corresponding services to UE if the UE dose not support other 3GPP positioning technologies, e.g. by utilizing trusted source.
  Objective 3: How to support roaming case.

## Slide 6: Mobility management enhancement for discontinuous satellite coverage
Justifications and requirements
The issue of Discontinuous satellite coverage was identified and studied at R18. To enable efficient paging and power saving, Registration and mobility management are considered to be enhanced.
Gaps and objectives
R18 SAT_ph2 has standardized some new features to handle the issue of discontinuous satellite coverage. It assumed the UE or 5GC has satellite coverage availability information which in practice may be unavailable for all cases, e.g. not standardized. There are also some topics leftover which need further study:
Objective 1: Enhancement on Registration and mobility management, e.g. Efficient Registration Area allocation and paging considering discontinuous coverage.
Objective 2: Enhancement on connection management to save power, e.g. Whether the UE can be in CM-connected with RRC inactive when there is no satellite coverage.

## Slide 7: Low latency call between UEs via satellite backhaul
Justifications and requirements
The scenario and benefit of Low latency phone call between UEs via satellite without going through the ground network is studied at TR 22.865. It applies to UE directly accessing a satellite which is assumed to use Regenerative payload. This scenario is also valuable if the UE accesses gNB which connects 5GC using satellite as backhaul.
Gaps and objectives
In R18 WI SATB it has standardized for UE to UE data forwarding via UPF on satellite as backhaul. It is for general application between UEs but not for IMS call. Considering IMS is internal system inside 3GPP network and the two UEs may register in the HPLMN or a VPLMN, or different CSCFs in a PLMN, it needs to study how to handle the issue of IMS call between UEs. It assums impact on IMS.
Objective 1: How to determine two UEs in the call are available for satellite path.
Objective 2: How to trigger and setup satellite path for communication between UEs.
Objective 3: How to support roaming case.

## Slide 8: Dual NR access including satellite
Justifications and requirements
Multi 3GPP connectivity including satellite access has been studied at 3GPP, e.g. in TS 22.261, TR 22.841, TR 38.821, to meet the performances on data rate and/or reliability.
Multi access is the prerequisite for implementing Multi 3GPP connectivity. The UE needs to simultaneously register over two 3GPP access including satellite access and support corresponding mobility management, then the UE can establish and move PDU session(s) or utilize ATSSS like features between two access
Gaps and objectives
3GPP dose not support dual NR, more specifically a terrestrial NR and a satellite NR.
Considering satellite access brings complexity and latency issue comparing terrestrial access, it is worthy to study how to simplify the Registration and mobility management, service request mechanism at one access(e.g. satellite) when UE connects to both accesses.
  Mechanism for Registration, mobility management and service request designed for a 3GPP and a non-3GPP access may be a reference.

## Slide 9: S&F operations under Transparent mode
Justifications and requirements
The requirement of delay tolerant communication service using satellite with discontinuous feeder link was studied at TR 22.865. Potential mechanism is Store and Forward (S&F) operations similar as SMS.
For Transparent mode, S&F operations could still work if the satellite and NG-RAN could collaborate to store and receive the UL data via the discontinuous feeder link.
Gaps and objectives
How to authenticate and enable S&F operations in UE and 5GS.
How to support S&F operations in UE and 5GS, with considering enhanced Connection management and Session management.
It assumes RAN to study the mechanism of sending UL packet to satellite and subsequent forwarding stored UL packet to NG-RAN under different feeder link status.
Corporative work between RAN and SA2 is forseen.

## Slide 10: Regenerative Mode
10
Justifications and requirements
Comparing to Transparent mode, Regenerative mode has the advantages of lower communication latency, fewer ground stations deployment and flexible satellite networking.
Regenerative mode was studied at R16&R17 in TR23.737 but not cover all possible aspects and was not concluded.
Gaps and objectives
How to support RAN mobility including handover and the impact to N2 and N3.
Mobility management and Session management with moving RAN node.
The mobility of 5GC NFs onboard the satellite and the impact to 5GC architecture.
How to resolve the QoS issue of variable delay, end-to-end loss and disordering of user plane packet because of moving RAN, 5GC NFs and ISL.
Since Regenerative mode has strong RAN dependency, it needs corporative work between RAN and SA2.

## Slide 11: Proposed objectives for R19 SID (FS_5GSAT_Ph3)
U2N relay via satellite access
  Enhancement on Authorization, Discovery, QoS/QoE and Mobility management, to support U2N relay service via satellite access.
Service provision for UE without GNSS
  Position and corresponding services determination&provision for UE without GNSS, considering different positioning technologies precision or other technologies.
Mobility management enhancement for discontinuous satellite coverage
  Further enhancement on Registration, mobility and connection management for discontinuous satellite coverage based on R18.
Low latency call between UEs via satellite backhaul
  Enhancement on 5GC and IMS to support Low latency call between UEs via satellite backhaul using onboarding UPF.
Dual NR access including satellite
  Enhancement on Registration and mobility management to support dual NR access including satellite, e.g. to simplify the corresponding process on satellite access.
S&F operations under Transparent mode
  Enhancement on Registration, Connection and Session management, to support store and orward operations under under different feeder link status. It has RAN dependency.
Regenerative Mode
  5GC architecture enhancement and optimiaztion to support RAN and NFs mobility, including handover, Mobility management and Session management, and QoS issue.

## Slide 12
Thank you!