## Slide 1: Minimize the number of Policy Associations
Belen Pancorbo
Ericsson

## Slide 2: Outline
PCC authorization:
  The SMF determines based on local configuration whether PCC authorization is required for the PDU Session, then requests to establish a SM Policy Association to the PCF.
AM Policies:
  The AMF also determines based on local configuration where AM Policies are needed, this local configuration,
The problem is that some AM and SM Policy Association may be established and maintained until the UE deregisters or the PDU Session terminates, although there are no policies for this SUPI (DNN and S-NSSAI). This impacts performance and increases signalling.
UE Policies:
  The AMF triggers the UE Policy Association using the UE policy container, if not present, then the AMF triggers, based on local configuration, the UE Policy Association Establishment procedure to the PCF to request UE Policies, if any.
The problem is that the AMF triggers the request for UE Policies without knowing if the UE needs UE Policies or not, for example some IoT devices may not need any UE Policies. For those UEs that do not need any UE Policies, the UE Policy Association remains established, that impacts the performance and causes extra signalling between the AMF and the PCF.

## Slide 3: Solution described in the TEI19 WID
Extend Access and Mobility Subscription Data Types used in the Nudm_SubscriberDataManagement Service and defined in TS 23.502 18.1.1 Table 5.2.3.3.1-1.
  New Field: Indication of Access and Mobility Policies enabled.
  Description of the new Field: Indicates if the user has Access and Mobility Policies enabled or not.
  New Field: Indication of UE Policies enabled.
  Description of the new Field: Indicates if the user has UE Policies enabled or not.
Extend Session Management Subscription Data Types used in the Nudm_SubscriberDataManagement Service and defined in TS 23.502 18.1.1 Table 5.2.3.3.1-1.
  New Field: PCC authorization is enabled.
  Description of the new Field: Indicates if the user has PCC authorization enabled for the PDU Session.
DM to include a new explicit indication of whether the UE/SUPI is required/authorized/allowed to receive UE policies, the AMF may be able to infer whether the UE/SUPI is required to receive UE policies based on existing subscription data.

## Slide 4: Solution described in the TEI19 WID
Extend AM Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.1.2
  Step 1, AMF decision is based on local policies and the indication of whether the SUPI has AM Policies enabled.
Extend UE Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.11
  Step 1, AMF decision is based on local policies and the indication of whether the SUPI has UE Policies enabled.
Extend SM Policy Establishment procedure defined in TS 23.502 18.1.1 clause 4.16.4
  Step 1, SMF decision is based on local policies and the indication of whether the PDU Session of this SUPI has PCC authorization enabled.
DM to include a new explicit indication of whether the UE/SUPI is required/authorized/allowed to receive UE policies, the AMF may be able to infer whether the UE/SUPI is required to receive UE policies based on existing subscription data.