## Slide 1: Motivation on study to support ProSe direct/indirect communication for IIOT and private networks Lenovo
Release 19 study proposal
S2-2306675

## Slide 2: Introduction
Stage 1 requirements for Direct and Indirect communication for industrial automation are described in 3GPP TS 22.104 and accommodate for the following features
  Network performance requirements for periodic deterministic communication (both unicast and multicast) related to KPIs for corporate carrying use cases
  Requirements for clock synchronisation (working clock domain)
For Industrial IIoT use cases, the following Stage 1 requirements described in 3GPP TS 22.104 for supporting direct device communication are of importance in stage 2 (further details in Clause 7 of 22.104).
  Support direct device connection between a group of UEs for periodic deterministic communication (both unicast and multicast) with respective service performance requirements in Table 5.2-1 related to cooperative carrying
  Support clock synchronization (working clock domain) between the UEs within the group of UEs using ProSe direct device communication.
  NOTE: Similar requirements are also specified for ProSe indirect communication (clause 8, 3GPP TS 22.104).

## Slide 3: Study proposal
Propose to agree on a study to support ProSe Direct and Indirect Communication to support the Industrial IoT use cases and requirements described in 3GPP TS 22.104
Main focus of the study:
  Identify enhancements needed to support of ProSe Direct/Indirect Communication in private networks (SNPN and PNI-NPN)
    It is expected that IIoT use cases require deployment of private networks.
  Identify enhancements needed in scenarios where 5GS is deployed as a layer-2 ethernet bridge when integrated with IEEE TSN network in order to support:
    Clock synchronization of a common working clock between a group of UEs using ProSe Direct/Indirect Communication
    TSN stream communication via ProSe Direct/Indirect Communication

## Slide 4: Objectives – Work Tasks
  The following work tasks are identified for this study:
  WT 1: Identify enhancements needed to support ProSe Direct/Indirect communication in private networks (SNPN and PNI-NPN).
    For PNI-NPN network identify enhancement to support ProSe direct and indirect communication in conjunction with closed access groups.
  WT 2: Identify whether and how enhancements are needed (incl. configuration of UEs, PC5 QoS enhancements) for conveying deterministic communication streams via a ProSe Direct/Indirect Communication.
  WT 3: Clock Synchronization
    WT 3.1: Identify whether and how enhancements are needed (incl. configuration of UEs, PC5 QoS enhancements) for supporting clock synchronization of a common working clock between a group of UEs using direct device connection ProSe communication.
    WT 3.2: Identify whether and how enhancements are needed (incl. configuration of UEs, PC5 QoS enhancements) for supporting clock synchronization (working clock domain) for UEs using ProSe indirect network connection.
  For all scenarios consider out-of-coverage, partial coverage and in-coverage cases.
  Coordination with RAN is expected (e.g. for QoS aspects)
  Expected TUs: 4 (3+1)

## Slide 5: Example topics to study – Clock Synchronisation
Consider clock synchronisation solutions where a group of UEs using direct device communication are all in coverage, partial coverage or out of coverage.
For scenarios where clock distribution can be supported via the direct connection the following need to be resolved:
  How UEs determine that 5GS clock needs to be distributed over ProSe direct communication?
  PC5 QoS parameters required to be supported for distributing clock information
  Whether a UE can use its internal clock for clock distribution (e.g. if UE(s) are out of coverage)

## Slide 6: Example topics to study – TSN stream via direct connection
UE sends TSN stream information over user plane via a direct connection to a second UE
Include both in-coverage, out-of-coverage and partial coverage scenarios
What needs to be studied:
  How UEs determine that TSN stream is sent over direct communication?
  How UEs determines PC5 QoS requirements over direct device connection for conveying TSN stream
  Architecture to support TSN stream communication via direct connection (e.g. use of UE-NW relay)