## Slide 1: Solution proposal for PIN to resolve Editor’s notes
vivo

## Slide 2: One PIN multiple PDU Sessions of a PEGC
Support with following principles
  A new ID (e.g., PIN Traffic ID) instead of PIN ID is used for URSP rule, which is not used to identifying PIN but for traffic mapping. The URSP rule for PIN is provisioned by 5GC, may be according to the information from AF, e.g., 4.15.6.7/10 of TS 23.502
    From UE perspective, there’s no difference between URSP rule with a PIN Traffic ID and URSP rule with PIN ID
  PIN is managed and identified by PEMC or AF transparently to 5GS, a PIN can be managed with multiple groups in application layer, each group is identified by an External/Internal GID, 5GC only manages the subscription data related to External/Internal GID (e.g., Group Data) and is not aware of the PIN
  Followings are out-of-SA2 scope
  It is application layer that AF interact with PEMC/PEGC to negotiate the meaning of the new ID per PIN (i.e., mapping between ID and Service Info, service info could be DNN, Domain descriptors, source/destination IP/non-IP descriptors, etc.). The mapping info also may be configured to PINE, so that PINE knows how to send the traffic for different service
  It is implementation aspect that how PEGC maps the PINE traffic with Service ID, e.g., based on different IP address of the PINE, different tunnel, and/or different SSID/BT ID, etc. An example is that a PINE accesses WiFi for internet and other/same PINE accesses BT for IMS.
  Revise CR4224 (S2-2306176, PDU Session mapping)
  Revise CR4287 (S2-2306178, Identifiers for PIN) to include 5.44.2 (UE policy delivery for PIN) that PIN Traffic ID in TD of URSP rule
  New CR to revise 6.6.2.1 of 23.503 accordingly

## Slide 3: Procedure and UDM subscription data
AF#1 and AF#2 are optional, which means steps 0a, 1a, and 2a are optional, pre-configuration in UDM/UDR can be used
AF#1 (for PIN subscription) and AF#2 (for PIN management) may not be same. There’s a case that operator only deploy AF#1 for PIN subscription, while AF#2 for PIN management is a third party AF, who is not able to manage subscription
In order to indicate PCF the URSP rule for application traffic using (DNN, S-NSSAI) of PDU Session for PIN shall not be generated to avoid application traffic of PEGC transferring over PDU Session for PIN, the “PIN communication indication” is included in Group Data
SMF applies PIN communication instead of 5G VN group communication to support device-2-device and device-2-DN communication
New CR to revise 5.29.2 of 23.501 to describe handling of the “PIN communication indication”
New CR to revise 4.15.6.3b of 23.502 to include “PIN communication indication” in Group Data, and revise 4.15.6.10 of 23.502 to enable URSP guidance for PIN

## Slide 4: Local switch (support device-2-deivce communication)
Communication between PEMCs and PEGCs of a PIN, e.g., for PIN management, is enabled by reusing 5G VN group communication feature without extension. (except new decision is made during the meeting that PEGC application traffic is allowed to be routed over the PDU Session for PIN)
5G VN local switch in 5.8.2.13.1 of 23.502 is based on UE IP address and CN tunnel info, which means the local switch is full-meshed among UEs, while PINE-PINE indirect communication is not full-meshed among PINEs and may be based on PINE IP address, extension for PIN is needed
PINE-PINE indirect communication via 5GS needs to be configured by SMF to UPF according to input, e.g., from AF
  Text described in 5.44.3.2: “An AF supports PIN service may also influence traffic routing for PDU sessions for PIN traffic”
In order to support PINE-PINE indirect communication via 5GS, SMF may reuse local switch mechanism for 5G VN with addition that Source and Destination Address are included in PDRs described in clause 5.8.2.13.1, whose values are set according to Traffic Description received by SMF, e.g., as described in clause 4.3.6 of 23.502
Revise CR4326 (S2-2304887, PEMC handling) to add NOTE that PEMC-PEGC communication reuses 5G VN group communication
Revise CR4450 (S2-2306180, 5.44.3.2 Session management) to describe device-2-device/DN communication configuration that PDR/FAR may be used, and if used, Source and Destination Address are included