## Slide 1: Way forward for packet loss during multicast MBS delivery solutions
Huawei, Hisilicon

## Slide 2
Solutions on the table
Solutions | Key points | Packet loss? | Latency introduced * | Impact to the NFs/services
Option 1 – Buffer at UPF | buffering at the MB-UPF can be applied sufficiently long for the majority of RAN nodes to activate the MBS session to reduce packet loss | Depends on the length of the buffer timer and the implementation of MB-UPF. | Yes - Depends on the length of the buffer timer, which is an implementation of MB-UPF. | No impact to the NFs It is a per MB-UPF node implementation, which may impact other services.
Option2 – AF indicating non-inactive MBS session | The AF indicates the MBS session can not becomes inactive | Yes. UP data which triggers the RAN paging can be lost. The UE can still becomes RRC_Inactive. | Yes. If UE becomes RRC Inactive, then RAN-paging is needed and corresponding latency (e.g. buffer at RAN)is introduced. | Option 5QI no. Option AF Indication: AF, NEF, MB-SMF.
Option 3 – exposing multicast MBS session status to the AF | Using the existing MB-SMF API to expose the multicast MBS session status | No. Firstly send notification to the AF and get the ACK, then set the MBS session to inactive (similar like the early notification in edge) | Buffering at the network and the AF is the same | AF, NEF, MB-SMF AF is assumed to activate the MBS session via CP before sending the data, if such MBS session is inactive.
*Latency is not a big issue, since even for unicast, some of the UEs have to experience such latency
*Packet loss is the key concern from SA6

## Slide 3
SA6 requirements from 22.179
[R-6.15.3.2-016] There shall be no (0 ms) initial lost audio at receiving user.
[R-6.15.3.2-017] There shall be no (0 ms) trailing lost audio at the end of the voice burst at receiving user.
Variable | Meaning | Value | Reference
KPI 1 | MCPTT Access time | < 300 ms | 6.15.3.2
KPI 2 | End-to-end MCPTT Access time | < 1000 ms | 6.15.3.2
KPI 3 | Mouth-to-ear latency | < 300 ms | 6.15.3.2
KPI 4a | Maximum Late call entry time (without application layer encryption) | < 150 ms | 6.15.4.2
KPI 4b | Maximum Late call entry time (with application layer encryption) | < 350 ms | 6.15.4.2
Compared with latency, the packet loss is the most critical requirements for public safety/SA6

## Slide 4
Way forward
Option 1 – Buffer at UPF:
  With no system impact.
  Trade-off between packet loss and latency;
  Acceptable solution if slight delay is not a big deal for public safety.
Option 2 – AF indicating non-inactive MBS session:
  With system impact
  Energy saving is based on RRC Inactive – but that may cause additional packet loss (UP-triggered RAN paging).
  Smaller delay compared with option 1 and option 2.
Option 3 – exposing multicast MBS session status to the AF
  With system impact
  Packet loss can be addressed if AF activate the MBS session before hand.
  Preferred solution
Due to packet loss is the key concern from SA6, Option1 and Option2 both cannot fully solve the packet loss issue. It is proposed to agree Option 3.

## Slide 5
Thanks