## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: PIN ID is used alone in URSP TD, a PIN may be associated with only one Group ID in 5GC. The Group ID is associated with only one (DNN, S-NSSAI) combination, AF can provide PIN ID associated with the (DNN, S-NSSAI) for the PIN (Do not support 1:* mapping) (S2-2306834, S2-2306735)
Option 2: Group ID is used alone in URSP TD, a PIN can be associated with multiple Group IDs in 5GC, each Group ID maps to a list of PEGC for a PIN. Each Group ID is associated with only one (DNN , S-NSSAI) combination, AF can provide different Group ID associated with different (DNN, S-NSSAI) for the PIN (support 1:* mapping) (S2-2306385, S2-2306384, S2-2306386, S2-2306387)
Option 3: PIN ID is used optionally together with IP/non-IP descriptors in URSP TD (support 1:* mapping) (S2-2306412)
Option 4: Based on option 1 with exception that an ID (not necessary to be PIN ID) is used alone in URSP TD (support 1:* mapping) (S2-2306712, S2-2306713, S2-2306720)
Q: Which option is preferred?
    Option 1: Yes: 6 No: 2
    Option 2: Yes: 1 No:
    Option 3: Yes: 4 No: 1
    Option 4: Yes: 5 No: 4
    Option 1: Yes: 11 (Working Assumption) No: 0
    Option 3: Yes: 4 No:

## Slide 3: Subscription data
Option 1: New single indication in existing subscription data: in Group Data (in case Group Data supported and used) for both SMF handling PDU Session for PIN and PCF handling URSP for PIN, as well as optionally (e.g., when Group Data not supported) in SM subscription data for SMF handling PDU Session for PIN and in UE context policy control data for PCF handling URSP for PIN (S2-2306652, S2-2307415, S2-2306719)
Option 2: New Two Indications in SM subscription data for SMF handling non-3GPP delay budget and for N3QAI separately (S2-2306725)
Option 3: New subscription data: New PIN subscription data is used (S2-2306413, S2-2306414)
Option 4: No enhancement for subscription data, (DNN, S-NSSAI) specific for PIN as subscription indication for PIN. (S2-2306836) + SMF behaviour for delay budget and non-3GPP QoS assistance information is determined based on DNN/SNSSAI (S2-2306718)
Which option is preferred?
    Option 1: YES: 5 NO: 2
    Option 2: YES: 2 NO:
    Option 3: YES: 5 NO: 2
    Option 4: YES: 5 NO: 3
    Option 1: YES: 5 NO:
    Option 3: YES: 3 NO:
    Option 4: YES: 9 (working Assumption) NO:

## Slide 4: End