## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: 5GC is aware of PIN member and PIN ID, PIN ID is used alone in URSP TD, a PIN is associated with only one Group ID in 5GC, the Group ID maps to full-group of PEGCs for a PIN and is an alias of PIN ID. The Group ID is associated with only one (DNN, S-NSSAI) combination (Do not support 1:* mapping)
Option 2: 5GC is aware of PIN member and PIN ID, Group ID is used alone in URSP TD, a PIN can be associated with multiple Group IDs in 5GC, each Group ID maps to a sub-group of PEGCs for a PIN. The Group ID is associated with only one (DNN , S-NSSAI) combination (support 1:* mapping)
Option 3: 5GC is aware of PIN member and PIN ID, PIN ID is used together with IP/non-IP descriptors in URSP TD (support 1:* mapping)
Option 4 (DEFAULT): Based on option 1 with exception that 5GC is not aware of PIN ID, PIN Traffic ID instead of PIN ID is used alone in URSP TD, a PIN can be associated with multiple Group IDs over application layer, each Group ID maps to a sub-group of PEGCs for a PIN. The Group ID is associated with only one (DNN, S-NSSAI) combination (support 1:* mapping)
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:
    Option 4: If no preference for options 1-3, option 4 is selected

## Slide 3: Subscription data
Option 1 (DEFAULT): Enhance existing subscription data
  Option 1.1 (DEFAULT): Indication in one place: in Group Data for both SMF handling PDU Session for PIN and AM-PCF handling URSP for PIN
  Option 1.2: Indication in multiple places (AF manipulates the indications shall be considered): Indication in SM subscription data for SMF handling PDU Session for PIN and UE context policy control data for AM-PCF handling URSP for PIN
    Alternative: Two Indications in SM subscription data for SMF handling non-3GPP delay budget and for N3QAI separately
Option 2: New subscription data: PIN subscription data (new) and new service operations used (S2-2306413, S2-2306414)
Q1: Whether Option 2 is preferred?
    YES: NO:
Q2: In case Option 2 is not selected in Q1, whether option 1.2 is preferred?
    YES: NO:
Q3: In case Option 1.2 is selected in Q2, whether the alternative of option 1.2 is preferred?
    YES: NO:
    (Default of option 1.2 is one indication in SM subscription data)

## Slide 4: End