## Slide 1: PIN: Way Forward for Open Issues
SA2#157

## Slide 2: Mapping between PIN and PDU Session of a PEGC
Option 1: PIN ID is used alone in URSP TD, a PIN may be associated with only one Group ID in 5GC, the Group ID maps to all PEGCs for a PIN and is an alias of PIN ID. The Group ID is associated with only one (DNN, S-NSSAI) combination, AF can provide PIN ID associated with the (DNN, S-NSSAI) for the PIN (Do not support 1:* mapping) (S2-2306834, S2-2306735)
Option 2: Group ID is used alone in URSP TD, a PIN can be associated with multiple Group IDs in 5GC, each Group ID maps to a list of PEGC for a PIN. Each Group ID is associated with only one (DNN , S-NSSAI) combination, AF can provide different Group ID associated with different (DNN, S-NSSAI) for the PIN (support 1:* mapping) (S2-2306385, S2-2306384, S2-2306386, S2-2306387)
Option 3: PIN ID is used together with IP/non-IP descriptors in URSP TD (support 1:* mapping) (S2-2306412)
Option 4: Based on option 1 with exception that an ID (not necessary to be PIN ID) is used alone in URSP TD (support 1:* mapping) (S2-2306712, S2-2306713, S2-2306720) In this option, PIN is an application layer concept, one PIN multiple PDU Sessions of a PEGC is over application layer, and one ID one PDU Session of a PEGC is in 5GC (same as option 1). A PIN may be associated with multiple Group IDs over application layer, each Group ID maps to a list of PEGC for a PIN. AF can provide different ID associated with different (DNN, S-NSSAI) for the PIN
Q: Which option is preferred?
    Option 1: Yes: No:
    Option 2: Yes: No:
    Option 3: Yes: No:
    Option 4: Yes: No:

## Slide 3: Subscription data
Option 1: Enhancing subscription data for PIN (application data in UDR also is enhanced to support storing of new traffic descriptor)
  Option 1.1: New indication in existing subscription data: in Group Data (in case Group Data supported and used) for both SMF handling PDU Session for PIN and AM-PCF handling URSP for PIN, as well as optionally (e.g., when Group Data not supported) in SM subscription data for SMF handling PDU Session for PIN and in UE context policy control data for AM-PCF handling URSP for PIN (S2-2306652, S2-2307415, S2-2306719)
    Alternative: Two Indications in SM subscription data for SMF handling non-3GPP delay budget and for N3QAI separately (S2-2306725)
  Option 1.2: New subscription data: New PIN subscription data and new service operations used (S2-2306413, S2-2306414)
Option 2: No enhancement for subscription data, (DNN, S-NSSAI) specific for PIN as subscription indication for PIN In this option, only application data in UDR is enhanced to support storing of new traffic descriptor (S2-2306836)
Q1: Which option is preferred?
    Option 1: YES: NO:
    Option 2: YES: NO:
Q2: In case Option 1 is selected in Q1, which sub-option is preferred?
    Option 1.1: YES: NO:
    Option 1.2: YES: NO:
Q3: In case Option 1.1 is selected in Q2, whether the alternative of option 1.1 is preferred?
    YES: NO:
    (Default of option 1.1 is one indication in SM subscription data)

## Slide 4: End