## Slide 1: Discussion about URSP over EPS (eUEPO)
Oracle
3GPP TSG-SA WG2 Meeting #158
Goteborg, Sweden, August 21 – 25, 2023
S2-2308554

## Slide 2
Slide #3 illustrates UE Policy Association Establishment on 5G side (taken from 29.513 for clarity’s purpose, however, reflects also 23.502 4.16.11)
Slide #4 illustrates URSP provisioning - E2E mobility from 5GS to EPS
Claim #1: (as shown in slide #3) during UE Policy Association Establishment on 5G side, the UE-PCF needs to:
  Check whether the UE Policy container includes indication of UE support for EpsUrsp (i.e URSP over EPS).
  Register itself in the BSF. Let’s denote this as (*)
  Store indication of UE support for EpsUrsp in the UDR, in case the UE Policy container has it. Let’s denote this as (**)
Justification for claim #1:
  2) Above (*) will enable step 5 in slide #4 – It seems to be already captured in 23.502 4.16.11 step 4 “…The (H-)PCF in roaming and the PCF in non-roaming may register to the BSF as the PCF serving this UE, if not already registered at the AM Policy Association establishment.” – so no CR is needed.
  3) Above (**) will enable step 4 in slide #4 - Seems to be missing.. Hence, a new CR is required to fix that (S2-2308551).
Claim #2: Both SM-PCF and UE-PCF need to store their ability to support EpsUrsp in the NRF (i.e URSP over EPS). Denoted as (***)
Justification for claim #2:
If (***) is not happening, then in slide #5 steps 2 and 8 the Discovery &selection of SM-PCF and UE-PCF by the SMF+PGW-C and by SM-PCF respectively will have to be done based on manual configuration or simply by getting lucky – either way would defeat the dynamic NRF mechanism. - Hence, a new CR is required to enable that (S2-2308550).
DP for URSP over EPS (by Oracle – 8/9/2023)

## Slide 3
29.513 Figure 5.6.1.2-1: UE Policy Association Establishment procedure - Non-roaming
Enhanced UE Policy Association Establishment on 5G side (Based on 23.502, 29.512, 29.525, 29.513)

## Slide 4
Note: The ‘E2E mobility’ scenario is not a subsequent scenario to ‘initial UE attach in EPS’. Hence, SM-PCF is not assumed to have yet an N43 association with UE-PCF for that subscriber.
URSP provisioning - E2E mobility from 5GS to EPS (Based on 23.502, 29.512, 29.525, 29.513)

## Slide 5
Initial URSP provisioning - E2E Initial Attach procedure in EPC (Based on 23.502, 29.512, 29.525, 29.513)

## Slide 6
Continue… Initial URSP provisioning - E2E Initial Attach procedure in EPC (Based on 23.502, 29.512, 29.525, 29.513)