## Slide 1: Consideration on DualSteer SID
Huawei, HiSilicon

## Slide 2: Outline
DualSteer
  Typical use cases for DualSteer in SA1
  Discussion and Analysis on the use cases
  Summary
ATSSS-lite
  Considerations
  Summary

## Slide 3: Typical Use Cases in SA1
Scenario 1：dual NR in same PLMN，both TN
Scenario 4：dual NR in different PLMN，both TN
Scenario 3：dual NR，including NTN
Scenario 2：NR + E-UTRA
Scenario 5：dual NR，PLMN + NPN

## Slide 4: Analysis on Use Cases in SA1
NR + NR (same PLMN)
Scenario: data is transmitted via dual NR in single PLMN and is anchored at CN to improve throughput (see TR 22.841--use case 12)
Considerations
  Since UE radio capability is shared by two RANs, no coordination between two RANs, leads to worse performance (need the evaluation by WG).
  Impact on secondary cell selection in both initial registration and mobility scenario
  Impact on RM and CM states since session both access are 3GPP access, it requires to have separate CM & RM states for each legs to manage the scenario that one or two accesses are available. Two independent states / NAS are needed.
  Impact on session management including policy and steering modes. If consider the additional N3GPP access leg, a new model of MA PDU session with three legs should be considered.
  DC/CA enable UE to use two radio for data transmission in which two RANs have well coordination and negotiation in terms of UE Radio capability, interference and radio resource allocation in order to meet the service requirement. Such solution does not have impact on RM, CM and SM.
  Conclusion: DC/CA can meet the service requirement of transmitting data via two NRs in single PLMN to improve throughput. Therefore, we do not see the need to study such scenario.
No UE capability coordination, “hard split” for two RAN
band combination, allowed feature set, power…
No interference coordination

## Slide 5: Analysis on Use Cases in SA1
LTE/EPC + NR/5GC
Scenario: data is transmitted via NR and LTE in single PLMN and is anchored at CN to improve throughput (see TR 22.841--use case 7/8 )
Considerations
  Any potential impacts in NR+NR listed in P4 also exist in LTE + NR.
  For traffic transmission over LTE+NR, DC has already supported it.
  For traffic switching between LTE and NR, currently dual-registration mode specified in TS 23.501 clause 5.17.2.3 can support UE to transfer the PDU session from 5GC to EPC or transfer the PDN connection from EPC to 5GC
  Conclusion: existing solution can meet the service requirements of transmitting the data via NR and LTE in single PLMN to improve throughput. Therefore, we do not see the need to studying such scenario.

## Slide 6: Analysis on Use Cases in SA1
Scenario 1: data is transmitted via NR and satellite to improve QoS (e.g. more throughput, less PER) or to achieve service continuity when NR coverage is weak. (see TR 22.841--use case 4/5/6] )
Scenario 2: split different services (e.g. latency tolerant or sensitive) in to different type of NR satellite e.g. LEO or GEO (see TR 22.841--use case 1] )
Considerations:
  Significant latency difference over TN and NTN or different types of NTN (~30ms for LEO and 280ms for GEO), which degrade the performance for packet splitting/aggregation because the latency will be dominated by the NTN leg. Additional cost for packet reordering is needed.
  NTN may not support the same QoS flow over NR (e.g. 5QI=10 is used for NTN), which is not aligned with the principle of access agnostic for QoS support in ATSSS.
  High latency communication happens due to discontinuous coverage of NTN and the UE is not reachable. Therefore, considering the high cost, high latency and low throughput over NTN, when the TN is available, we do not see the need to transmit the traffic over NTN access.
  For NTN+NTN, apart from having impacts on RM, CM and SM which are the common issues for UE registering to 5GC via two 3GPP access networks, we also need to consider the features in different types of NTN (e.g. discontinuous coverage or the potential features studied in SAT topic)
  Conclusion: The motivation to perform traffic aggregation, splitting and steering over dual NTN or TN+NTN is not clear. At present, we do not see the need to studying such scenario.
TN + NTN
NTN + NTN

## Slide 7: Analysis on Use Cases in SA1
Scenario 1: in roaming case, data is transmitted via two NR in two VPLMNs to improve throughput (see TR 22.841--use case 3)
Scenario 2: data is transmitted via NR in VPLMN and NR in HPLMN to improve throughput (see TR 22.841--use case 2/3/11)
Considerations:
Commercial value is not clear: when UE is in a single PLMN coverage, why it should select another PLMN for service transmission?
Impacts on UE network selection and cell selection when considering the slices.
Impacts on RM and CM. UE shall maintain two NAS state over the 3GPP accesses because two AMF will be involved in multiple PLMNs case.
Why not just use the DC/CA in the single VPLMN in roaming or the HPLMN in non-roaming? DC/CA in a single PLMN can still meet the requirement of transmitting traffic over two radio. What is the value of studying a such complicated solution which may not have better performance than DC/CA since there is no RAN coordination for UE radio capability sharing or radio resource allocation.
If multiple PLMNs are needed, why not using MUSIM, which enable UE to connect with two access networks belonging to two PLMNs, achieving the service requirements as indicated by the Use Case.
  Conclusion: At present, since DC/CA or MUSIM can meet the service requirement, we do not see the need to study such scenario where there are significant impacts on the whole 5G system.
VPLMN + VPLMN
VPLMN + HPLMN

## Slide 8: Analysis on Use Cases in SA1
Scenario：There is overlap coverage of PLMN and NPN in local area. Data is transmitted via NPN and PLMN to improve throughput or achieve service continuity. (see TR 22.841--use case 3/15)
Conclusion: Existing solution can meet the service requirements. We do not see the need to study such scenario.
NR (PLMN) + NR (SNPN)
NR (PLMN) + NR (PNI-NPN)
Consideration:
The scenario breaks the principle for SNPN because it requires roaming/interconnection architecture between SNPN and PLMN, making the SNPN no more “stand-alone”
MA PDU session over PLMN and PNI-NPN is not feasible for CAG only UE or PLMN only UE as they have no access to PLMN or CAG cell respectively. When UE establishes the MA PDU session over PNI-NPN and PLMN, the UE is in fact using dual NR over PLMN as only non PNI-NPN dedicated DNN/S-NSSAI can be supported over PLMN.
For SNPN+PLMN, TS 23.501 Annex D.6 provides solution for establishing MA PDU session over SNPN access network and PLMN access network, with one network acting as the N3GPP access of the other one.

## Slide 9: WT scope
Irrespectively from the scenarios the issue to be investigated the issue listed below. It should be noted that depending by the scenarios the detailed list of the problem to be solved may be different (e.g. TSN in satellite scenario not supported):
  How a UE can register via the same 3GPP access, in case of same RAT type (e.g. NR-NR), different RAT types (e.g. NT + NTN, NTN Geo – NTN Leo)
  Mobility and session continuity
  connection management
  Session management
  Slice aspects
  ES
  Location services support (impact on LCS)
  Various restrictions, e.g. service restriction, forbidden area, LADN
  Charging data reporting
  Network sharing
  Support of MBS (e.g. which is impact considering the N3mb to RAN, UPF & MB-UPF?)
  Support of Prose for UE-relay
  Impact on URLLC

## Slide 10: Summary
There is no demonstrated benefits to study any use cases in DualSteer since DC/CA or MUSIM in multiple PLMN case can achieve it.
Studying whole new mechanism for traffic transmission over two access networks and anchoring at 5GC will have significant impacts on 5G system, even probably causing degradation of performance. We do not see the motivation to study such complicated solution while the performance compared with DC/CA is not clear.
For LTE+NR, DC can achieve it. We do not see the gap.
For TN+NTN, traffic steering/splitting/aggregation is no needed. When TN is available, there is no benefit to steer traffic over NTN which will degrade the performance.
For multiple PLMNs or PLMN + NPN case, the commercial value is not clear and breaks the principle of NPN. Existing solution such as MUSIM or SNPN-PLMN interworking architecture can meet the requirement. We do not see the need to study such scenario.

## Slide 11: ATSSS-like proposal
WT-A-2C: Study an ATSSS-like solution between one 3GPP access and one WLAN. Since the first release of 5GS, untrusted/trusted WLAN (i.e., N3IWF and TNGF) have not been fully adapted that also prevents adaption of 5GS capabilities like ATSSS. A ‘lightweight’ ATSSS-like capabilities between one 3GPP and one WLAN can be beneficial for the ecosystem until (un)trusted access nodes become widely available.
TNGF/N3IWF removed

## Slide 12: ATSSS-like
Implication of lack of AN node (TNGF/N3IWF)
  Violation of AN & CN decoupling requirements. See 23.501 “4.1 General concepts”
  The 5G System architecture is defined to support data connectivity and services enabling deployments to use techniques such as e.g. Network Function Virtualization and Software Defined Networking. The 5G System architecture shall leverage service-based interactions between Control Plane (CP) Network Functions where identified. Some key principles and concept are to:
  Minimize dependencies between the Access Network (AN) and the Core Network (CN). The architecture is defined with a converged core network with a common AN - CN interface which integrates different Access Types e.g. 3GPP access and non-3GPP access.
  Violation of security requirement associated to AN&CN decoupling
NO N2 therefore
  No NAS support from N3GPP and therefore no support of any feature requiring NAS. Note (solution to use the 3GPP , but if it is not present the N3GPP shall be terminated)
  NO AMF support for N3GPP leg
    impact on Slice. How slices selection are supported? What is the leg without any slice?
    Impact on mobility. How and what is mobility management without AMF on N3GPP leg.
  NO SMF support for N3GPP leg
    Impact on Session management: which is the status of session on N3GPP? How can be established a PDU session on N3GPP without SMF involvement? What are the status connect/idle ?
QoS model impact
  Lack of N2  UE does not receives QoS rules and UPF get QoS rule, how UP link enforcement is performed?
  Lack of N3, i.e. no GTP-U how the PDR/FAR and UPF behavior is changed
MA PDU session not supported since the N3GPP legs is something else. What is a PDU session on N3GPP leg ? see next slide

## Slide 13: ATSSS-like
Removing the layer related to N3IWF, shall a new layer tunneling be added in order to:
  IP address management from SMF. Otherwise the IP address is assigned by local network (i.e. Local IP address)
  Enable E2E QoS from UE to UPF
  Enabled mobility
  Which kind of tunnel?
    IPinIP
    GRE
    IPsec
    …..
MAP PDU session with Untrusted Non-3GPP access

## Slide 14: ATSSS-like conclusion
The ATSSS-like is lightweight but the solution to support would be probably NOT Lite since a lot of changes is required in the session management, connection management, QoS management, new PDU session, etc for this new scenario in respect MA PDU session and assumption on PDU session on N3GPP access
The scope of the work is not clear, since in the call has been mentioned that the problem is to have a solution without TNGF/N3IWF since not deployed for unknown reason, and an access node may be present in solution, therefore which is the problem to be solved?
The SID description needs to consider all the issues to be investigated, therefore the TU needs to be consistent