## Slide 1: Motivation on studying Analytics Framework Enhancements to Enable Policy Recommendations
Lenovo

## Slide 2: Current status on analytics usage by each NF
A Consumer requests one or more analytics from an NWDAF
NWDAF collects data to derive the requested analytics
Each Consumer performs an action taking into account the analytics provided by an NWDAF

## Slide 3: Current Analytics Framework status
The analytics consumer NF currently requests exploratory, descriptive or predictive analytics
The action(s) that each Analytics consumer NF can take based on the analytics received are implementation/configuration specific.
Each NF identifies if the action improved the system by continuously monitoring analytic data from the NWDAF.
Results in additional computation load and latency for the NF to determine if the action had the required result
OBSERVATION: Computation cost of current mechanism is high

## Slide 4: Example framework for policy recommendations
Introduce a closed loop principle where data are used to determine accuracy of recommendation.
Recommendation takes into account broader view of the network (i.e. data collection from multiple NFs) and does not rely only on the analytic(s) subscribed from NWDAF.
Example Policy recommendation: Recommended QoS rule for the PCF to reach a target Service Experience.
  NWDAF or new NF collect data from 5GC NFsv(or OAM) and use a prescriptive AI/ML model to determine a recommendation
  When PCF takes an action based on recommendation NWDAF (or new NF) verifies accuracy of recommendation by collecting additional data from 5GC NF (or OAM).

## Slide 5: Proposed Objectives for Policy Recommendations
Specify enhancements in the analytics framework/architecture to enable recommendations
In this release focus on enhancing the Policy framework and enable policy recommendations leveraging the existing analytics capabilities at the NWDAF.
As part of the study the following will be defined:
  Identify how Analytic(s) provided by the NWDAF can be leveraged to enable policy recommendations
    Identify if new analytics need to be defined to assist the analytics framework in determining policy recommendations
  Identify what policy recommendations can be provided by the analytics framework (e.g. QoS recommendation, RFSP recommendation etc).
  How the policy framework (i.e PCF) request policy recommendations? What parameters are included in the request to the analytics framework?
  Identify which function can provide policy recommendations (NWDAF, new NF, PCF?)
  Identify procedure for verifying accuracy of a policy recommendation.