## Slide 1
Discussion for TSC enhancement in Release 19
Ling Zhang
Siemens AG

## Slide 2: Enhancements for TSN configuration
Time-sensitive communication requirements in TS 22.104 cl. 5.6A:
    The 5G system shall support the fully distributed model for configuration of time-sensitive networking.
    The 5G system shall support the fully distributed model for configuration of time-sensitive networking that is aligned with Multiple Stream Registration Protocol (MSRP, IEEE 802.1Q [19] clause 35.1), IEEE P802.1CS Link-local Registration Protocol (LRP) [24], and IEEE P802.1Qdd Resource Allocation Protocol (RAP) [25].
    The 5G system shall support the user-network / network-network interface for the dynamic configuration of the fully distributed model for time-sensitive networking.
Enhancements on 5GS Bridge to support:
  Fully distributed TSN configuration model and protocols including LRP/RAP (defined by IEEE).
  Distributed TSN streams establishment and dynamic configuration for the TSN streams.
  TSN management using NETCONF with YANG model, and the 5GS Bridge’s translation of the NETCONF/YANG configurations into corresponding configurations of the 5GS.

## Slide 3: Enhancements of TSC for Industrial IOT
Improved time synchronization with smaller 5G time sync budget (stable time synchronization accuracy of the 5G system of 700-800 ns with two wireless links on the path of the time synchronization messages).
Enhanced 5G-VN capabilities supporting:
  Dynamic addition of new VN members
  Large numbers of VLANs/UEs
  Multiple VLANS/TSN streams per UE
  Multiple non-3GPP devices behind UE
In current release it does not guarantee that the Ethernet network remains loop-free. Further study is needed to support loop prevention with spanning tree for TSC traffic.

## Slide 4: Work tasks
It is proposed to include the following work tasks in the Rel-19 study corresponding to the TSC/URLLC/TRS enhancement topic.
WT-1: Enhancements supporting improved time synchronization with smaller 5G time sync budget
WT-2: Enhancements supporting 5G-VN capabilities for Industrial IOT requirements on:
  Dynamic addition of new VN members
  Large numbers of VLANs/UEs
  Multiple VLANS/TSN streams per UE
  Multiple non-3GPP devices behind UE
WT-3: Enhancements supporting TSN configuration for:
  Fully distributed TSN configuration model and protocols including LRP/RAP (defined by IEEE)
  Distributed TSN streams establishment and dynamic configuration for the TSN streams
  TSN management using NETCONF with YANG model, and the 5GS Bridge’s translation of the NETCONF/YANG configurations into corresponding configurations of the 5GS
WT-4: Enhancements supporting loop prevention with spanning tree for TSC traffic