## Slide 1: Modification on WT#2 for UPEAS_Ph2
Samsung

## Slide 2: Introduction
The purpose of the discussion paper is to address the SBI interface between UPF and AF over N6 in WT#2 of UPEAS_Ph2
WT#2 of UPEAS_Ph2 (SID of UPEAS_Ph2)
  WT#2: Study whether there are any potential enhancements on the UPF event exposure service that would optimize the procedures related to UPF data collection, e.g. direct/indirect subscription of the UPF via control plane from application.
  NOTE 2: Solutions need to analyse benefits compared to existing mechanisms.

## Slide 3: Service subscription to UPF by AF in Rel-18
Subscription to UPF Event Exposure service via NEF (over Control Plane) based on Rel-18
  AF subscribes the UPF Event Exposure service to measure E2E latency of its service (IP Flow)
  It needs to find the serving UPF which handles specific IP Flow, but there are two UPFs for the UE
    In order to identify the serving UPF, only with GPSI, it is not possible
  AF sends the request with it IP address and UE’s IP address
    Both IP addresses are public IP address which can not be used in operator’s network
  When receiving the request from the AF, it needs to translate UE’s IP address into private IP address
  NEF requests the UDM to ask the serving SMF
  NEF forwards the request the serving SMF
  Finally, serving SMF sends the request to the serving UPF
RAN
UE
AF
NEF
IP Flow
IP(QoS) Flow
Serving UPF
UDM
SMF
DN
CN
UPF

## Slide 4: What is the benefit using SBI over N6
Basically, the serving UPF is Home Router of the UE, so AF simply sends the request (contained in user data packet) to the UE
  No need to translate UE’s IP address into private IP address
  No need to request to NEF, UDM and SMF in order to find the serving UPF
  No need to maintain of subscription configuration in SMF
AF
NEF
UDM
SMF
UPF
Nnef_EventExposure_Subscribe
Request
2. Nudm_EventExposure_Subscribe
Request
3. Nsmf_EventExposure_Subscribe
Request
4. Nupf_EventExposure_Subscribe
Request
Event Subscription Data
Event Subscription Data
Event Subscription Data
Event Subscription Data
AF
NEF
UDM
SMF
UPF
Nupf_UPFDiscovery_Request
Request
2. Nudm_EventExposure_Subscribe
Request
3. Nsmf_EventExposure_Subscribe
Request
4. Nupf_EventExposure_Subscribe
Request
Event Subscription Data
Event Subscription Data
Event Subscription Data
Event Subscription Data
Subscription to UPF based on Rel-18(CP)
Subscription to UPF based on N6(UP)

## Slide 5: Proposal
Observation
  Subscription to UPF from application via control plan is complicated and burdens to other NFs (e.g. NEF, SMF, UDM)
  Problem with public UE IP address and private UE IP address
Proposal
  Remove restriction regarding subscription to UPF via user plane